## Slide 1: Lecture 2: Representing Integers
CS 105 Fall 2026

## Slide 2: Review: Bits Require Interpretation
10001100 00001100 10101100 00000000
might be interpreted as
  The integer 3,485,745
  A floating point number close to 4.884569 x 10-39
  The string “105”
  A portion of an image or video
  An address in memory

## Slide 3: Representing Integers
Arabic Numerals: 47
Roman Numerals: XLVII
Brahmi Numerals:
Tally Marks: IIII IIII IIII IIII IIII IIII IIII IIII IIII II

## Slide 4: Base-10 Integers
1000 (103) | 100 (102) | 10 (101) | 1 (100)
0 | 0 | 0 | 5
0 | 0 | 4 | 7
1 | 8 | 8 | 7

## Slide 5: Base-2 Integers (aka Binary Numbers)
128 (27) | 64 (26) | 32 (25) | 16 (24) | 8 (23) | 4 (22) | 2 (21) | 1 (20)
0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 6: Binary Numbers
Decimal (Base-10):
Binary (Base-2):
1011
1011

## Slide 7: Exercise 1: Binary Numbers
Consider the following four-bit binary values. What is the (base-10) integer interpretation of these values?
  0001
  1010
  0111
  1111
1
10
7
15

## Slide 8: Hexidecimal Numbers
00101100 00110101 00110000 11100001
Dec | Hex
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
8 | 
9 | 
10 | 
11 | 
12 | 
13 | 
14 | 
15 | 
0
1
2
3
4
5
6
7
8
9
a
b
c
d
e
f
2
c
3
5
3
0
e
1
0x2c3530e1

## Slide 9: Exercise 2: Hexidecimal Numbers
Consider the following hexidecimal values. What is the representation of each value in binary?
  0x0a
  0x11
  0x2f
00001010 (10)
00010001 (17)
00101111 (47)

## Slide 10: Addition Example
Compute 5 + 6 assuming all ints are stored as eight-bit (1 byte) unsigned values
Like you learned in grade school, only binary!
0 0 0 0 0 1 0 1
+ 0 0 0 0 0 1 1 0
1
1
0
1
1
… and with a finite number of digits
0
0
0
0
= 11 (Base-10)

## Slide 11: Addition Example with Overflow
Compute 200 + 100 assuming all ints are stored as eight-bit (1 byte) unsigned values
Like you learned in grade school, only binary!
1 1 0 0 1 0 0 0
+ 0 1 1 0 0 1 0 0
0
0
1
1
… and with a finite number of digits
0
1
0
0
1
1
= 44 (Base-10)

## Slide 12: Error Cases (Unsigned Ints)
Assume -bit unsigned values
overflow has occurred iff
[ ]
representable values
[ ]
Possible values of
modular addition

## Slide 13: Exercise 3: Binary Addition
Given the following 5-bit unsigned values, compute their sum and indicate whether or not an overflow occurred
x | y | x+y | overflow?
00010 | 00101 |  | 
01100 | 00100 |  | 
10100 | 10001 |  | 
00111
10000
00101
no
no
yes
x+y | overflow?

## Slide 14: Multiplication Example
Compute 5 x 6 assuming all ints are stored as eight-bit (1 byte) unsigned values
Like you learned in grade school, only binary!
0 0 0 0 0 1 0 1
x 0 0 0 0 0 1 1 0
… and with a finite number of digits
= 30 (Base-10)
0 0 0 0 0 0 0 0
0 0 0 0 0 1 0 1 0
+ _
0 0 0 0 0 1 0 1 0 0
0 0 0 1 1 1 1 0

## Slide 15: Multiplication Example
Compute 200 x 3 assuming all ints are stored as eight-bit (1 byte) unsigned values
Like you learned in grade school, only binary!
1 1 0 0 1 0 0 0
x 0 0 0 0 0 0 1 1
… and with a finite number of digits
= 88 (Base-10)
1 1 0 0 1 0 0 0
+ _
1 1 0 0 1 0 0 0 0
0 1 0 1 1 0 0 0
1 0

## Slide 16: Exercise (4): Binary Multiplication
Given the following 3-bit unsigned values, compute their product and indicate whether or not an overflow occurred
x | y | x*y | overflow?
100 | 101 |  | 
010 | 011 |  | 
111 | 010 |  | 
100
110
110
yes
no
yes
x*y | overflow?

## Slide 17
What about positive/negative integers?

## Slide 18: Representing Signed Integers
Option 1: sign-magnitude
  One bit for sign; interpret rest as magnitude
+/- | 64 (26) | 32 (25) | 16 (24) | 8 (23) | 4 (22) | 2 (21) | 1 (20)
0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0 | 1 | 0 | 1
-
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Notes: Issues: two zeros, arithmetic is different for pos vs neg (and weird around zero), e.g, try 5+1 vs -5+1 vs. -5 + 6

## Slide 19: Representing Signed Integers
Option 2: excess-K
  Choose a positive K in the middle of the unsigned range
128 (27) | 64 (26) | 32 (25) | 16 (24) | 8 (23) | 4 (22) | 2 (21) | 1 (20) | -128
0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Notes: issue: zero no longer zero -> multiplication is weird

## Slide 20: Representing Signed Integers
Option 3: two’s complement
  Like unsigned, except the high-order contribution is negative
-128 (-27) | 64 (26) | 32 (25) | 16 (24) | 8 (23) | 4 (22) | 2 (21) | 1 (20)
0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 21: Important Signed Integers
 | 8 | 16 | 32 | 64
TMax | 0x7F | 0x7FFF | 0x7FFFFFFF | 0x7FFFFFFFFFFFFFFF
TMin | 0x80 | 0x8000 | 0x80000000 | 0x8000000000000000
0 | 0x00 | 0x0000 | 0x00000000 | 0x0000000000000000
-1 | 0xFF | 0xFFFF | 0xFFFFFFFF | 0xFFFFFFFFFFFFFFFF

## Slide 22: Exercise 4: (Signed) Binary Numbers
Consider the following one-byte binary values. What is the (signed) integer interpretation of these values?
  01101001
  10010111
  01000010
  10111110
What is the one-byte binary representation of the following integers?
  47
  -47
105
-105
66
-66
-x == -x+1-1 == -1-x+1 == 111…1-x+1 = ~x+1
00101111
11010001

## Slide 23: Integers in C
C Data Type | Size (bytes)
unsigned char | 1
unsigned short | 2
unsigned int | 4
unsigned long | 8
C Data Type | Size (bytes)
char | 1
short | 2
int | 4
long | 8
Notes: Note: unsigned demo

## Slide 24: Addition Example
Compute 5 + -3 assuming all ints are stored as four-bit signed values
Exactly the same as unsigned numbers!
0 1 0 1
+ 1 1 0 1
0
1
0
0
1
… but with different error cases
= 2 (Base-10)
1

## Slide 25: Addition/Subtraction with Overflow
Compute 5 + 6 assuming all ints are stored as four-bit signed values
0 1 0 1
+ 0 1 1 0
1
1
0
1
1
= -5 (Base-10)

## Slide 26: Exercise (5): (Signed) Binary Addition
Given the following 5-bit signed values, compute their sum and indicate whether or not an overflow occurred
x | y | x+y | overflow?
00010 | 00101 |  | 
01100 | 00100 |  | 
10100 | 10001 |  | 
00101
10000
00101
no
yes
yes
x+y | overflow?

## Slide 27: Multiplication Example
+ _
Compute 3 x 2 assuming all ints are stored as four-bit signed values
Exactly like unsigned multiplication!
0 0 1 1
x 0 0 1 0
… except with different error cases
= 6 (Base-10)
0 0 0 0
0 0 1 1 0
0 1 1 0

## Slide 28: Multiplication Example
Compute 5 x 2 assuming all ints are stored as four-bit signed values
0 1 0 1
x 0 0 1 0
= -6 (Base-10)
0 0 0 0
0 1 0 1 0
+ _
1 0 1 0

## Slide 29: Exercise 5: (Signed) Binary Multiplication
Given the following 3-bit signed values, compute their product and indicate whether or not an overflow occurred
x | y | x*y | overflow?
100 | 101 |  | 
010 | 011 |  | 
111 | 010 |  | 
100
110
110
yes
yes
no
x*y | overflow?

## Slide 30: Casting between Numeric Types
Casting from shorter to longer types preserves the value
Casting from longer to shorter types drops the high-order bits
Casting between signed/unsigned types preserves the bits (it just changes the interpretation)
Implicit casting occurs in assignments and parameter lists. In mixed expressions, signed values are implicitly cast to unsigned
    Source of many errors!
Notes: Note: casting part of signed demo

## Slide 31: Arithmetic Logic Unit (ALU)
circuit that performs bitwise operations and arithmetic on integer binary types

## Slide 32: Review: Bitwise vs Logical Operations
Bitwise Operators &, |, ~, ^
  View arguments as bit vectors
  operations applied bit-wise in parallel
Logical Operators &&, ||, !
  View 0 as “False”
  View anything nonzero as “True”
  Always return 0 or 1
  Early termination
Shift operators <<, >>
  Left shift fills with zeros
  For unsigned integers, right shift is logical (fills with zeros)

## Slide 33: Exercise 6: Bitwise vs Logical Operations
What is the binary representation of each of the following expressions? Assume signed char data type (one byte).
  ~(-30)
  -30 & 22
  -30 && 22
  22 << 1
  22 >> 1
  -30 >> 1
= ~(11100010) = 00011101 = 29
= 11100010 && 00010110 = 00000001 = 1
= 00010110 << 1 = 00101100 = 44
= 11100010 >> 1 = 11110001 = -15
= 11100010 & 00010110 = 00000010 = 2
= 00010110 >> 1 = 00001011 = 11

## Slide 34: Multiplying with Shifts
Multiplication is slow
Bit shifting is kind of like multiplication, and is often faster
  x * 8 = x << 3
  x * 10 = x << 3 + x << 1
Most compilers will automatically replace multiplications with shifts where possible

## Slide 35: Endianness
47 vs 74

## Slide 36: Endianness
Big Endian: low-order bits go on the right (47)
  I tend to think in big endian numbers, so examples in class will generally use this representation
  Networks generally use big endian (aka network byte order)
Little Endian: low-order bits go on the left (74)
  Most modern machines use this representation
I will try to always be clear about whether I'm using a big endian or little endian representation
When in doubt, ask!