## Slide 1: Lecture 26: TCP
CS 105 Spring 2026

## Slide 2: OSI Network Model
Notes: http://www.cs.cornell.edu/courses/cs4410/2018sp/schedule/slides/09-networking.pdf

## Slide 3: Transport Layer Protocols
User Datagram Protocol (UDP)
unreliable, unordered delivery
connectionless
best-effort, segments might be lost, delivered out-of-order, duplicated
reliability (if required) is the responsibility of the app
Transmission Control Protocol (TCP)
reliable, in-order delivery
connection setup
flow control
congestion control
Notes: flow control = don't overwhelm the receiver
congestion control = don't swamp the network
Note: neither guarantees latency or bandwidth

## Slide 4: Sockets Interface
1. Start server
Client / Server
Session
socket
socket
bind
listen
read
write
read
write
Connection
request
read
close
close
EOF
Await connection
request from
next client
accept
connect

## Slide 5: Sockets Interface
2. Start client
1. Start server
Client / Server
Session
socket
socket
bind
listen
read
write
read
write
Connection
request
read
close
close
EOF
Await connection
request from
next client
accept
connect

## Slide 6: accept Illustrated
listenfd(3)
Client
1. Server blocks in accept, waiting for connection request on listening descriptor listenfd
clientfd
Server
listenfd(3)
Client
clientfd
Server
2. Client makes connection request by calling and blocking in connect
Connection
request
listenfd(3)
Client
clientfd
Server
3. Server returns connfd from accept. Client returns from connect. Connection is now established between clientfd and connfd
connfd(4)

## Slide 7: TCP Connections
TCP is connection-oriented
A connection is initiated with a three-way handshake
Recall: server will typically create a new socket to handle the new connection
SYN
SYN, ACK
ACK
…
Notes: demo handshake in wireshark with loopback

## Slide 8: Exercise: Connection Setup
Consider the network operations we've discussed thus far: socket, bind, listen, accept, connect. What sequence are these operations called in if a client wants to send one message to the server?
  socket
  connect
  socket
  bind
  listen
  accept
client
server

## Slide 9: Sockets Interface
3. Exchange
data
2. Start client
1. Start server
Client / Server
Session
socket
socket
bind
listen
read
write
read
write
Connection
request
read
close
close
EOF
Await connection
request from
next client
accept
connect

## Slide 10: Communicating over a channel
Consider the network operations we've discussed thus far: socket, bind, listen, accept, connect. What sequence are these operations called in if a client wants to send one message to the server?
  socket
  connect
  write
  socket
  bind
  listen
  accept
  read
client
server

## Slide 11: Reliable Transport
Each SYN segment will include a randomly chosen sequence number
Sequence number of each segment is incremented by data length
Receiver sends ACK segments acknowledging latest sequence number received
Sender maintains copy of all sent but unacknowledged segments; resends if ACK does not arrive within timeout
Timeout is dynamically adjusted to account for round-trip delay
SYN
SYN, ACK
ACK
data (Seq = 47)
ACK 47
data (Seq = 48)
ACK 48
data (Seq = 49)
ACK 49
data (Seq = 49)
Send Timeout
Notes: demo sequence numbers in wireshark

## Slide 12: Transport-Layer Segment Formats
UDP
TCP
application message (payload)
Source Port #
Dest. Port #
sequence number
acknowledgement number
receive window
HL
F
S
R
P
A
U
checksum
U data pointer
options
application message (payload)
Source Port #
Dest. Port #
Notes: S,A,F flags used to manage connection
sequence number and acknowledgement number (+ A flag) are used to implement reliable transport

## Slide 13: Pipelined Protocols
Pipelining allows sender to send multiple "in-flight", yet-to-be-acknowledged packets
  increases throughput
  needs buffering at sender and receiver

## Slide 14: Example: Window Size = 4
sender can have up to 4 unacknowledged messages
when ACK for first message is received, it can send another message
ACK 47
data (Seq = 47)
data (Seq = 48)
data (Seq = 49)
data (Seq = 50)
ACK 48
ACK 49
ACK 50
data (Seq = 51)
data (Seq = 52)
data (Seq = 53)
data (Seq = 54)

## Slide 15: Pipelined Protocols
Pipelining allows sender to send multiple "in-flight", yet-to-be-acknowledged packets
  increases throughput
  needs buffering at sender and receiver
what should we do if a packet goes missing in the middle?

## Slide 16: TCP Fast Retransmit
Receiver always acks the last id it successfully received
Sender detects loss without waiting for timeout, resends missing packet
ACK 47
data (Seq = 47)
data (Seq = 48)
data (Seq = 49)
data (Seq = 50)
ACK 47
ACK 47
data (Seq = 51)
data (Seq = 48)
data (Seq = 49)
ACK 47
ACK 51
ACK 51

## Slide 17: Exercise: TCP Sequence Numbers
Consider the sequence of transmitted messages shown on the right
What will be the next ACK number sent by the server?
What will be the next Seq number sent by the client?
ACK 13
data (Seq = 13)
data (Seq = 14)
data (Seq = 15)
data (Seq = 16)
data (Seq = 17)
ACK 13

## Slide 18: Pipelined Protocols
Pipelining allows sender to send multiple "in-flight", yet-to-be-acknowledged packets
  increases throughput
  needs buffering at sender and receiver
what should we do if a packet goes missing in the middle?
how big should the window be?

## Slide 19: TCP Congestion Control
TCP operates under a principle of additive increase-multiplicative decrease
  window size++ every RTT if no packets lost
  window size/2 if a packet is dropped

## Slide 20: TCP Fairness
Goal: if k TCP sessions share same bottleneck link of bandwidth R, each should have average rate of R/k
R
R
Connection 1 Throughput
Connection 2 Throughput
Loss: decreases throughput proportional to current bandwidth
Congestion avoidance: increases throughput linearly (evenly)

## Slide 21: TCP Slow Start
Problem: linear increase takes a long time to build up a decent window size, and most transactions are small
Solution: allow window size to increase exponentially until first loss

## Slide 22: Exercise: TCP Window Size
Assume someone changes the code of their TCP client by modifying the congestion avoidance as follows: instead of increasing the window size by 1 each time an ACK is received, they double the window size each time an ACK is received (like in the slow-start phase).
What would be the pros and cons of this modification?

## Slide 23: Sockets Interface
5. Drop client
4. Disconnect client
3. Exchange
data
2. Start client
1. Start server
Client / Server
Session
socket
socket
bind
listen
read
write
read
write
Connection
request
read
close
close
EOF
Await connection
request from
next client
accept
connect

## Slide 24: TCP Connections
TCP is connection-oriented
A connection is initiated with a three-way handshake
Recall: server will typically create a new socket to handle the new connection
FIN works (mostly) like SYN but to teardown a connection
SYN
SYN, ACK
ACK
…
FIN
ACK
Notes: demo in wireshark

## Slide 25: TCP Summary
Reliable, in-order message delivery
Connection-oriented, three-way handshake
Transmission window for better throughput
  timeouts based on link parameters (e.g., RTT, variance)
Congestion control
  Linear increase, exponential backoff
Fast adaptation
  Exponential increase in the initial phase