## Slide 1: Introduction and Design
Mobile Robotics
Anthony J. Clark

## Slide 2: Today
Administrivia
Warm-up poll questions
Defining robot requirements
Designing the course robot
Design your robot

## Slide 3: Administrivia
Mobile Robotics - Course Website
I am administering the course in a “flipped” style so that we can use class time to build and code
We’ll have
  Quizzes every class period
  Exercises every week
  You must pass all of them for an A
  See the course website for more details
Exercises will build on each other

## Slide 4: Class Workflow
 |  |  | Week A |  |  |  |  | Week B |  | 
 | Mon | Tue | Wed | Thu | Fri | Mon | Tue | Wed | Thu | Fri
Reading | Read |  | Read |  |  | Read |  | Read |  | 
Quiz A1 |  | Quiz |  |  |  | Deadline |  |  |  | 
Quiz A2 |  |  |  | Quiz |  |  |  | Deadline |  | 
Exercise A |  | Exercise |  | Continue |  | Due |  |  |  | Deadline
Quiz B1 |  |  |  |  |  |  | Quiz |  |  | …
Quiz B2 |  |  |  |  |  |  |  |  | Quiz | …
Exercise B |  |  |  |  |  |  | Exercise |  | Continue | …

## Slide 5: Robotics Stack
We’ll cover most of the robotics stack
  Low level: motor control, sensor interfacing
  Mid level: motion profile, coordination
  High level: AI, navigation, mapping

## Slide 6: Communications Channel?
Email
Slack
Discord
Canvas
Other?

## Slide 7: Polling (Sheet)
What robotics experience do you have (e.g., Vex, FIRST, etc.)?
Have you taken CS 105 (or similar “low-level” course)?
What is a robot?
What role does artificial intelligence play in robotics?
Notes: A collection of subsystems.

## Slide 8: Rule-Compliance Path Planner
Pengfei Lin, 2024

## Slide 9: Our Final Task

## Slide 10: Requirements
What would you do if I asked you to design a robot?
What questions should we ask (and answer) to design a robot?

## Slide 11: Requirements Engineering
Requirements elicitation
Requirements specification
Verification and validation
Requirements management

## Slide 12: Our Requirements
Our robot should:
  Automatically halt when no longer connected via wireless communication
  Autonomously navigate around a course,
  Avoid obstacles (static and dynamic),
  Recognize and react to signs,

## Slide 13: Requirements Engineering
Functional requirements and constraints
  How fast does the robot need to move?
  How maneuverable does the robot need to be?
  How small or large (footprint and mass) can the robot be?
  Will the robot interact closely with people?
  How costly is the robot to manufacture?
  What is the robot’s environment?
Nonfunctional requirements
  How easy is it to build the robot?
  How easy is it to fix the robot?
  Can the robot be reused in future semesters?
Notes: robot characteristics
  mechanisms
  electronics
  programming
  fabrication
design considerations
  power
  materials
  senses
  strength
  agility
  stability
  style

## Slide 14: Refining the Requirements
What kind of processing speed is needed (MCU or SBC or …)?
How much memory and storage are needed?
What is the appropriate transmission (motors, drive system, etc.)?
What form of internal communication is needed (I2C, SPI, UART, etc.)?
What power and logic levels are needed?
What battery systems (type, capacity, C-rating, voltage)?
What form of external communication is useful (wired, BLE, Wi-Fi)?
How much redundancy is needed?
What are your priorities?
Notes: motors (DC)
  power
  voltage
  current
wheel encoders sensors
  logic level
  communication
motor control
  peak and steady current
  voltage input
  voltage output
  logic level
power management
  power levels
  charging
microcontroller
  processor speed
  processor word size
  voltage
  memory
  power consumption
  communication with peripherals (I2C, DIO, A2D etc.)
  communication with host (USB, WiFi, etc.)
battery
  capacity
  voltage
  current
sensors
  communication
  logic level
  power level
  current
  accuracy
  speed
  resolution
miscellaneous
  switch
  fuse
  LEDs
  buttons
  screen
  breadboard/protoboard

## Slide 15: My Process for This Course
Decide on a drive system (direct drive).
Decide roughly on a linear robot velocity (about 50 cm/s).
Roughly pick a wheel diameter (about 7 cm).
Compute the needed motor RPMs (about 140 rpm).
Find motors (select 310 rpm @ 6 V, 170 mA; including encoders).
Notes: A bit of chicken and egg problem between power systems and drive/compute.

## Slide 16: Motor Search
Motor | Manufacturer | Cost | No Load RPM | Ratio | Voltage | No-Load Current | Stall Current | Torque oz-in | Logic | Notes
ROB-16413 | Sparkfun | $ 6.88 | 90 @ 4.5V | 48:1 | 3-9V | ? | ? | ? | 3.3-5V | 
FIT0458 | DFRobot | $ 7.40 | 160 @ 6V | 120:1 | 3-7.5V | 170mA | 2.8A | 2.78 | 4.5-7.5V | L-Shape
FIT0450 | DFRobot | $ 7.40 | 160 @ 6V | 120:1 | 3-7.5V | 170mA | 2.8A | 2.78 | 4.5-7.5V | Same as above, but flat
FIT0482 | DFRobot | $ 11.90 | 310 @ 6V | 50:1 | 3-12v | 60mA |  | 4.8 | 3.3-5V | 
4638 | Adafruit | $ 12.50 | 200 @ 6V | 50:1 |  | 100mA | 200mA | 2.78 |  | 120 RPM rated speed
DC 6V 300RPM | ASLONG | $ 8.85 | 300 @ 6V | 30:1 | 3-12V |  |  |  | 3.3-5V | SHIPPING!!!
MiniQ | DFRobot | $ 33.00 | 260 @ 6v | 50:1 |  |  | 360mA | 10 | 3.3-5V | Includes 2 motors (5.90), encoders (4.50) wheels (2.90), and mounts (3.50)
Walking speed | 1.34 m/s (3 mph)
Wheel radius | 5 cm
RPM | 100 rpm
Angular velocity | 10.47 rad/s
Linear velocity | 0.52 m/s

## Slide 17: My Process for This Course
Decide on a drive system (direct drive).
Decide roughly on a linear robot velocity (about 50 cm/s).
Roughly pick a wheel diameter (about 7 cm).
Compute the needed motor RPMs (about 140 rpm).
Find motors (select 310 rpm @ 6 V, 170 mA; including encoders).
Select motor driver (select 0-11 V, 1.2 A per channel).
Decide on sensor modalities (inertial, distance, compass, camera).
Decide on communication needs (BLE and Wi-Fi).
Find compute devices (select ESP32-S3).
Design power system (1S 3.7 V battery; estimate 190 rpm).
Notes: A bit of chicken and egg problem between power systems and drive/compute.

## Slide 18: Parts Search
Part | Source | Cost | # | Total | Note | Options | B | C | D | E | F
Chassis | Cardboard | $ - | 1 | $ - | Makerspace |  |  |  |  |  | 
Caster Wheel | RobotsShop/Pololu | $ 2.29 | 1 | $ 2.29 | Could go without, but cheap | Pololu Ball Caster with 1/2″ Plastic Ball |  |  |  |  | 
Wheels (x2) | Cardboard | $ - | 2 | $ - | Makerspace |  |  |  |  |  | 
Motor w/ Encoder (x2) | DigiKey/SparkFun | $ 6.88 | 2 | $ 13.76 | Probably want faster than 1st option | ROB-16413 | FIT0458 | FIT0450 | 4638 | RM-ASMO-01B | MiniQ Motor Wheel Set with Encoder
Motor Mount (x2) | 3D Print | $ - | 2 | $ - | Makerspace |  |  |  |  |  | 
Motor Driver |  | $ 15.00 | 1 | $ 15.00 | Dual H-bridge matching motors; provide power for MCU? |  |  |  |  |  | 
Microcontroller | Seeed Studio | $ 30.88 | 1 | $ 30.88 | Maybe the Seeed Xiao ESP32S3 Sense | Grove - Vision AI Module V2 | Grove - Vision AI Module with Himax | Grove module + camera + esp32 ? Includes imu, cam, mic |  |  | 
IMU | Inc |  | 1 | $ - |  |  |  |  |  |  | 
Camera | Inc |  | 1 | $ - |  | Gravity: Huskylens |  |  |  |  | 
Microphone | Inc |  | 1 | $ - |  |  |  |  |  |  | 
Distance Sensor |  | $ 10.00 | 1 | $ 10.00 | ToF | VL53L0X Time-of-Flight Distance Sensor | Skip to the beginning of the images gallery Grove - IR Distance Interrupter v1.2 |  |  |  | 
Power Switch |  | $ 3.00 | 1 | $ 3.00 | Rated for all parts |  |  |  |  |  | 
Power Fuse |  | $ 2.00 | 1 | $ 2.00 | Rated for all parts |  |  |  |  |  | 
Voltage Regulator |  |  |  | $ - | Maybe use motor driver? |  |  |  |  |  | 
Battery |  | $ 5.00 | 1 | $ 5.00 |  |  |  |  |  |  | 
Battery Monitor |  |  | 1 | $ - | Similar to Duckiebot |  |  |  |  |  | 
SD Card |  |  | 1 | $ - |  |  |  |  |  |  | 
MoCap Marker |  |  | 1 | $ - |  |  |  |  |  |  | 
USB Cable |  | $ 2.00 | 1 | $ 2.00 | USB-C for programming and charging? |  |  |  |  |  | 
Charger |  |  | 1 | $ - | Built-in? |  |  |  |  |  | 
OLED Display |  | $ 7.00 |  | $ - |  |  |  |  |  |  | 
 |  |  |  | $ 83.93 |  |  |  |  |  |  | 

## Slide 19: Finalized List
Category | Per Unit | Note | Status | Source
Robot Kit | $ 16.40 | Expansion Board Base for XIAO | Delivered | Seeed Studio
Robot Kit | $ 31.38 | Grove Vision AI v2 Kit (AI Module + Camera + Micro) | Delivered | Seeed Studio
Robot Kit | $ 18.62 | SATEL-VL53L7CX | Delivered | Digikey
Robot Kit | $ 2.00 | QMC5883L Triple Axis Compass (x10) | Delivered | Amazon
Robot Kit | $ 3.00 | MPU6050 6DOF IMU (x5) | Delivered | Amazon
Robot Kit | $ 4.95 | BALL CASTER WITH 3/4" PLASTIC | Delivered | Pololu
Robot Kit | $ 23.80 | Gearmotor with Encoder Pair | Delivered | Digikey
Robot Kit | $ 4.95 | DRV8835 DUAL MTR DRIVER CARRIER | Delivered | Pololu
Robot Kit | $ 4.80 | 32GB Class 10 MicroSDHC Flash Memory Card | Delivered | Amazon
Robot Kit | $ 2.25 | BREADBRD DBL STRIP 70TIE-PTS | Delivered | Digikey
Robot Kit | $ 3.69 | Protected 2600mAh 10A 18650 Button Top Battery | Delivered | Liion Wholesale
Robot Kit | $ 1.12 | BATT CONTACT CLIP 18650 1CEL SMD | Delivered | Digikey
Robot Kit | $ 2.00 | Voltage Tester | Delivered | Amazon
Robot Kit | $ 1.10 | Extra-Long Break-Away 0.1" 16-pin Strip Male Header | Delivered | Amazon
Robot Kit | $ 0.82 | N20 Micro Motor Mount Set | Delivered | Amazon
Robot Kit | $ 20.00 | Cables, straps, brackets, connectors, fasteners, etc. | N/A | N/A
Robot Kit Total | $ 140.88 |  |  | 
Course Parts | $ 114.95 | XRP ROBOTICS PLATFORM KIT | Delivered | Digikey
Course Parts | $ 100.00 | Adeept |  | 
Course Parts | $ 100.00 | Adeept |  | 
Course Parts | $ 515.00 | Crazyflie 2.1 |  | Crazyflie?
Course Parts | $ 34.75 | XTAR VC8S Battery Charger | Delivered | Liion Wholesale
Course Parts | $ 9.99 | Anker USB C to USB C Cable | Delivered | Amazon
Course Parts | $ 32.99 | Anker USB C 715 (Nano 65W) | Delivered | Amazon
Course Parts | $ 8.99 | M3 Black Nylon Standoff Spacer With Screws Hex Nuts | Delivered | Amazon
Course Parts | $ 9.99 | M2 Black Nylon Standoff Spacer With Screws Hex Nuts | Delivered | Amazon
Course Parts | $ 7.99 | Reusable Multi-Purpose Wrap Fasteners | Delivered | Amazon
Course Parts | $ 3.78 | Rubber Bands Size #30 | Delivered | Amazon
Course Parts | $ 6.99 | Double Sided Sticky Dot | Delivered | Amazon
Course Parts | $ 28.99 | 6 Qt Clear Storage Box | Delivered | Amazon
Course Parts | $ 12.20 | JUMPER KIT VARIOUS 26AWG 65PCS | Delivered | Digikey
Course Parts | $ 3.50 | Grove - 4 pin Female Jumper to Grove | Delivered | Seeed Studio
Course Parts | $ 4.50 | GROVE2DUPONT CONVERSION CABLE 20 | Delivered | Digikey
Course Parts | $ 8.60 | GROVE 4PIN FEMALE JUMPERS 5PACK | Delivered | Digikey
Course Parts Total | $ 1,003.21 |  |  | 
Other | $ 111.17 | Estimated | N/A | N/A
Other | $ 200.00 | Estimated | N/A | N/A
Other Total | $ 311.17 |  |  | 
*Missing a few late additions

## Slide 20: Things to Check
Power levels: voltage in Volts (V) and current in amps (A)
Logic levels: chips need to agree on what a logic “1” is in terms of voltage
Power reset: actuators should typically be powered after compute
Power monitor: don’t over discharge your batteries

## Slide 21: Prototyping
Define goals
Brainstorm designs
Sketch your layout (I’ve given you all “component templates”)
Prototype with simple materials (cardboard, sticky dots, etc.)
Model with CAD and fabricate
Make notes on what works and what doesn’t
Refine (back to step 5)

## Slide 22: First Quiz
Complete the first quiz on gradescope.

## Slide 23: Exercise 1
Arts and crafts day at the Hive
Pair-up
Multiple pairs can work together (no more than 6)
“Design” your robot
You’ll start with electronics on Thursday

## Slide 24
Wheel
Parts (These Won’t Print Correctly)

## Slide 25
Strap
Strap
Full Layout
Wheel
Wheel
Wires

## Slide 26
Top
Wheel
Wheel
Wires

## Slide 27
Cross Bar

## Slide 28
Strap
Strap
Bottom
Wires