## Slide 1: Embedded Systems
Mobile Robotics
Anthony J. Clark

## Slide 2: Today
Our robot’s task
Project workflow
Hardware Systems
Software Systems
Arduino Ecosystem

## Slide 3: Our Robot’s Task

## Slide 4: Project Workflow
Specify the requirements
Design your software
Program your software
Upload your program
  Connected using a “programmer”
  Connected with USB using a bootloader
  Connected over Wi-Fi using OTA
Monitor and direct your robot using WebSockets

## Slide 5: Embedded Systems

## Slide 6: Hardware System
CPU: Xtensa® dual-core 32-bit LX7 microprocessor (240 MHz)
Cache: 16 KB instruction and 32 KB data
  four-way set associative
  16 bytes block size
Internal memory: 384 KB ROM and 512 KB SRAM
External memory: 8 MB PSRAM and 8 MB Flash

## Slide 8: Motor Driver Interface

## Slide 9: Other Peripherals Using I2C

## Slide 10: Wi-Fi Communication

## Slide 11: Hardware/Software Interface
Heap
Uninitialized Static (bss segment)
Initialized Static (data segment)
Code (text segment)
Stack
High Memory Address
Low Memory Address
Flash
SPI RAM
Cache
dRAM
iRAM
ROM
External Memory
Internal Memory

## Slide 12: On Reset (Jumps to Bootloader)

## Slide 13: Toit (and Jaguar) vs. Bare Metal (ESP-IDF)

## Slide 14: Blinking With Toit
import gpio
main:
pin := gpio.Pin 32 --output
while true:
pin.set 0
sleep --ms=500
pin.set 1
sleep --ms=500

## Slide 15: Fibers: Independent Control Flow
import gpio
LED1 ::= gpio.Pin.out 17
LED2 ::= gpio.Pin.out 18
main:
task:: my-task-1
task:: my-task-2
my-task-1:
while true:
sleep --ms=500
LED1.set 1
sleep --ms=500
LED1.set 0
my-task-2:
while true:
sleep --ms=123
LED2.set 1
sleep --ms=123
LED2.set 0

## Slide 16: Why Leave Toit?
[jaguar] INFO: program 8358aee2-45c6-0193-6318-b75de00f59f3 stopped
[jaguar] INFO: program c6925192-2d45-548f-7f78-726e3c457cad started
Heap report @ out of memory in primitive 6:2:
┌────────┬────────┬────────────────────────────────────────────────┐
│ Bytes │ Count │ Type │
├────────┼────────┼────────────────────────────────────────────────┤
│ 40960 │ 12 │ toit processes │
│ 16384 │ 4 │ system 0 0ff85ae2-63d2-e530-c9fe-c844785c0276 │
│ 20480 │ 5 │ other 1 31709de1-906c-ce7d-8698-87e163711ebb │
│ 4096 │ 1 │ current 7 c6925192-2d45-548f-7f78-726e3c457cad │
│ 667648 │ 1 │ heap metadata │
│ 4096 │ 1 │ spare new-space │
│ 16808 │ 7 │ heap overhead │
│ 192 │ 4 │ thread/other │
└────────┴────────┴────────────────────────────────────────────────┘
Total: 729704 bytes in 16 allocations (8%), largest free 7452k, total free 7471k
******************************************************************************
Decoding by `jag`, device has version <2.0.0-alpha.159>
******************************************************************************
MALLOC_FAILED error.
0: Bus.test <sdk>/i2c.toit:65:5
1: Bus.scan <sdk>/i2c.toit:60:10
2: main display.toit:23:18
******************************************************************************
[jaguar] ERROR: program c6925192-2d45-548f-7f78-726e3c457cad stopped - exit code 1

## Slide 17: Blinking With ESP-IDF
#include <stdio.h>
#include "freertos/FreeRTOS.h"
#include "freertos/task.h"
#include "driver/gpio.h"
#include "esp_log.h"
#include "led_strip.h"
#include "sdkconfig.h"
#define BLINK_GPIO CONFIG_BLINK_GPIO
static uint8_t s_led_state = 0;
static void blink_led(void) {
gpio_set_level(BLINK_GPIO, s_led_state);
}
static void configure_led(void) {
gpio_reset_pin(BLINK_GPIO);
gpio_set_direction(BLINK_GPIO, GPIO_MODE_OUTPUT);
}
void app_main(void) {
configure_led();
while (1) {
blink_led();
s_led_state = !s_led_state;
vTaskDelay(CONFIG_BLINK_PERIOD / portTICK_PERIOD_MS);
}
}
https://github.com/espressif/esp-idf/blob/master/examples/get-started/blink/main/blink_example_main.c

## Slide 18: Arduino Ecosystem
Bootloader (otherwise, must use a hardware programmer)
Open-source hardware (kits, boards, and shields)
Open-source software (many Arduino libraries)
Arduino® UNO R4 Minima

## Slide 19: Blinking an LED (Light-Emitting Diode)
void setup() {
pinMode(LED_BUILTIN, OUTPUT);
}
void loop() {
digitalWrite(LED_BUILTIN, HIGH);
delay(1000)
digitalWrite(LED_BUILTIN, LOW);
delay(1000)
}

## Slide 20: Arduino Bootloader

## Slide 21
https://github.com/arduino/ArduinoCore-avr/blob/master/cores/arduino/main.cpp
#include <Arduino.h>
int atexit(void (* /*func*/ )()) { return 0; }
void initVariant() __attribute__((weak));
void initVariant() { }
void setupUSB() __attribute__((weak));
void setupUSB() { }
int main(void) {
init();
initVariant();
setup();
for (;;) {
loop();
if (serialEventRun) serialEventRun();
}
return 0;
}
https://github.com/espressif/arduino-esp32/blob/master/cores/esp32/main.cpp

## Slide 22: Embedded Software
Don’t block other tasks with delays
Deal with hardware and time constrains
Use an event-driven approach

## Slide 23: Blinking is Blocking
void setup() {
pinMode(LED_BUILTIN, OUTPUT);
}
void loop() {
digitalWrite(LED_BUILTIN, HIGH);
delay(1000)
digitalWrite(LED_BUILTIN, LOW);
delay(1000)
}
void setup() {
pinMode(LED_BUILTIN, OUTPUT);
setupMotors();
}
void loop() {
if shouldHaltMotors() haltMotors();
digitalWrite(LED_BUILTIN, HIGH);
delay(1000)
digitalWrite(LED_BUILTIN, LOW);
delay(1000)
}

## Slide 24: Blinking Without Blocking
const int blinkInterval = 1000;
int ledState = LOW;
unsigned long previousMillis = 0;
void setup() {
pinMode(LED_BUILTIN, OUTPUT);
}
void loop() {
unsigned long currentMillis = millis();
if (currentMillis - previousMillis >= blinkInterval) {
previousMillis = currentMillis;
ledState = (ledState == LOW) ? HIGH : LOW;
digitalWrite(LED_BUILTIN, ledState);
}
}
void setup() {
pinMode(LED_BUILTIN, OUTPUT);
}
void loop() {
digitalWrite(LED_BUILTIN, HIGH);
delay(1000)
digitalWrite(LED_BUILTIN, LOW);
delay(1000)
}

## Slide 25: Blinking Without Blocking
const int blinkInterval = 1000;
int ledState = LOW;
unsigned long previousMillis = 0;
void setup() {
pinMode(LED_BUILTIN, OUTPUT);
setupMotors();
}
void loop() {
if shouldHaltMotors() haltMotors();
unsigned long currentMillis = millis();
if (currentMillis - previousMillis >= blinkInterval) {
previousMillis = currentMillis;
ledState = (ledState == LOW) ? HIGH : LOW;
digitalWrite(LED_BUILTIN, ledState);
}
}

## Slide 26: Pseudocode For Software Architecture
global state for module 1
global state for module 2
…
set update period for module 1
set update period for module 2
…
setup
initialize non-trivial global states
loop
short update/poll for module 1
short update/poll for module 2
…

## Slide 27: Pseudocode For Software Architecture
global state for module 1
global state for module 2
…
set update period for module 1
set update period for module 2
…
setup
initialize non-trivial global states
loop
short update/poll for module 1
short update/poll for module 2
…
const int blinkInterval = 1000;
int ledState = LOW;
unsigned long previousMillis = 0;
void setup() {
pinMode(LED_BUILTIN, OUTPUT);
setupMotors();
}
void loop() {
if shouldHaltMotors() haltMotors();
unsigned long currentMillis = millis();
if (currentMillis - previousMillis >= blinkInterval) {
previousMillis = currentMillis;
ledState = (ledState == LOW) ? HIGH : LOW;
digitalWrite(LED_BUILTIN, ledState);
}
}