## Slide 1: Lecture 4: Floats
CS 105

## Slide 2: Representing Integers
unsigned:
signed (two's complement):
  Note: to compute –x for a signed int x, flip all the bits, then add 1
128 (27) | 64 (26) | 32 (25) | 16 (24) | 8 (23) | 4 (22) | 2 (21) | 1 (20)
-128 (27) | 64 (26) | 32 (25) | 16 (24) | 8 (23) | 4 (22) | 2 (21) | 1 (20)

## Slide 3: Fractional binary numbers
What is 1001.1012?
Notes: Grade school version

## Slide 4: Fractional Binary Numbers
2i
2i-1
4
2
1
1/2
1/4
1/8
2-j
bi | bi-1 | ••• | b2 | b1 | b0 | b-1 | b-2 | b-3 | ••• | b-j
• • •
Representation
  Bits to right of “binary point” represent fractional powers of 2
  Represents rational number:
• • •

## Slide 5: Example: Fractional Binary Numbers
What is 1001.1012?
Notes: 101.112
010.1112
001.01112

## Slide 6: Example: Fractional Binary Numbers
What is 1001.1012?
Notes: 101.112
010.1112
001.01112

## Slide 7: Example: Fractional Binary Numbers
What is 1001.1012?
What is the binary representation of 13 9/16?
1101.
1001
Notes: 101.112
010.1112
001.01112

## Slide 8: Exercise 1: Fractional Binary Numbers
Translate the following fractional numbers to their binary representation
  5 3/4
  2 7/8
  1 7/16
Translate the following fractional binary numbers to their decimal representation
  000.01100
  000.11000
  001.10000
Notes: 101.112
010.1112
001.01112

## Slide 9: Exercise 1: Fractional Binary Numbers
Translate the following fractional numbers to their binary representation
  5 3/4
  2 7/8
  1 7/16
Translate the following fractional binary numbers to their decimal representation
  000.01100
  000.11000
  001.10000
101.11000
010.11100
001.01110
What do you notice about shifting?
Notes:   Divide by 2 by shifting right (unsigned)
  Multiply by 2 by shifting left
  Numbers of form 0.111111…2 are just below 1.0
    1/2 + 1/4 + 1/8 + … + 1/2i + … ➙ 1.0

## Slide 10: Representable Numbers
Limitation #1
  Can only exactly represent numbers of the form x/2k
  Other rational numbers have repeating bit representations
  Value Representation
    1/3 0.0101010101[01]…2
    1/5 0.001100110011[0011]…2
    1/10 0.0001100110011[0011]…2
Limitation #2
  Just one setting of binary point within the w bits
  Limited range of numbers (Very small values? Imprecise values?)

## Slide 11: Floating Point Representation
Numerical Form:
  Sign bit determines whether number is negative or positive
  Significand normally a fractional value in range [1.0,2.0)
  Exponent weights value by power of two
Notes: Normalize demo: 1.0 hex->interpretation on board, then 1.25, then demo exponent changes with bigger and smaller values

## Slide 12: Exercise 2: Floating Point Numbers
For each of the following numbers, specify a binary fractional number M in [1.0,2.0) and a binary number E such that the number is equal to
  5 3/4
  2 7/8
  1 1/2
  3/4
Notes:   Divide by 2 by shifting right (unsigned)
  Multiply by 2 by shifting left
  Numbers of form 0.111111…2 are just below 1.0
    1/2 + 1/4 + 1/8 + … + 1/2i + … ➙ 1.0

## Slide 13: Exercise 2: Floating Point Numbers
For each of the following numbers, specify a binary fractional number M in [1.0,2.0) and a binary number E such that the number is equal to
  5 3/4
  2 7/8
  1 1/2
  3/4
M = 1.0111
M = 1.0111
E = 2
E = 1
M = 1.1000
M = 1.1000
E = 0
E = -1
Notes:   Divide by 2 by shifting right (unsigned)
  Multiply by 2 by shifting left
  Numbers of form 0.111111…2 are just below 1.0
    1/2 + 1/4 + 1/8 + … + 1/2i + … ➙ 1.0

## Slide 14: One Way To View Floats
Sign bit
Window into two consecutive powers of two
  [0.5, 1], [1, 2], [2, 4], …, [2127, 2128]
Offset dividing the window into 223 buckets
  Finer grained near zero
Credit to Fabien Sanglard: https://fabiensanglard.net/floating_point_visually_explained/

## Slide 15: Floating Point Representation
Numerical Form:
  Sign bit determines whether number is negative or positive
  Significand normally a fractional value in range [1.0,2.0)
  Exponent weights value by power of two
Encoding:
  s is sign bit s
  exp field encodes (but is not equal to E)
    normally
  frac field encodes M (but is not equal to M)
    normally
bias
Float (32 bits):
k = 8, n = 23
bias = 127
Double (64 bits)
k=11, n = 52
bias = 1023
Notes: Normalize demo: 1.0 hex->interpretation on board, then 1.25, then demo exponent changes with bigger and smaller values

## Slide 16: IEEE 754 single-precision binary floating-point format

## Slide 17: Exercise 3: Floating Point Representations
What are the values of s, exp, and frac that correspond to the float representation of 5 3/4, assuming 1-bit s, 3-bit exp, and 4-bit frac?
  , M = 1.0111, E = 2
  s is sign bit s
exp field encodes (but is not equal to E)
  normally
frac field encodes M (but is not equal to M)
  normally
Under those assumptions, what is the full representation of 5 3/4 as a one-byte floating point value?

## Slide 18: Exercise 3: Floating Point Representations
What are the values of s, exp, and frac that correspond to the float representation of 5 3/4, assuming 1-bit s, 3-bit exp, and 4-bit frac?
  , M = 1.0111, E = 2
  s is sign bit s
exp field encodes (but is not equal to E)
  normally
frac field encodes M (but is not equal to M)
  normally
Under those assumptions, what is the full representation of 5 3/4 as a one-byte floating point value?
s = 0
exp = 101
frac = 0111
01010111
= 0x57

## Slide 19: Example: Floats
What fractional number is represented by the bytes 0x3ec00000? Assume big-endian order.
Float (32 bits):
k = 8, n = 23
bias = 127
  s is sign bit s
  exp field encodes (but is not equal to E)
    normally
  frac field encodes M (but is not equal to M)
    normally
0011 1110 1100 0000 0000 0000 0000 0000
s=0
exp=125
frac = 100000000000000000000002
s=0
E = -2
M = 1.100000000000000000000002 = 1.510
Notes: .375

## Slide 20
C Float Demo

## Slide 21: Exercise 4: Floats
What fractional number is represented by the bytes 0x423c0000? Assume big-endian order.
Float (32 bits):
k = 8, n = 23
bias = 127
  s is sign bit s
  exp field encodes (but is not equal to E)
    normally
  frac field encodes M (but is not equal to M)
    normally
0100 0010 0011 1100 0000 0000 0000 0000
s=0
exp=132
frac = 011110000000000000000002
s=0
E = 5
M = 1.011110000000000000000002
Notes: .375

## Slide 22: Limitation so far…
What is the smallest non-negative number that can be represented?
What we like the smallest non-negative number to be?
0000 0000 0000 0000 0000 0000 0000 0000
s=0
exp=0
frac = 000000000000000000000002
s=0
E = -127
M = 1.000000000000000000000002
Notes: .375

## Slide 23: Normalized and Denormalized
Normalized Values
  exp is neither all zeros nor all ones (normal case)
  exponent is defined as , where (e.g., 127 for float or 1023 for double)
  significand is defined as
Denormalized Values
  exp is either all zeros or all ones
  if all zeros: and
  if all ones: infinity (if frac is all zeros) or NaN (if frac is non-zero)
s | exp | frac
Notes: Can represent smaller fractional values

## Slide 24: Visualization: Floating Point Encodings
+
−
0
+Denorm
+Normalized
−Denorm
−Normalized
+0
NaN
NaN

## Slide 25: Exercise 5: Limits of Floats
What is the difference between the largest (non-infinite) positive number that can be represented as a (normalized) float and the second-largest?
s | exp | frac
1 | 8-bits | 23-bits

## Slide 26: Exercise 5: Limits of Floats
What is the difference between the largest (non-infinite) positive number that can be represented as a (normalized) float and the second-largest?
Any number between these two gets rounded.
s | exp | frac
1 | 8-bits | 23-bits
0111 1111 0111 1111 1111 1111 1111 1111
s=0
E = 127
M = 1.111111111111111111111112

## Slide 27: Correctness
Example 1: Is (x + y) + z = x + (y + z)?
  Ints: Yes!
  Floats:
    (2^30 + -2^30) + 3.14 ➙ 3.14
    2^30 + (-2^30 + 3.14) ➙ 0.0
Notes: Source: xkcd.com/571

## Slide 28: Floating Point in C
C Guarantees Two Levels
  float single precision (32 bits)
  double double precision (64 bits)
Conversions/Casting
  Casting between int, float, and double changes bit representation
  double/float → int
    Truncates fractional part
    Like rounding toward zero
    Not defined when out of range or NaN: Generally sets to TMin
  int → double
    Exact conversion,
  int → float
    Will round
Notes: all ints are representable as floats as long as int has ≤ 53 bit size

## Slide 29: Exercise 6: Casting with Floats
Assume you have three variables: an int x, a float f, and a double d. Assume that all three variables store numeric values (not ,, or NaN). Which of the following expressions are guaranteed to evaluate to True?
  x == (int)(double)(x)
  x == (int)(float)(x)
  d == (double)(float) d
  f == (float)(double) f

## Slide 30: Exercise 6: Casting with Floats
Assume you have three variables: an int x, a float f, and a double d. Assume that all three variables store numeric values (not ,, or NaN). Which of the following expressions are guaranteed to evaluate to True?
  x == (int)(double)(x)
  x == (int)(float)(x)
  d == (double)(float) d
  f == (float)(double) f
True
False
False
True

## Slide 31: Floating Point Operations
All the bitwise and logical operations still work
Float arithmetic operations done by separate hardware unit (FPU)

## Slide 32: Floating Point Addition
Float operations done by separate hardware unit (FPU)
  Assume E1 > E2
Exact Result:
  Sign s, significand M:
    Result of signed align & add
  Exponent E: E1
Fixing
  If M ≥ 2, shift M right, increment E
  if M < 1, shift M left k positions, decrement E by k
  Overflow if E out of range
  Round M to fit frac precision
(–1)s1 M1
(–1)s2 M2
E1–E2
+
(–1)s M
Get binary points lined up

## Slide 33: FP Multiplication
Exact Result:
  Sign s: s1 ^ s2
  Significand M: M1 x M2
  Exponent E: E1 + E2
Fixing
  If M ≥ 2, shift M right, increment E
  If E out of range, overflow
  Round M to fit frac precision
Implementation
  Biggest chore is multiplying significands

## Slide 34: Exercise 7: Feedback
Rate how well you think this recorded lecture worked
  Better than an in-person class
  About as well as an in-person class
  Less well than an in-person class, but you still learned something
  Total waste of time, you didn't learn anything
How much time did you spend on this video lecture (including time spent on exercises)?
Are there particular questions you’d like me to discuss in the problem session?
Do you have any other comments or feedback?