## Slide 1: Lecture 4: Floats
CS 105 Spring 2026

## Slide 2: Review: Representing Integers
unsigned:
signed (two's complement aka normal integers):
128 (27) | 64 (26) | 32 (25) | 16 (24) | 8 (23) | 4 (22) | 2 (21) | 1 (20)
-128 (27) | 64 (26) | 32 (25) | 16 (24) | 8 (23) | 4 (22) | 2 (21) | 1 (20)

## Slide 3: Fractional binary numbers
2i
2i-1
4
2
1
1/2
1/4
1/8
2-j
bi | bi-1 | ••• | b2 | b1 | b0 | b-1 | b-2 | b-3 | ••• | b-j
• • •
Representation
  Bits to right of “binary point” represent fractional powers of 2
  Represents rational number:
• • •

## Slide 4: Example: Fractional Binary Numbers
What is 1001.1012?
What is the binary representation of 13 9/16?
1101.
1001
Notes: 101.112
010.1112
001.01112

## Slide 5: Exercise 1: Fractional Binary Numbers
Translate the following fractional numbers to their binary representation
  5 3/4
  2 7/8
  1 7/16
Translate the following fractional binary numbers to their decimal representation
  .011
  .11
  1.1
101.11
10.111
1.0111
.375
.75
1.5
Notes:   Divide by 2 by shifting right (unsigned)
  Multiply by 2 by shifting left
  Numbers of form 0.111111…2 are just below 1.0
    1/2 + 1/4 + 1/8 + … + 1/2i + … ➙ 1.0

## Slide 6: Representable Numbers
Limitation #1
  Can only exactly represent numbers of the form x/2k
  Other rational numbers have repeating bit representations
  Value Representation
    1/3 0.0101010101[01]…2
    1/5 0.001100110011[0011]…2
    1/10 0.0001100110011[0011]…2
Limitation #2
  Just one setting of binary point within the w bits
  Limited range of numbers (very small values? very large?)

## Slide 7: Floating Point Representation
Numerical Form:
  Sign bit determines whether number is negative or positive
  Significand normally a (binary) fractional value in range [1.0,2.0)
  Exponent weights value by power of two
Examples:
  1.0
  -1.25
  64
  -.625
s = 0, M = 1.0, E = 0
s = 1, M = 1.01, E = 0
s = 0, M = 1.0, E = 6
s = 0, M = 1.01, E = -1
1.0
-1.01
1000000
-0.101
Notes: Define values s, M, E for each

## Slide 8: Exercise 2: Floating Point Numbers
For each of the following numbers, specify a bit s, binary fractional number M in [1.0,2.0) and a binary number E such that the number is equal to
  5 3/4
  2 7/8
  -1 1/2
  -3/4
101.11
10.111
-1.1
-0.11
s = 0, M = 1.0111, E = 2
s = 0, M = 1.0111, E = 1
s = 1, M = 1.1, E = 0
s = 1, M = 1.1, E = -1
Notes:   Define values s, M, E for each
  Divide by 2 by shifting right (unsigned)
  Multiply by 2 by shifting left
  Numbers of form 0.111111…2 are just below 1.0
    1/2 + 1/4 + 1/8 + … + 1/2i + … ➙ 1.0

## Slide 9: Floating Point Representation
Numerical Form:
  Sign bit determines whether number is negative or positive
  Significand normally a fractional value in range [1.0,2.0)
  Exponent weights value by power of two
Encoding:
  s is sign bit s
  exp field encodes (but is not equal to E)
    normally
  frac field encodes M (but is not equal to M)
    normally
bias
Float (32 bits):
k = 8, n = 23
bias = 127
Double (64 bits)
k=11, n = 52
bias = 1023
Notes: Normalize demo: 1.0 hex->interpretation on board, then 1.25, then demo exponent changes with bigger and smaller values

## Slide 10: Example: Floats
What fractional number is represented by the bytes 0x3ec00000? Assume big-endian order.
Float (32 bits):
k = 8, n = 23
bias = 127
  s is sign bit s
  exp field encodes (but is not equal to E)
    normally
  frac field encodes M (but is not equal to M)
    normally
0011 1110 1100 0000 0000 0000 0000 0000
s=0
exp=125
frac = 100000000000000000000002
s=0
E = -2
M = 1.100000000000000000000002 = 1.510
Notes: .375

## Slide 11: Exercise 3: Floats
What fractional number is represented by the bytes 0xc23c0000? Assume big-endian order.
Float (32 bits):
k = 8, n = 23
bias = 127
  s is sign bit s
  exp field encodes (but is not equal to E)
    normally
  frac field encodes M (but is not equal to M)
    normally

## Slide 12: Limitation so far…
How do we represent zero?
s | exp | frac
1 | 8-bits | 23-bits
Notes: .375

## Slide 13: Normalized and Denormalized
Normalized Values
  exp is neither all zeros nor all ones (normal case)
  exponent is defined as , where (e.g., 127 for float or 1023 for double)
  significand is defined as
Denormalized Values
  exp is either all zeros or all ones
  if all zeros: and
  if all ones: infinity (if frac is all zeros) or NaN (if frac is non-zero)
s | exp | frac

## Slide 14: Visualization: Floating Point Encodings
+
−
0
+Denorm
+Normalized
−Denorm
−Normalized
+0
NaN
NaN

## Slide 15: Limits of Floats
Denormalized Floats
Smallest Power of 2
  M = 0.000…01 =
  val =
Biggest Power of 2
  M = 0.100...00 =
  val =
Normalized Floats
Smallest Power of 2
  M = 1.000…00
  exp = 00000001 = 1
  val =
Biggest Power of 2
  M = 1.000...00 =
  exp = 11111110 = 254
  val =

## Slide 16: Example: Limits of Floats
There are big gaps between representable numbers (when exponent is big)
s | exp | frac
1 | 8-bits | 23-bits
0111 1111 0111 1111 1111 1111 1111 1111
s=0
E = 127
M = 1.111111111111111111111112

## Slide 17: Correctness
Example 1: Is (x + y) + z = x + (y + z)?
  Ints: Yes!
  Floats:
    (2^30 + -2^30) + 3.14 ➙ 3.14
    2^30 + (-2^30 + 3.14) ➙ 0.0

## Slide 18: Floating Point Operations
All of the bitwise and logical operations still work
Float arithmetic operations done by separate hardware unit (FPU)

## Slide 19: Floating Point Addition
Float operations done by separate hardware unit (FPU)
  Assume E1 >= E2
Exact Result:
  Sign s, significand M:
    Result of signed align & add
  Exponent E: E1
Fixing
  If M ≥ 2, shift M right, increment E
  if M < 1, shift M left k positions, decrement E by k
  Overflow if E out of range
  Round M to fit frac precision
(–1)s1 M1
(–1)s2 M2
E1–E2
+
(–1)s M
Get binary points lined up

## Slide 20: Floating Point Multiplication
Exact Result:
  Sign s: s1 ^ s2
  Significand M: M1 x M2
  Exponent E: E1 + E2
Fixing
  If M ≥ 2, shift M right, increment E
  If E out of range, overflow
  Round M to fit frac precision
Implementation
  Biggest chore is multiplying significands

## Slide 21: Floating Point in C
C Guarantees Two Levels
  float single precision (32 bits)
  double double precision (64 bits)
Conversions/Casting
  Casting between int, float, and double changes bit representation
  double/float → int
    Truncates fractional part
    Like rounding toward zero
    Not defined when out of range or NaN: Generally sets to TMin
  int → double
    Exact conversion,
  int → float
    Will round
This is what most languages
call floats!

## Slide 22: Example: Casting with Floats
Assume you have three variables: an int x, a float f, and a double d. Assume that all three variables store numeric values (not ,, or NaN). Which of the following expressions are guaranteed to evaluate to True?
  x == (int)(double)(x)
  x == (int)(float)(x)
  d == (double)(float) d
  f == (float)(double) f

## Slide 23: Example: Casting with Floats
Assume you have three variables: an int x, a float f, and a double d. Assume that all three variables store numeric values (not ,, or NaN). Which of the following expressions are guaranteed to evaluate to True?
  x == (int)(double)(x)
  x == (int)(float)(x)
  d == (double)(float) d
  f == (float)(double) f
True
False
False
True