## Slide 1: Lecture 25: Network Security
CS 138 Spring 2026

## Slide 2: Remote Adversaries

## Slide 3: Denial of Service Attacks
Goal: violate availability by making system unable to respond to requests from legitimate users
  Resource-saturation attacks
  Vulnerability-based attacks

## Slide 4: Networking Stack
7 - Application
6 - Presentation
5 - Session
4 - Transport
3 - Network
2 - Data Link
1 - Physical
HTTP
TLS/SSL
TCP/UDP
IP
Ethernet
0s and 1s
Deliver content
Manage encoding
Manage sessions
Deliver (un)reliably
Deliver globally
Deliver locally
Deliver signals

## Slide 5: Ping
The Internet Control Message Protocol (ICMP) is an network-layer support protocol used to pass operational information and error messages
traceroute: display path to a host in an IP network
ping: test reachability of a host in an IP network
  sends ICMP echo request packet to target host and waits for ICMP echo reply
  Uses CPU, network bandwidth
Notes: i

## Slide 6: Ping Flood

## Slide 7: Ping Flood
ping -f
Notes: https://www.youtube.com/watch?v=xGhB1Kp7Eow

## Slide 8: Defenses against Ping Floods
Disable ICMP functionality
Non-centralized firewalls

## Slide 9: UDP
User Datagram Protocol (UDP) is a connection-less, unreliable transport protocol, often used for streaming
in a UDP flood, attacker overwhelms server (or network) with large quantity of (useless) UDP packets
Flood

## Slide 10: TCP
Reliable
  acknowledgement
  checksum
  sequence number
In-order
  sequence number
Congestion control
  slow start
  congestion avoidance
  fast retransmit
  fast recovery

## Slide 11: SYN Flood
Notes: A syn flood is a form of DDoS attack that takes advantage of how TCP handles sessions. Recall that a session is established with a three-way TCP hand- shake: the source sends a SYN (synchronize) packet to the destination, the destination sends back a SYN+ACK packet, and the source completes the handshake by sending an ACK (acknowledge). The destination maintains a SYN RECV queue that keeps track handshakes in progress (those for which it has sent a SYN+ACK response but not yet received the final ACK). The default queue size on most modern machines is 1024 (machines with low memory have smaller queues); pending handshakes typically time out after minutes. A SYN flood proceeds by sending SYN packets but never completing the TCP handshake, filling up the queue and leaving the target unable to respond to additional incoming requests.
SYN floods are so common that TCP supports a special-purpose defense designed to mitigate this threat: SYN cookies. The idea is to eliminate the need to store pending SYN packets by encoding the necessary information in the sequence number using a pseudorandom function (more specifically, and HMAC). This prevents the SYN RECV queue from filling up, mitigating the thread of SYN floods. However, SYN cookies do not support all of the options available in the full TCP spec and are therefore officially recommended only as a last resort.

## Slide 12: Defending Against SYN Floods
Increase RECV queue size
Recycle oldest half-open connections
SYN cookies

## Slide 13: ACK Flood
Target
Attacker
Normal User
SYN
SYN-ACK
ACK
ACK
ACK
ACK
ACK

## Slide 14: Review: Domain Name System (DNS)
Principals are identified by names
  for web hosts, typically a domain name
  e.g., www.cs.pomona.edu
Internet hosts are identified by IP addresses
  used by network layer to route packets between hosts
The role of DNS is to translate between domain names and IP addresses
Notes: dig -t A pomona.edu

## Slide 15: DNS Flood

## Slide 16: DNS Flood
Notes: The Dyn DDOS attack was accomplished through a large number of DNS lookup requests from tens of millions of IP addresses
October 21, 2016
Victims include: Airbnb, BBC, CNN, Comcast, Fox News, The Guardian, GitHub, Netflix, Paypal, Reddit, Slack, Tumbler, Twitter, Verizon, Visa, Yelp

## Slide 17: DNS Reflection Attacks
Notes: dig -t A pomona.edu
dig -t ANY pomona.edu

## Slide 18: Botnets
Notes: https://github.com/0x27/linux.mirai/blob/master/mirai/bot/scanner.c
creates botnet, controlled 2.5 million machines at peak
password map: https://krebsonsecurity.com/wp-content/uploads/2016/10/IoTbadpass-Sheet1.pdf
owners identified January 2017, arrested, pled guilty December 2017
clones (eg., Darkai) still operational

## Slide 19: DDoS as a Service
Notes: https://krebsonsecurity.com/2018/04/ddos-for-hire-service-webstresser-dismantled/
Specify target, duration, method, pay with Paypal or bitcoin
WebStresser.org taken offline in April 2018, but many others do (and will) exist

## Slide 20: DDoS as a Service

## Slide 21: DDoS Attacks in 2025
Notes: Netscout 2025 report: https://www.netscout.com/threatreport/
https://vercara.digicert.com/resources/annual-ddos-report-2025-trends-and-insights

## Slide 22: DDoS Attacks in 2025

## Slide 23: Mitigating DoS Attacks
Notes: DDoS-mitigation strategies include content distribution (increasing the number of available replicas), distributed scrubbing (a distributed reverse proxy identifies and drops malformed or suspicious traffic), traffic shaping (buffering and rate-limiting incoming traffic), and egress filtering (preventing outgoing traffic from being used in a DDoS attack). As a general rule, DDoS mitigation depends on deploying extensive defensive resources and can be bypassed by a sufficiently determined and resourceful adversary.

## Slide 24: Mitigating DoS Attacks
Notes: Mitigating denial of service attacks is a complex and evolving art. Several companies (Akamai, CloudFlare, Google Shield) offer DDoS mitigation as a service, and their precise techniques are generally a closely-guarded trade secret.

## Slide 25: Denial of Service Attacks
Goal: violate availability by making system unable to respond to requests from legitimate users
  Resource-saturation attacks
  Vulnerability-based attacks

## Slide 26: Remote Requests
Port Open
Port Closed
No machine
  ICMP response from router
Machine but port closed
  TCP reset packet
Intercepted
  Silence (depends on config)

## Slide 27: Port Scanning
Starting Nmap 7.40 ( https://nmap.org ) at 2017-03-18 21:43 EDT
Nmap scan report for scanme.nmap.org (45.33.32.156)
Host is up (0.12s latency).
Other addresses for scanme.nmap.org (not scanned): 2600:3c01::f03c:91ff:fe18:bb2f
Not shown: 993 closed ports
PORT STATE SERVICE VERSION
21/tcp open ftp
22/tcp open ssh OpenSSH 6.6.1p1 Ubuntu 2ubuntu2.8 (Ubuntu Linux; protocol 2.0)
80/tcp open http Apache httpd 2.4.7 ((Ubuntu))
554/tcp open rtsp
7070/tcp open realserver
9929/tcp open nping-echo Nping echo
31337/tcp open Elite
Device type: general purpose
Running (JUST GUESSING): Linux 3.X (85%)
OS CPE: cpe:/o:linux:linux_kernel:3.13
Aggressive OS guesses: Linux 3.13 (85%)
No exact OS matches for host (test conditions non-ideal).
Network Distance: 13 hops
Service Info: OS: Linux; CPE: cpe:/o:linux:linux_kernel
Nmap done: 1 IP address (1 host up) scanned in 20.31 seconds
Notes: Computer Fraud and Abuse Act of America Section 1030(a)(5)(B). This act applies against anyone who “intentionally accesses a protected computer without authorization, and as a result of such conduct, causes damage” (and meets other requirements).

## Slide 28: Firewalls

## Slide 29: Packet Filtering
Protocol | Source IP | Dest. IP | Dest. Port | Action
TCP | * | 192.168.1.* | 25 | Permit
UDP | * | 192.168.1.* | 69 | Permit
TCP | 192.168.1.* | * | 80 | Permit
TCP | * | 192.168.1.18 | 80 | Permit
TCP | * | 192.168.1.* | * | Deny
TCP | * | 192.168.1.* | * | Deny

## Slide 30: Stateful Inspection
Notes: Discussion: how to detect/mitigate a port scan
SYN frequency: use keyed hash table & count SYNs, problem: attacker learns limit
sequential behavior: store last dest & count increment-by-1, problem: randomize order
diversity: count unique ip-port pairs, problem: complicated
failures: track failure/success ratio
anomaly detection: dest ip-port has probability P(d), high (5-10%) for popular dests, low for weird ones), accumulate anomaly score –log (P(d))

## Slide 31: Deep-Packet Inspection
alert tcp $EXTERNAL_NET any -> $HOME_NET 53 (msg:"OS-LINUX OS-LINUX x86 Linux overflow attempt"; flow:to_server,established; content:"1|C0 B0 02 CD 80 85 C0|uL|EB|L^|B0|"; metadata:ruleset community, service dns; classtype:attempted-admin; sid:264; rev:13;)

## Slide 32: But there's a problem…
Notes: https://transparencyreport.google.com/https/overview?hl=en

## Slide 33: Machine Learning

## Slide 34: Network Security