## Slide 1: Memory
CS51 – Spring 2026
Computer Systems
Notes: Today we will continue seeing circuits, but this time sequential circuits.

## Slide 2: Administrative
Assignment 3
Assignment 4
  Released
  Don’t forget to do pre-lab
Lab tomorrow

## Slide 3: 2-bit decoder recap
What does a 2-bit decoder do?

## Slide 4: 2-bit decoder recap
Sends ‘1’ along one input line according to d1 d0
enable=0 turns off all lines
d1 | d0 | out0 | out1 | out3 | out3
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1

## Slide 5: 3-bit decoder
acts as the enable bit to two decoders.
When is 0, the top decoder is activated, sending output to one of t0xx.
When is 1, the bottom decoder is activated, sending output to one of t1xx.
Inputs |  |  | Outputs |  |  |  |  |  |  | 
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Inputs |  |  | Outputs |  |  |  |  |  |  | 
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 6: Decoder application example
How do clocks like this work?

## Slide 7: Decoding 7-segment displays
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
7 segments, labeled a to g
Different combinations of these segments, generate the digits 0-9

## Slide 8: 7-segment display
Number to display
circuit
c
d
g
f
e
b
a
a b c d
e f g
hardware component with 7 inputs

## Slide 9: 7-segment display
Number to display
circuit
c
d
g
f
e
b
a
7
c
d
g
f
e
b
a
a = 0
b = 0
c = 1
d = 1
e = 0
f = 0
g = 1
hardware component with 7 inputs
a b c d
e f g

## Slide 10: 7-segment displays in clocks
Digit | Illuminated segments |  |  |  |  |  | 
 | a | b | c | d | e | f | g
0 |  | x | x | x | x | x | x
1 |  |  |  | x |  |  | x
2 | x |  | x | x | x | x | 
3 | x |  | x | x |  | x | x
4 | x | x |  | x |  |  | x
5 | x | x | x |  |  | x | x
6 | x | x | x |  | x | x | x
7 |  |  | x | x |  |  | x
8 | x | x | x | x | x | x | x
9 | x | x | x | x |  |  | x
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c

## Slide 11: 7-segment display
Number to display
circuit
c
d
g
f
e
b
a
a b c d
e f g
hardware component with 7 inputs
How many binary inputs do we need for the numbers 0-9?

## Slide 12: Decoding 7-segment displays in clocks
Input | Digit | Illuminated segments |  |  |  |  |  | 
 |  | a | b | c | d | e | f | g
0000 | 0 |  | x | x | x | x | x | x
0001 | 1 |  |  |  | x |  |  | x
0010 | 2 | x |  | x | x | x | x | 
0011 | 3 | x |  | x | x |  | x | x
0100 | 4 | x | x |  | x |  |  | x
0101 | 5 | x | x | x |  |  | x | x
0110 | 6 | x | x | x |  | x | x | x
0111 | 7 |  |  | x | x |  |  | x
1000 | 8 | x | x | x | x | x | x | x
1001 | 9 | x | x | x | x |  |  | x
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c

## Slide 13: Our friend the decoder
4-input bits
decoder
2-bit decoder: 4 output lines
3-bit decoder: 8 output lines
How many output lines?

## Slide 14: Our friend the decoder
4-input bits
decoder
2-bit decoder: 4 output lines
3-bit decoder: 8 output lines
16 output lines: exactly 1 will be activated depending on the input

## Slide 15: Our friend the decoder
Input | Digit | Illuminated segments |  |  |  |  |  | 
 |  | a | b | c | d | e | f | g
0000 | 0 |  | x | x | x | x | x | x
a b c d
e f g
0000
decoder
c
d
g
f
e
b
a
0000 line will be 1
all others will be 0

## Slide 16: Our friend the decoder
Input | Digit | Illuminated segments |  |  |  |  |  | 
 |  | a | b | c | d | e | f | g
0000 | 0 |  | x | x | x | x | x | x
a b c d
e f g
0000
decoder
c
d
g
f
e
b
a
0000 line will be 1
all others will be 0
c
d
g
f
e
b
a
How do we get it to display a 0?

## Slide 17: Our friend the decoder
Input | Digit | Illuminated segments |  |  |  |  |  | 
 |  | a | b | c | d | e | f | g
0000 | 0 |  | x | x | x | x | x | x
a b c d
e f g
0000
decoder
c
d
g
f
e
b
a
0000 line will be 1
all others will be 0
c
d
g
f
e
b
a
Connect the 0000 line to: b c d e f g
When the line is active those segments will illuminate
When it’s not active, no display

## Slide 18: Our friend the decoder
Input | Digit | Illuminated segments |  |  |  |  |  | 
 |  | a | b | c | d | e | f | g
0001 | 1 |  |  |  | x |  |  | x
a b c d
e f g
0001
decoder
c
d
g
f
e
b
a
0001 line will be 1
all others will be 0
How do we get it to display a 1?
c
d
g
f
e
b
a

## Slide 19: Our friend the decoder
Input | Digit | Illuminated segments |  |  |  |  |  | 
 |  | a | b | c | d | e | f | g
0001 | 1 |  |  |  | x |  |  | x
a b c d
e f g
0001
decoder
c
d
g
f
e
b
a
0001 line will be 1
all others will be 0
c
d
g
f
e
b
a
Connect the 0001 line to: d g
When the line is active those segments will illuminate
When it’s not active, no display

## Slide 20: Our friend the decoder
Input | Digit | Illuminated segments |  |  |  |  |  | 
 |  | a | b | c | d | e | f | g
0000 | 0 |  | x | x | x | x | x | x
0001 | 1 |  |  |  | x |  |  | x
a b c d
e f g
decoder
c
d
g
f
e
b
a
0001 line
4-input bits
0000 line
Both of these lines want to connect to d
How do we do this? Hint: gate??

## Slide 21: Our friend the decoder
Input | Digit | Illuminated segments |  |  |  |  |  | 
 |  | a | b | c | d | e | f | g
0000 | 0 |  | x | x | x | x | x | x
0001 | 1 |  |  |  | x |  |  | x
a b c d
e f g
decoder
c
d
g
f
e
b
a
0001 line
4-input bits
0000 line
Since only one line will be active at a time, use OR gate

## Slide 22: A 7-segment display in Logisim
Input | Digit | Illuminated segments |  |  |  |  |  | 
 |  | a | b | c | d | e | f | g
0000 | 0 |  | x | x | x | x | x | x
0001 | 1 |  |  |  | x |  |  | x
0010 | 2 | x |  | x | x | x | x | 
0011 | 3 | x |  | x | x |  | x | x
0100 | 4 | x | x |  | x |  |  | x
0101 | 5 | x | x | x |  |  | x | x
0110 | 6 | x | x | x |  | x | x | x
0111 | 7 |  |  | x | x |  |  | x
1000 | 8 | x | x | x | x | x | x | x
1001 | 9 | x | x | x | x |  |  | x
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
a
b
c
d
e
f
g
Notes: Cool stuff?

## Slide 23: A 7-segment display in Logisim
Check it out!

## Slide 24: PRACTICE TIME – Expanding to 16 characters
Input | Character | Illuminated segments |  |  |  |  |  | 
 |  | a | b | c | d | e | f | g
0000 | 0 |  | x | x | x | x | x | x
0001 | 1 |  |  |  | x |  |  | x
0010 | 2 | x |  | x | x | x | x | 
0011 | 3 | x |  | x | x |  | x | x
0100 | 4 | x | x |  | x |  |  | x
0101 | 5 | x | x | x |  |  | x | x
0110 | 6 | x | x | x |  | x | x | x
0111 | 7 |  |  | x | x |  |  | x
1000 | 8 | x | x | x | x | x | x | x
1001 | 9 | x | x | x | x |  |  | x
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
Imagine that the 7-segment display we have built so far is expanded to include 16 characters, the existing 10 digits, and A-F, as depicted here to differentiate among them.
How will the design of the circuit change on Logisim-Evolution?

## Slide 25: ANSWER– Expanding to 16 characters
Input | Character | Illuminated segments |  |  |  |  |  | 
 |  | a | b | c | d | e | f | g
0000 | 0 |  | x | x | x | x | x | x
0001 | 1 |  |  |  | x |  |  | x
0010 | 2 | x |  | x | x | x | x | 
0011 | 3 | x |  | x | x |  | x | x
0100 | 4 | x | x |  | x |  |  | x
0101 | 5 | x | x | x |  |  | x | x
0110 | 6 | x | x | x |  | x | x | x
0111 | 7 |  |  | x | x |  |  | x
1000 | 8 | x | x | x | x | x | x | x
1001 | 9 | x | x | x | x |  |  | x
1010 | A | x | x | x | x | x |  | x
1011 | B | x | x |  |  | x | x | x
1100 | C | x |  |  |  | x | x | 
1101 | D | x |  |  | x | x | x | x
1110 | E | x | x | x |  | x | x | 
1111 | F | x | x | x |  | x |  | 
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
Expanded table:
Circuit in Logisim-Evolution is expanded to include all outputs of decoders connected to 6 additional or gates

## Slide 26: Combinational circuits
All circuits we have seen have been combinational: their output depends on the present inputs and there is no notion of memory of past inputs.
combinational circuits perform arithmetic and logical operations, transmit data, or convert code. So far, we have seen for
  Arithmetic and logical operations: logic circuits and half/full/and ripple-carry adders
  Transmit data: decoders (and we will see multiplexers in the next assignment)
  Convert code: 7-segment display decoders

## Slide 27: Computer simplified
hard drive
media drive
CPU
RAM
“the computer”
display
network
input devices

## Slide 28: Inside the CPU: Arithmetic Logic Unit (ALU)
Performs arithmetic and logical operations
Arithmetic: add, subtract, multiply, …
Logical: AND, OR, shift

## Slide 29: Inside the CPU: Arithmetic Logic Unit (ALU)
Performs arithmetic and logical operations
Arithmetic: add, subtract, multiply, …
Logical: AND, OR, shift
Opcode specifies what operation
(encoded in binary)

## Slide 30: Inside the CPU: Arithmetic Logic Unit (ALU)
Performs arithmetic and logical operations
Arithmetic: add, subtract, multiply, …
Logical: AND, OR, shift
Opcode specifies what operation
(encoded in binary)
Where do the numbers come from?

## Slide 31: Inside the CPU
CPU
processor
…
registers
Floating-point unit (FPU)
…
registers: local, fast memory slots

## Slide 32: Memory hierarchy
processor
…
registers
RAM
hard drive
Why do we have these different types of memory?

## Slide 33: Memory speed
operation | access time | times slower than register access | for comparison…
register | 0.3 ns | 1 | 1 s
RAM | 120 ns | 400 | 6 min
Hard disk (SSD) | 1ms | ~million | 1 month
Hard disk (HDD) | 10ms | ~million | 10 months
google.com | 0.4s | ~billion | 30 years

## Slide 34: Memory
RAM
010101111000101000010010 …
What is a byte?
?

## Slide 35: Memory
RAM
01010111 10001010 00010010 …
byte = 8 bits
byte is abbreviated as B
My laptop has 64GB (gigabytes) of memory. How many bits is that?

## Slide 36
Units of memory
Bit:
Nibble:
Byte: 8 bits
Kilobyte (KB):
Megabyte (MB)
Gigabyte (GB):
Terabyte (TB):

## Slide 37
Units of memory
Bit: the smallest unit of memory.
Nibble: 4 bits, half a byte
Byte: 8 bits, the basic unit of measuring memory. Notation is B, e.g., 8B is 8 bytes or 64 bits.
Kilobyte (KB): bytes bytes. (thousand bytes)
  Kibibyte = 210 bytes = 1024 bytes (approximately a thousand bytes)
Megabyte (MB): Kilobytes = bytes. (million bytes)
Gigabyte (GB): Megabytes = bytes. (billion bytes)
Terabyte (TB): Gigabytes = bytes. (quadrillion bytes)

## Slide 38: Memory
RAM
01010111 10001010 00010010 …
byte = 8 bits
byte is abbreviated as B
My laptop has 64GB (gigabytes) of memory. How many bits is that?

## Slide 39: Memory
RAM
01010111 10001010 00010010 …
byte = 8 bits
byte is abbreviated as B
64GB = 64,000,000,000 = 64 billion bytes = 512 billion bits

## Slide 40: Memory hierarchy
processor
…
registers
RAM
hard drive
Capacity:
hundreds of registers
Gigabytes
Terabytes

## Slide 41: Memory
RAM
01010111
10001010
0001001
01011010
…
Memory is byte addressable
address
0
1
2
3
…

## Slide 42: Memory
RAM
01010111
10001010
0001001
01011010
…
Memory is organized into “words”, which is the most common functional unit
address
0
1
2
3
…

## Slide 43: Memory
RAM
10101011 10001010 00010010 01011010
11001011 00001110 01010010 01010110
10111011 10010010 00000000 01110100
…
Most modern computers use 32-bit (4 byte) or 64-bit (8 byte) words
address
0
4
8
...
32-bit words

## Slide 44: Memory capacity
Memory is commonly byte addressable (i.e., we can ask for a specific byte)
32-bit processors access memory locations using a 32-bit number
What is the largest a 32-bit, byte-addressable memory can be? Hint: how many unique addresses are possible?

## Slide 45: Memory capacity
With 32 bits, we can represent 232 unique numbers.
We could therefore address about 4 billion bytes, which is 4GB

## Slide 46: Memory capacity
64-bit processors access memory locations using a 64-bit number
What is the largest a 64-bit, byte-addressable memory can be? Hint: how many unique addresses are possible?

## Slide 47: Memory capacity
With 64 bits, we can represent 232 unique numbers.
KB, GB, TB, Petabyte, Exabyte
16 Exabytes = 16 * 106 TB = 16 Million Terabytes

## Slide 48
Memory implemented
Memory is generally implemented as a grid/matrix of bytes
16 rows
16 columns
 | c0 | c1 | c2 | c3 | c4 | c5 | c6 | c7 | c8 | c9 | c10 | c11 | c12 | c13 | c14 | c15
r0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r11 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r13 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r14 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Notes: Let's think now how do we go about implementing a 2^𝑁x〖 2〗^M memory array?
We want to organize the words in 2^𝑁 rows and 2^𝑀 columns.
We already saw that we can reference a particular row/word if we had and address of 𝑁 bits. We will consider this number as the row address.
How many bits would we need to address a particular column?
  𝑀. This is our column address
We can pack together this 𝑁+𝑀 bits into a single number that we can use to address a specific memory cell.

## Slide 49
Memory implemented
Memory is generally implemented as a grid/matrix of bytes
16 rows
16 columns
 | c0 | c1 | c2 | c3 | c4 | c5 | c6 | c7 | c8 | c9 | c10 | c11 | c12 | c13 | c14 | c15
r0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r11 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r13 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r14 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
How much memory is this?
Notes: Let's think now how do we go about implementing a 2^𝑁x〖 2〗^M memory array?
We want to organize the words in 2^𝑁 rows and 2^𝑀 columns.
We already saw that we can reference a particular row/word if we had and address of 𝑁 bits. We will consider this number as the row address.
How many bits would we need to address a particular column?
  𝑀. This is our column address
We can pack together this 𝑁+𝑀 bits into a single number that we can use to address a specific memory cell.

## Slide 50
Memory implemented
Memory is generally implemented as a grid/matrix of bytes
16 rows
16 columns
 | c0 | c1 | c2 | c3 | c4 | c5 | c6 | c7 | c8 | c9 | c10 | c11 | c12 | c13 | c14 | c15
r0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r11 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r13 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r14 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
= 256 bytes
Notes: Let's think now how do we go about implementing a 2^𝑁x〖 2〗^M memory array?
We want to organize the words in 2^𝑁 rows and 2^𝑀 columns.
We already saw that we can reference a particular row/word if we had and address of 𝑁 bits. We will consider this number as the row address.
How many bits would we need to address a particular column?
  𝑀. This is our column address
We can pack together this 𝑁+𝑀 bits into a single number that we can use to address a specific memory cell.

## Slide 51
Memory implemented
16 rows
16 columns
 | c0 | c1 | c2 | c3 | c4 | c5 | c6 | c7 | c8 | c9 | c10 | c11 | c12 | c13 | c14 | c15
r0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r11 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r13 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r14 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
We can access a given by via a row index and a column index
What row/column would this entry be? (Assuming indices start at 0)
Notes: Let's think now how do we go about implementing a 2^𝑁x〖 2〗^M memory array?
We want to organize the words in 2^𝑁 rows and 2^𝑀 columns.
We already saw that we can reference a particular row/word if we had and address of 𝑁 bits. We will consider this number as the row address.
How many bits would we need to address a particular column?
  𝑀. This is our column address
We can pack together this 𝑁+𝑀 bits into a single number that we can use to address a specific memory cell.

## Slide 52
Memory implemented
16 rows
16 columns
 | c0 | c1 | c2 | c3 | c4 | c5 | c6 | c7 | c8 | c9 | c10 | c11 | c12 | c13 | c14 | c15
r0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r11 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r13 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r14 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
We can access a given by via a row index and a column index
row = 4, column = 3
Notes: Let's think now how do we go about implementing a 2^𝑁x〖 2〗^M memory array?
We want to organize the words in 2^𝑁 rows and 2^𝑀 columns.
We already saw that we can reference a particular row/word if we had and address of 𝑁 bits. We will consider this number as the row address.
How many bits would we need to address a particular column?
  𝑀. This is our column address
We can pack together this 𝑁+𝑀 bits into a single number that we can use to address a specific memory cell.

## Slide 53
Memory implemented
16 rows
16 columns
 | c0 | c1 | c2 | c3 | c4 | c5 | c6 | c7 | c8 | c9 | c10 | c11 | c12 | c13 | c14 | c15
r0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r11 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r13 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r14 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
We can access a given by via a row index and a column index
Everything is binary: how many bits do we need to specify the row and column?
Notes: Let's think now how do we go about implementing a 2^𝑁x〖 2〗^M memory array?
We want to organize the words in 2^𝑁 rows and 2^𝑀 columns.
We already saw that we can reference a particular row/word if we had and address of 𝑁 bits. We will consider this number as the row address.
How many bits would we need to address a particular column?
  𝑀. This is our column address
We can pack together this 𝑁+𝑀 bits into a single number that we can use to address a specific memory cell.

## Slide 54
Memory implemented
16 rows
16 columns
 | c0 | c1 | c2 | c3 | c4 | c5 | c6 | c7 | c8 | c9 | c10 | c11 | c12 | c13 | c14 | c15
r0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r11 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r13 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r14 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
We can access a given by via a row index and a column index
4 bits each for a total of 8 bits
<8-bit memory address>
4 bits for row
4 bits for column
Notes: Let's think now how do we go about implementing a 2^𝑁x〖 2〗^M memory array?
We want to organize the words in 2^𝑁 rows and 2^𝑀 columns.
We already saw that we can reference a particular row/word if we had and address of 𝑁 bits. We will consider this number as the row address.
How many bits would we need to address a particular column?
  𝑀. This is our column address
We can pack together this 𝑁+𝑀 bits into a single number that we can use to address a specific memory cell.

## Slide 55
Memory implemented
16 rows
16 columns
 | c0 | c1 | c2 | c3 | c4 | c5 | c6 | c7 | c8 | c9 | c10 | c11 | c12 | c13 | c14 | c15
r0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r11 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r13 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r14 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
We can access a given by via a row index and a column index
What would be this memory address in binary?
<8-bit memory address>
4 bits for row
4 bits for column
Notes: Let's think now how do we go about implementing a 2^𝑁x〖 2〗^M memory array?
We want to organize the words in 2^𝑁 rows and 2^𝑀 columns.
We already saw that we can reference a particular row/word if we had and address of 𝑁 bits. We will consider this number as the row address.
How many bits would we need to address a particular column?
  𝑀. This is our column address
We can pack together this 𝑁+𝑀 bits into a single number that we can use to address a specific memory cell.

## Slide 56
Memory implemented
16 rows
16 columns
 | c0 | c1 | c2 | c3 | c4 | c5 | c6 | c7 | c8 | c9 | c10 | c11 | c12 | c13 | c14 | c15
r0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r11 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r13 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r14 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
We can access a given by via a row index and a column index
0100 0011
row
column
Notes: Let's think now how do we go about implementing a 2^𝑁x〖 2〗^M memory array?
We want to organize the words in 2^𝑁 rows and 2^𝑀 columns.
We already saw that we can reference a particular row/word if we had and address of 𝑁 bits. We will consider this number as the row address.
How many bits would we need to address a particular column?
  𝑀. This is our column address
We can pack together this 𝑁+𝑀 bits into a single number that we can use to address a specific memory cell.

## Slide 57
Memory implemented
16 rows
16 columns
 | c0 | c1 | c2 | c3 | c4 | c5 | c6 | c7 | c8 | c9 | c10 | c11 | c12 | c13 | c14 | c15
r0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r11 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r13 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r14 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
We can access a given by via a row index and a column index
What would be this memory address in binary?
<8-bit memory address>
4 bits for row
4 bits for column
Notes: Let's think now how do we go about implementing a 2^𝑁x〖 2〗^M memory array?
We want to organize the words in 2^𝑁 rows and 2^𝑀 columns.
We already saw that we can reference a particular row/word if we had and address of 𝑁 bits. We will consider this number as the row address.
How many bits would we need to address a particular column?
  𝑀. This is our column address
We can pack together this 𝑁+𝑀 bits into a single number that we can use to address a specific memory cell.

## Slide 58
Memory implemented
16 rows
16 columns
 | c0 | c1 | c2 | c3 | c4 | c5 | c6 | c7 | c8 | c9 | c10 | c11 | c12 | c13 | c14 | c15
r0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r11 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r13 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r14 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
We can access a given by via a row index and a column index
Note we use unsigned numbers
1101 0100
row
column
Notes: Let's think now how do we go about implementing a 2^𝑁x〖 2〗^M memory array?
We want to organize the words in 2^𝑁 rows and 2^𝑀 columns.
We already saw that we can reference a particular row/word if we had and address of 𝑁 bits. We will consider this number as the row address.
How many bits would we need to address a particular column?
  𝑀. This is our column address
We can pack together this 𝑁+𝑀 bits into a single number that we can use to address a specific memory cell.

## Slide 59: Quick aside
4-bit decoder
4 bits
decoder
How many lines out?

## Slide 60: Quick aside
4-bit decoder
4 bits
decoder
16 lines out, exactly one line will be 1

## Slide 61: Quick aside: multiplexer
16:1 multiplexer
4 bits
decoder
How many lines out?

## Slide 62: Quick aside: multiplexer
4:1 multiplexer
4 inputs
2 inputs to “select” which line

## Slide 63: Quick aside: multiplexer
4:1 multiplexer
4 inputs
0 0

## Slide 64: Quick aside: multiplexer
4:1 multiplexer
4 inputs
1 0

## Slide 65: Quick aside: multiplexer
16:1 multiplexer
16 inputs
4 inputs to “select” which line

## Slide 66
From addresses to actual memory cells
The decoder will be responsible for taking the 4-bits of the row address and mapping it to one of the 16 rows.
The multiplexer will be responsible for taking the 4-bits of the column address as selection lines and to map to a single column.
Column address multiplexer
 | c0 | c1 | c2 | c3 | c4 | c5 | c6 | c7 | c8 | c9 | c10 | c11 | c12 | c13 | c14 | c15
r0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r11 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r13 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r14 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
r15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4-bit column
address
4-bit row
address
Row address decoder
Notes: To convert from an address to the actual memory cell that contains the desired bit, we will utilize one multiplexer and one decoder.
The decoder will be responsible for taking the 4-bits of the row address and mapping it to one of the 16 rows.
The multiplexer will be responsible for taking the 4-bits of the column address as selection lines and to map to a single column.

## Slide 67: How do we store bits?
Anything unusual about this circuit?

## Slide 68: Case I: ,
Case | Input |  | Output | 
IV | 0 | 0 |  | 
I | 0 | 1 |  | 
II | 1 | 0 |  | 
III | 1 | 1 |  | 
Case | Input |  | Output | 
IV | 0 | 0 |  | 
I | 0 | 1 |  | 
II | 1 | 0 |  | 
III | 1 | 1 |  | 
What will be the output?
X | Y | X Y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
X | Y | 
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
0
1
Notes: Case I will be R=1 and S=0. Remember, NOR is the negation of the OR gate: it produces TRUE/1 only when both its inputs are FALSE/0. The NOR gate 𝑁_1 sees that 𝑅 is 1 so it produces 0 for 𝑄. The NOR gate 𝑁_2 sees both 𝑄 and 𝑆 being 0 so it produces 1 for 𝑄′.

## Slide 69: Case I: ,
Case | Input |  | Output | 
IV | 0 | 0 |  | 
I | 0 | 1 | 0 | 1
II | 1 | 0 |  | 
III | 1 | 1 |  | 
Case | Input |  | Output | 
IV | 0 | 0 |  | 
I | 0 | 1 | 0 | 1
II | 1 | 0 |  | 
III | 1 | 1 |  | 
What will be the output?
X | Y | X Y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
X | Y | 
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
0
0
1
1
0
1
Notes: Case I will be R=1 and S=0. Remember, NOR is the negation of the OR gate: it produces TRUE/1 only when both its inputs are FALSE/0. The NOR gate 𝑁_1 sees that 𝑅 is 1 so it produces 0 for 𝑄. The NOR gate 𝑁_2 sees both 𝑄 and 𝑆 being 0 so it produces 1 for 𝑄′.

## Slide 70: Case II: ,
Case | Input |  | Output | 
IV | 0 | 0 |  | 
I | 0 | 1 | 0 | 1
II | 1 | 0 |  | 
III | 1 | 1 |  | 
Case | Input |  | Output | 
IV | 0 | 0 |  | 
I | 0 | 1 | 0 | 1
II | 1 | 0 |  | 
III | 1 | 1 |  | 
What will be the output?
X | Y | X Y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
X | Y | 
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
1
0
Notes: Case I will be R=1 and S=0. Remember, NOR is the negation of the OR gate: it produces TRUE/1 only when both its inputs are FALSE/0. The NOR gate 𝑁_1 sees that 𝑅 is 1 so it produces 0 for 𝑄. The NOR gate 𝑁_2 sees both 𝑄 and 𝑆 being 0 so it produces 1 for 𝑄′.

## Slide 71: Case II: ,
Case | Input |  | Output | 
IV | 0 | 0 |  | 
I | 0 | 1 | 0 | 1
II | 1 | 0 | 1 | 0
III | 1 | 1 |  | 
Case | Input |  | Output | 
IV | 0 | 0 |  | 
I | 0 | 1 | 0 | 1
II | 1 | 0 | 1 | 0
III | 1 | 1 |  | 
What will be the output?
X | Y | X Y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
X | Y | 
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
1
1
0
0
1
0
Notes: Case I will be R=1 and S=0. Remember, NOR is the negation of the OR gate: it produces TRUE/1 only when both its inputs are FALSE/0. The NOR gate 𝑁_1 sees that 𝑅 is 1 so it produces 0 for 𝑄. The NOR gate 𝑁_2 sees both 𝑄 and 𝑆 being 0 so it produces 1 for 𝑄′.

## Slide 72: Case IV: ,
Case | Input |  | Output | 
IV | 0 | 0 |  | 
I | 0 | 1 | 0 | 1
II | 1 | 0 | 1 | 0
III | 1 | 1 |  | 
Case | Input |  | Output | 
IV | 0 | 0 |  | 
I | 0 | 1 | 0 | 1
II | 1 | 0 | 1 | 0
III | 1 | 1 |  | 
What will be the output?
X | Y | X Y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
X | Y | 
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
1
0
0
0
Notes: Case I will be R=1 and S=0. Remember, NOR is the negation of the OR gate: it produces TRUE/1 only when both its inputs are FALSE/0. The NOR gate 𝑁_1 sees that 𝑅 is 1 so it produces 0 for 𝑄. The NOR gate 𝑁_2 sees both 𝑄 and 𝑆 being 0 so it produces 1 for 𝑄′.

## Slide 73: Case IV: ,
Case | Input |  | Output | 
IV | 0 | 0 |  | 
I | 0 | 1 | 0 | 1
II | 1 | 0 | 1 | 0
III | 1 | 1 |  | 
Case | Input |  | Output | 
IV | 0 | 0 |  | 
I | 0 | 1 | 0 | 1
II | 1 | 0 | 1 | 0
III | 1 | 1 |  | 
What will be the output?
X | Y | X Y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
X | Y | 
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
1
0
0
0
0
1
nothing changes
Notes: Case I will be R=1 and S=0. Remember, NOR is the negation of the OR gate: it produces TRUE/1 only when both its inputs are FALSE/0. The NOR gate 𝑁_1 sees that 𝑅 is 1 so it produces 0 for 𝑄. The NOR gate 𝑁_2 sees both 𝑄 and 𝑆 being 0 so it produces 1 for 𝑄′.

## Slide 74: Case IV: ,
Case | Input |  | Output | 
IV | 0 | 0 |  | 
I | 0 | 1 | 0 | 1
II | 1 | 0 | 1 | 0
III | 1 | 1 |  | 
Case | Input |  | Output | 
IV | 0 | 0 |  | 
I | 0 | 1 | 0 | 1
II | 1 | 0 | 1 | 0
III | 1 | 1 |  | 
What will be the output?
X | Y | X Y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
X | Y | 
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
0
1
0
0
Notes: Case I will be R=1 and S=0. Remember, NOR is the negation of the OR gate: it produces TRUE/1 only when both its inputs are FALSE/0. The NOR gate 𝑁_1 sees that 𝑅 is 1 so it produces 0 for 𝑄. The NOR gate 𝑁_2 sees both 𝑄 and 𝑆 being 0 so it produces 1 for 𝑄′.

## Slide 75: Case IV: ,
Case | Input |  | Output | 
IV | 0 | 0 |  | 
I | 0 | 1 | 0 | 1
II | 1 | 0 | 1 | 0
III | 1 | 1 |  | 
Case | Input |  | Output | 
IV | 0 | 0 |  | 
I | 0 | 1 | 0 | 1
II | 1 | 0 | 1 | 0
III | 1 | 1 |  | 
What will be the output?
X | Y | X Y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
X | Y | 
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
0
1
0
0
0
1
nothing changes
Notes: Case I will be R=1 and S=0. Remember, NOR is the negation of the OR gate: it produces TRUE/1 only when both its inputs are FALSE/0. The NOR gate 𝑁_1 sees that 𝑅 is 1 so it produces 0 for 𝑄. The NOR gate 𝑁_2 sees both 𝑄 and 𝑆 being 0 so it produces 1 for 𝑄′.

## Slide 76: Case IV: ,
0
1
0
0
0
1
1
0
0
0
0
1
0
1
0
0
1
0
0
0
Notes: Case I will be R=1 and S=0. Remember, NOR is the negation of the OR gate: it produces TRUE/1 only when both its inputs are FALSE/0. The NOR gate 𝑁_1 sees that 𝑅 is 1 so it produces 0 for 𝑄. The NOR gate 𝑁_2 sees both 𝑄 and 𝑆 being 0 so it produces 1 for 𝑄′.

## Slide 77: SR-latch
Case | Input |  | Output | 
IV | 0 | 0 |  | 
I | 0 | 1 | 0 | 1
II | 1 | 0 | 1 | 0
III | 1 | 1 |  | 
Case | Input |  | Output | 
IV | 0 | 0 |  | 
I | 0 | 1 | 0 | 1
II | 1 | 0 | 1 | 0
III | 1 | 1 |  | 
Hold current state
Reset: Q = 0
Set: Q = 1
messy… not allowed

## Slide 78: Case III: ,
Case | Input |  | Output | 
IV | 0 | 0 |  | 
I | 0 | 1 | 0 | 1
II | 1 | 0 | 1 | 0
III | 1 | 1 |  | 
Case | Input |  | Output | 
IV | 0 | 0 |  | 
I | 0 | 1 | 0 | 1
II | 1 | 0 | 1 | 0
III | 1 | 1 |  | 
What will be the output?
X | Y | X Y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
X | Y | 
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Notes: Case I will be R=1 and S=0. Remember, NOR is the negation of the OR gate: it produces TRUE/1 only when both its inputs are FALSE/0. The NOR gate 𝑁_1 sees that 𝑅 is 1 so it produces 0 for 𝑄. The NOR gate 𝑁_2 sees both 𝑄 and 𝑆 being 0 so it produces 1 for 𝑄′.

## Slide 79: Case III: ,
Case | Input |  | Output | 
IV | 0 | 0 |  | 
I | 0 | 1 | 0 | 1
II | 1 | 0 | 1 | 0
III | 1 | 1 | 0 | 0
Case | Input |  | Output | 
IV | 0 | 0 |  | 
I | 0 | 1 | 0 | 1
II | 1 | 0 | 1 | 0
III | 1 | 1 | 0 | 0
What will be the output?
X | Y | X Y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
X | Y | 
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
1
1
0
0
0
0
Notes: Case I will be R=1 and S=0. Remember, NOR is the negation of the OR gate: it produces TRUE/1 only when both its inputs are FALSE/0. The NOR gate 𝑁_1 sees that 𝑅 is 1 so it produces 0 for 𝑄. The NOR gate 𝑁_2 sees both 𝑄 and 𝑆 being 0 so it produces 1 for 𝑄′.

## Slide 80: Case I: ,
Case | Input |  | Output | 
IV | 0 | 0 |  | 
I | 0 | 1 | 0 | 1
II | 1 | 0 | 1 | 0
III | 1 | 1 | 0 | 0
Case | Input |  | Output | 
IV | 0 | 0 |  | 
I | 0 | 1 | 0 | 1
II | 1 | 0 | 1 | 0
III | 1 | 1 | 0 | 0
What will be the output?
X | Y | X Y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
X | Y | 
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
0
0
Notes: Case I will be R=1 and S=0. Remember, NOR is the negation of the OR gate: it produces TRUE/1 only when both its inputs are FALSE/0. The NOR gate 𝑁_1 sees that 𝑅 is 1 so it produces 0 for 𝑄. The NOR gate 𝑁_2 sees both 𝑄 and 𝑆 being 0 so it produces 1 for 𝑄′.

## Slide 81: SR-latch - Abstraction
As an application of abstraction, instead of seeing the full circuit on the right, you might encounter the following symbol for SR-latches:
’
Notes: As an application of abstraction, instead of seeing the full circuit on the right, you might encounter the following symbol for SR-latches.

## Slide 82: Latches for memory
Latches can store 1 bit
Other latches exists (e.g., D latch)
Other circuits that store 1 bit (e.g., flip-flops)
Can combine these to make memory (registers, RAM)

## Slide 83: Latches for memory
Latches can store 1 bit
Other latches exists (e.g., D latch)
Other circuits that store 1 bit (e.g., flip-flops)
Can combine these to make memory (registers, RAM)
Why do we have hard drives?

## Slide 84: Latches for memory
When power goes off, we lose what we stored!