## Slide 1: Binary Arithmetic
CS51 – Fall 2026
+
-
>>
01
Computer Systems
Notes: Last time, we saw that there are different numeral systems. We examined binary, decimal, and hexadecimal and learned how to convert a number from one representation to another. Today, we will focus on binary numbers alone and learn how to perform basic arithmetic with them

## Slide 2
Addition
Notes: How do we perform addition in decimal?

## Slide 3
Think
How do you add the numbers
Notes: Let's go back to primary education. How would you add the two decimal numbers 4597 and 334?

## Slide 4
Think
How do you add the numbers
0 1 1 1 carry
4 5 9 710
+ 3 3 410
4 9 3 110
Notes: Presumably, you started with adding the rightmost digits (the least significant digits). If the sum is greater or equal to 10, then carry a 1 and write down the sum%10. Repeat with the next digits to the left, but this time include the carry in the addition.

## Slide 5
Think
How do you add the numbers
Notes: OK you (thankfully!) remember decimal addition. How would we go about adding together these two base 5 numbers?

## Slide 6
Think
How do you add the numbers
1 0 1 carry
2 2 35
+ 4 1 45 1 1 4 25
Notes: Again, we'd start with the least significant digits and add them up. If the sum exceeds our base (i.e.5), we have a carry of 1.

## Slide 7
Think
How do you add the numbers
Can you confirm this is correct by checking the decimal equivalent?
1 0 1 carry
2 2 35
+ 4 1 45 1 1 4 25
Notes: Let's further convince ourselves that this is correct by checking the decimal equivalent

## Slide 8
Think
How do you add the numbers
1 0 1 carry
2 2 35 = 2*25 + 2*5 + 3*1 = 63
+ 4 1 45 = 4*25 + 1*5 + 4*1 = 109 1 1 4 25 = 1* 125 + 1*25 + 4*5 + 2*1 = 172
0 0 1 carry
6 310
+ 1 0 910 1 7 210
Notes: Remember all the work we did from last class meeting? Looks like we got it right

## Slide 9
Think
How do you add the binary numbers
Notes: What if we wanted to add the two binary numbers 1 and 0101?

## Slide 10
Think
How do you add the binary numbers
0 0 1 carry
12
+ 1 0 12 1 1 02
Notes: we'd follow the same process from right to left. if we add two bits equal to 1, then we get back 0 and have a carry of 1.

## Slide 11
Think
How do you add the binary numbers
Can you confirm this is correct by checking the decimal equivalent?
0 0 1 carry
12
+ 1 0 12 1 1 02
Notes: Again, can we confirm that what we did is correct by converting it to its decimal representation we are more comfortable with

## Slide 12
Think
How do you add the binary numbers
Can you confirm this is correct by checking the decimal equivalent?
0 0 1 carry
12 = 110
+ 1 0 12 = 4+1=510 1 1 02 =4+2=610
0 carry
110
+ 510 610
Notes: Indeed, it's 1+5=6.

## Slide 13
Think
How do you add the hexadecimal numbers
0 0 1 1 carry
1 1 F 516
+ 1 4 E16 1 3 4 316
Notes: Indeed, it's 1+5=6.

## Slide 14
Think
How do you add the hexadecimal numbers
Can you confirm this is correct by checking the decimal equivalent?
0 0 1 1 carry
1 1 F 516
+ 1 4 E16 1 3 4 316
Notes: Can you confirm it is correct by calculating the decimal equivalent representations

## Slide 15
Think
How do you add the hexadecimal numbers
Can you confirm this is correct by checking the decimal equivalent?
0 0 1 1 carry
1 1 F 516= 163+162+15x16+5 = 459710
+ 1 4 E16 = 162+4x16+14 = 33410 1 3 4 316 = 163+3x162+4x16+3 = 493110
0 0 1 1 carry
4 5 9 710
+ 3 3 410 4 9 3 110
Notes: Indeed they add up to 4931.

## Slide 16
PRACTICE TIME - Addition
Compute the following sums
Notes: OK Let's see whether we can do addition in binary and hex.

## Slide 17
ANSWER - Addition
Compute the following sums
0 1 1 1 carry 0 0 0
0 1 1 12 9 B 316
+ 0 1 0 12 + 3 816
1 1 0 02 9 E B16
Notes: Dod you get these results?

## Slide 18
Overflow

## Slide 19: Simplified view of a computer
RAM
hard drive
“the computer”
CPU
010010010011010010010111100010001010
Both RAM and the hard drive store a sequence of bits.
Notes: Remember we said a computer at its basis is the CPU communicating with the RAM, that is the memory, where temporary data are stored as long as we have power. More permanent data are stored in the hard drive. Both types of memory store information in sequences of bits.

## Slide 20: Word length
RAM
hard drive
“the computer”
CPU
To simplify hardware, these bits are grouped into fixed length chunks called “words”, e.g., in groups of 4.
0100 1001 0011 0100 1001 0111 1000 1000 1010
Notes: To simplify hardware, we group bits into fixed length chunks called words.

## Slide 21: Computers today
RAM
hard drive
“the computer”
CPU
Most computers today work with 64-bit words.
Notes: Most computers today read words in 64 bits. When I grew up, most had 32-bit words but as our computational needs go up, computer architecture has to adapt.

## Slide 22
Think
What happens if we want to add the binary numbers but only have 4 bits available?
Notes: What if we want to add two binary numbers and we know that the result has to fit in a fixed number of bits, e.g., can you try to add the two binary numbers 1001 and 1101?

## Slide 23
Think
What happens if we want to add the binary numbers but only have 4 bits available?
1 0 0 1 carry
1 0 0 12
+ 1 1 0 12 1 0 1 1 02
Notes: You see that we would need an extra bit!

## Slide 24
Overflow
If we operate on a fixed number of bits, addition can overflow if the result is too big to fit in the available space.
1 0 0 1 carry
1 0 0 12
+ 1 1 0 12 1 0 1 1 02
Notes: This can be a problem and the problem is known as overflow.

## Slide 25
Think
If we operate on a fixed number of bits, addition can overflow if the result is too big to fit in the available space.
How can we detect overflow?
1 0 0 1 carry
1 0 0 12
+ 1 1 0 12 1 0 1 1 02
Notes: How do you think we can detect overflow?

## Slide 26
Think
If we operate on a fixed number of bits, addition can overflow if the result is too big to fit in the available space.
How can we detect overflow?
  If the carry bit for the MSB is 1, then we have overflow
1 0 0 1 carry
1 0 0 12
+ 1 1 0 12 1 0 1 1 02
Notes: We just need to check the carry bit for the most significant (remember, left most) bit. If it's 1, then we know we are in trouble.

## Slide 27
Signed numbers
Notes: Everything we have seen so far has assume we are working with positive numbers only, including 0. Now we will move into signed numbers, that is numbers that can tell us whether they are positive or negative.

## Slide 28: Binary numbers revisited
What is -610 in binary?
Notes: Here's a question for you. Say we have the -6 decimal number. How do we represent it in binary?

## Slide 29: One option: sign/magnitude
fixed bit length (e.g., 4 bits)
sign
0 = positive
1 = negative
magnitude
Notes: Our first option is to work with a representation called sign or magnitude. If we have a fixed number of bits, say 4, we reserve the left most bit for the sign. The convention is that if it's a 0, then the number is positive. If it's 1, it's negative. The remaining 3 bits are known as the magnitude.

## Slide 30: One option: sign/magnitude
fixed bit length (e.g., 4 bits)
sign
0 = positive
1 = negative
magnitude
What is -610 in sign/magnitude?
Notes: So if we go back to -6 from decimal and want to represent it in binary using the sign/magnitude representation, what would that look like?

## Slide 31: One option: sign/magnitude
fixed bit length (e.g., 4 bits)
sign
0 = positive
1 = negative
magnitude
What are the range of values we can support with 4 bits in sign/magnitude representation?
1
1
1
0
Notes: If we had 4 bits available and we use the sign/magnitude representation, what is the range of decimal values we can support?

## Slide 32: One option: sign/magnitude
fixed bit length (e.g., 4 bits)
sign
0 = positive
1 = negative
magnitude
What are the range of values we can support with 4 bits in sign/magnitude representation?
1111 = -7 to 0111 = 7
1
1
1
0
Notes: The largest magnitude is 111 with 3 bits, that is 7. So we can go from -7 to 7

## Slide 33: Think
fixed bit length (e.g., 4 bits)
sign
0 = positive
1 = negative
magnitude
Any problems?
1
1
1
0
Notes: Do you foresee any problems with this representation?

## Slide 34: Think
fixed bit length (e.g., 4 bits)
sign
0 = positive
1 = negative
magnitude
Any problems?
We have two zeros, 0000 and 1000
1
1
1
0
Notes: We end up with two zeros, one for the positive and one for the negative sign.

## Slide 35
Think
Try to add and - using sign/magnitude representation. You can assume you have 8 bits.
Notes: There's also one more problem. Try to add 47 and -47 in binary using sign/magnitude representation.

## Slide 36
Think
Try to add and - using sign/magnitude representation. You can assume you have 8 bits.
00101111
+10101111
011011110 =
Which is nonsensical!
Notes: Instead of 0, we got the nonsensical 222?!

## Slide 37: A better option: two's complement representation
For a number with bits, the MSB represents
unsigned
20
21
22
23
20
21
22
-23
signed
(two's complement)
Notes: We will see another representation that addresses both of these problems. This representation is known as two's complement and the basic idea behind it is that the MSB (meaning the left most bit represents the number -2^(n-1). Every other bit works as usual.

## Slide 38: Think
What numbers do we get?
unsigned
20
21
22
23
signed
(two's complement)
20
21
22
-23
1
0
0
1
1
0
0
1
Notes: With that in mind, what numbers do we get if we have the bits 1001 in unsigned and signed (in two's complement) representation?

## Slide 39: Think
What numbers do we get?
unsigned
20
21
22
23
signed
(two's complement)
20
21
22
-23
1
0
0
1
1
1
9
-7
0
0
Notes: In the case of unsigned, we have 1x2^3+1x2^0=9. But in two's complement that is -2^3+2^0 = -8+1=-7.

## Slide 40: Think
What numbers do we get now?
unsigned
20
21
22
23
signed
(two's complement)
20
21
22
-23
1
1
1
1
1
1
1
1
Notes: What if we read the 4-bit number 1111 in each of the two representations?

## Slide 41: Think
What numbers do we get now?
unsigned
20
21
22
23
signed
(two's complement)
20
21
22
-23
1
1
1
1
1
1
1
1
15
-1
Notes: In the case of unsigned, we have 1x2^3+1x2^2+1x2^1+1x2^0=1. But in two's complement that is -2^3+2^2+2^1+2^0 = -8+4+2+1=-1

## Slide 42: Think
What numbers do we get now?
unsigned
20
21
22
23
signed
(two's complement)
20
21
22
-23
1
1
0
0
1
1
0
0
Notes: OK what about now?

## Slide 43: Think
What numbers do we get now?
unsigned
20
21
22
23
signed
(two's complement)
20
21
22
-23
1
1
0
0
1
1
0
0
12
-4
Notes: Did you get 12 and -4?

## Slide 44: Think
How many numbers can we represent with each representation if we have 4 bits?
unsigned
20
21
22
23
signed
(two's complement)
20
21
22
-23
Notes: If we have 4 bits, how many numbers can we represent in unsigned and how many in signed (with two's complement)

## Slide 45: Think
unsigned
20
21
22
23
signed
(two's complement)
20
21
22
-23
How many numbers can we represent with each representation if we have 4 bits?
  16 numbers: 0000, 0001, …, 1111, regardless of representation
Notes: It's 16 (2^4), regardless of the representation

## Slide 46: Think
unsigned
20
21
22
23
signed
(two's complement)
20
21
22
-23
What is the range of numbers we can represent for each approach with 4 bits?
Notes: What is the range of numbers that each approach can support with 4 bits?

## Slide 47: Think
unsigned
20
21
22
23
signed
(two's complement)
20
21
22
-23
What is the range of numbers we can represent for each approach with 4 bits?
  unsigned: 0, 1, … 15
  signed: -8, -7, …, 7
Notes: For unsigned, since they are all positive it goes 0 to 15. But for signed it's -8 to 7

## Slide 48
binary representation | unsigned | 
0000 | 0 | 
0001 | 1 | 
0010 | ? | 
0011 |  | 
0100 |  | 
0101 |  | 
0110 |  | 
0111 |  | 
1000 |  | 
1001 |  | 
1010 |  | 
1011 |  | 
1100 |  | 
1101 |  | 
1110 |  | 
1111 |  | 
Notes: If 0000 corresponds to 0 in unsigned and 0001 to 1, what does 0010 correspond to?

## Slide 49
binary representation | unsigned | 
0000 | 0 | 
0001 | 1 | 
0010 | 2 | 
0011 |  | 
0100 |  | 
0101 |  | 
0110 |  | 
0111 |  | 
1000 |  | 
1001 |  | 
1010 |  | 
1011 |  | 
1100 |  | 
1101 |  | 
1110 |  | 
1111 |  | 
Notes: 2, right? What about the rest of the column

## Slide 50
binary representation | unsigned | two's complement
0000 | 0 | ?
0001 | 1 | 
0010 | 2 | 
0011 | 3 | 
0100 | 4 | 
0101 | 5 | 
0110 | 6 | 
0111 | 7 | 
1000 | 8 | 
1001 | 9 | 
1010 | 10 | 
1011 | 11 | 
1100 | 12 | 
1101 | 13 | 
1110 | 14 | 
1111 | 15 | 
Notes: Well we just said, it would be 0,…, 15. How about two's complement representation of 0000?

## Slide 51
binary representation | unsigned | two's complement
0000 | 0 | 0
0001 | 1 | 1
0010 | 2 | 2
0011 | 3 | 3
0100 | 4 | 4
0101 | 5 | 5
0110 | 6 | 6
0111 | 7 | 7
1000 | 8 | ?
1001 | 9 | 
1010 | 10 | 
1011 | 11 | 
1100 | 12 | 
1101 | 13 | 
1110 | 14 | 
1111 | 15 | 
Notes: It's of course 0. And the same applies all the way to 0111. How about 1000?

## Slide 52
binary representation | unsigned | two's complement
0000 | 0 | 0
0001 | 1 | 1
0010 | 2 | 2
0011 | 3 | 3
0100 | 4 | 4
0101 | 5 | 5
0110 | 6 | 6
0111 | 7 | 7
1000 | 8 | -8
1001 | 9 | ?
1010 | 10 | 
1011 | 11 | 
1100 | 12 | 
1101 | 13 | 
1110 | 14 | 
1111 | 15 | 
Notes: Did you get -8? How about the rest of the column?

## Slide 53
binary representation | unsigned | two's complement
0000 | 0 | 0
0001 | 1 | 1
0010 | 2 | 2
0011 | 3 | 3
0100 | 4 | 4
0101 | 5 | 5
0110 | 6 | 6
0111 | 7 | 7
1000 | 8 | -8
1001 | 9 | -7
1010 | 10 | -6
1011 | 11 | -5
1100 | 12 | -4
1101 | 13 | -3
1110 | 14 | -2
1111 | 15 | -1
Notes: Did you get this? Do you notice that 1xxxx is always the smallest number we can represent with the number of bits we have available and then the negative numbers keep increasing?

## Slide 54
binary representation | unsigned | two's complement
0000 | 0 | 0
0001 | 1 | 1
0010 | 2 | 2
0011 | 3 | 3
0100 | 4 | 4
0101 | 5 | 5
0110 | 6 | 6
0111 | 7 | 7
1000 | 8 | -8
1001 | 9 | -7
1010 | 10 | -6
1011 | 11 | -5
1100 | 12 | -4
1101 | 13 | -3
1110 | 14 | -2
1111 | 15 | -1
How can you tell if a number is negative?
Notes: Assuming two's complement representation, how can you tell if a number is negative?

## Slide 55
binary representation | unsigned | two's complement
0000 | 0 | 0
0001 | 1 | 1
0010 | 2 | 2
0011 | 3 | 3
0100 | 4 | 4
0101 | 5 | 5
0110 | 6 | 6
0111 | 7 | 7
1000 | 8 | -8
1001 | 9 | -7
1010 | 10 | -6
1011 | 11 | -5
1100 | 12 | -4
1101 | 13 | -3
1110 | 14 | -2
1111 | 15 | -1
How can you tell if a number is negative?
Look at the MSB
Notes: You just look at the most significant bit.

## Slide 56
binary representation | unsigned | two's complement
0000 | 0 | 0
0001 | 1 | 1
0010 | 2 | 2
0011 | 3 | 3
0100 | 4 | 4
0101 | 5 | 5
0110 | 6 | 6
0111 | 7 | 7
1000 | 8 | -8
1001 | 9 | -7
1010 | 10 | -6
1011 | 11 | -5
1100 | 12 | -4
1101 | 13 | -3
1110 | 14 | -2
1111 | 15 | -1
The smallest number is 1 followed by 0s for the rest of the bits
Notes: Here's another cool fact. If you have n bits, the smallest number you can represent will be 1000.000 where 1 is the MSB and 0s go to the rest of n-1 bits!

## Slide 57
binary representation | unsigned | two's complement
0000 | 0 | 0
0001 | 1 | 1
0010 | 2 | 2
0011 | 3 | 3
0100 | 4 | 4
0101 | 5 | 5
0110 | 6 | 6
0111 | 7 | 7
1000 | 8 | -8
1001 | 9 | -7
1010 | 10 | -6
1011 | 11 | -5
1100 | 12 | -4
1101 | 13 | -3
1110 | 14 | -2
1111 | 15 | -1
-1 is always all 1s
Notes: And one more: -1 is going to be all 1s

## Slide 58: A two’s complement trick
1101
0011
flip the bits
0010
-3
add 1
You can also calculate the value of a negative number represented as two's complement as follows:
  Flip all of the bits (0  1 and 1 0)
  Add 1
  The resulting number is the magnitude of the original negative number
Notes: There is a cool trick you can use to calculate the value of a negative number in two's complement. You flip the bits (so 0s turn to 1s and 1s to 0s). You add a 1 the usual way. And the resulting number is the magnitude of the negative number.

## Slide 59: Think
You can also calculate the value of a negative number represented as two's complement as follows:
  Flip all of the bits (0  1 and 1 0)
  Add 1
  The resulting number is the magnitude of the original negative number
Which number is 1110?
1110
Notes: Your turn. Which negative number is 1110?

## Slide 60: Think
You can also calculate the value of a negative number represented as two's complement as follows:
  Flip all of the bits (0  1 and 1 0)
  Add 1
  The resulting number is the magnitude of the original negative number
1110
0010
flip the bits
0001
-2
add 1
Notes: You know that 1110 is going to be negative so follow the trick of flipping its bits, adding 1. You get 0010 which is 2. So then your original number was -2

## Slide 61
00012
01 012
+
?
Addition with 4-bit two's complement numbers
Notes: OK, say we have these two 4-bit two's complement numbers, what's the result of this addition?

## Slide 62
Addition with 4-bit two's complement numbers
00012
01 012
+
01 102
1
0
0
Notes: We add up as before, using the carry bit when needed

## Slide 63
Addition with 4-bit two's complement numbers
0110
0101
+
?
Notes: What about now? Assume that from now on all is binary numbers

## Slide 64
Addition with 4-bit two's complement numbers
0110
0101
+
1011?
0
0
1
Notes: So I got 1011. Is this right? Remember, I added two positive numbers (how do I know this? they have 0 at the MSB) and ended up with a negative?

## Slide 65
Addition with 4-bit two's complement numbers
0110
0101
+
1011?
6
5
-5? (11 unsigned)
Overflow! We cannot represent this number (it’s too large)
0
0
1
Notes: We have overflow as we cannot represent this number. 6+5=11 which is out of the range of -8,..,7 we can represent with 4 bits.

## Slide 66
Addition with 4-bit two's complement numbers
0110
1101
+
?
Notes: What about adding these two two's complement binary numbers?

## Slide 67
Addition with 4-bit two's complement numbers
0110
1 101
+
0011
1
0
0
1
Notes: We get 0011 but also have a carry of 1 floating

## Slide 68
Addition with 4-bit two's complement numbers
0110
1101
+
0011
6
-3
3
ignore the last carry
1
0
0
1
Notes: If we ignore the last carry, we actually see that what we got is correct!

## Slide 69: Think
How do you know that overflow has occurred with two's complement numbers?
Notes: So how do we know that overflow has occurred when adding two two's complement numbers?

## Slide 70: Overflow in two's complement
How do you know that overflow has occurred with two's complement numbers?
  Can only happen when adding two numbers of the same sign
  Add the numbers and discard the last carry bit
  Check the sign of the resulting number: if the resulting differs than the sign of the two numbers added, there is overflow
Notes: Overflow can now only happen if we add two numbers with the same sign (i.e., two positive or two negative numbers). So we will add the numbers as usual and discard the carry bit for the MSB. Since overflow can happen only if two numbers have the same sign, we check the sign of the resulting number (i.e. the MSB) and if it's different than the two numbers we added, then we have overflow. That is, if you have two positive numbers (MSB is 0) and you get a result with MSB 1, you know you are in trouble. Similarly, adding two negative numbers (MSB 1) and getting MSB 0 in the result means overflow.

## Slide 71
Subtraction
Notes: Any idea about how we can perform subtraction in binary?

## Slide 72: Subtraction
Negate the 2nd number (flip the bits and add 1)
Add them!
Notes: The work is actually quite simple. We just have to negate the 2nd number, that is flip its bits from 0 to 1 and 1 to 0 and then 1, and add the first and negated number.

## Slide 73
PRACTICE TIME – Subtracting two’s complements
Calculate using 4-bit two's complement numbers.
Notes: Let's practice by calculating 3-5 in two's complement assuming 4 bits,

## Slide 74
ANSWER – Subtracting two’s complements
Calculate using 4-bit two's complement numbers.
is
Take the two’s complement of -
  Invert
  Add 1:
Add them:
  How do you know ?
    Invert and then 1:
    So
Notes: Did you get this?

## Slide 75
Sign extension in two’s complements
Sign extension: when extending a two’s complement number in more bits, we need to copy the sign bit.
For example, if we have 4 bits the numbers and are written in binary as and .
If we want to sign extend them to 8 bits, we would need to copy the sign bit 4 times to and , respectively.
Notes: When we want to extend a two's complement number to more bits, we are going to copy the sign bit (0 for positive, 1 for negative). E.g., if we have 4 bits and the binary representations for -3 and 3 (1101 and 0011, respectively), we would pad them with 1s and 0s, respectively.

## Slide 76
Why number representation errors matter
1. Ariane 5 Rocket Explosion (1996)
  Flight software converted a 64-bit floating point value into a 16-bit signed integer.
  The value was too large which caused an overflow which led to system failure.
  The rocket self-destructed 40 seconds after launch leading to a loss of $370 million.
2. Classic Video Games
  Many classic video games stored scores/lives in 8-bit signed integers (−128, … ,127)
  If score exceeded 127 it wrapped to negative values.
  Players suddenly saw “negative lives” or game crashes.
Notes: Why do representations of numbers matter? Here are two examples when things can go wrong. Ariane 5 rocket launched in 1996 and the flight software converted a 64-bit floating point number into a 16-bit integer. The value was too large, causing an overflow and system failure. The rocket self-destructed less than a minute pass its launch, taking with it more than $370 million. A less catastrophic example would be to look at classic video games, e.g., some used 8 bits to store scores or lives. If a score exceeded the max number, ie. 127, it wrapped to negative values and played suddenly saw negative lives or game crashes.

## Slide 77
Shifting
Notes: We will move next to shifting, a type of operation we can do on numbers.

## Slide 78: Shifting: variable length numbers
Shifting shifts the binary representation of the number right or left
37 >> 2
number to be shifted
right shift
number of positions to shift
?
Notes: The next topic we will cover is that of shifting. Shifting shifts the binary representation of a number either right or left. For example, here I am saying I want to shift 37 2 positions to the right (note the direction of ?>>)

## Slide 79: Shifting: variable length numbers
37 >> 2
37
number in binary
100101
shift right two positions
(discard bits shifting off)
100101
9
decimal form
Shifting shifts the binary representation of the number right or left
Notes: So how do we shift 37 2 positions to the right? We convert it to its binary representation (assume unsigned numbers). Shift right two positions by discarding the 2 lowest bits. Convert 1001 to decimal and you get 9. So 37>>2=9!

## Slide 80: Think
37 >> 3
?
Shifting shifts the binary representation of the number right or left
Notes: What if I asked you to shift 37 3 positions to the right?

## Slide 81: Think
37 >> 3
37
number in binary
100101
shift right three positions
(discard bits shifting off)
100101
4
decimal form
Shifting shifts the binary representation of the number right or left
Notes: You would repeat the same process discarding the last 3 bits and end up with 100 which is equal to 4.

## Slide 82: Shifting 8-bit numbers
37 >> 2
37
number in binary
00100101
What is 37 as an 8-bit binary number?
pad with 0s
Shifting shifts the binary representation of the number right or left
Notes: What if instead of a variable number of bits, we have a fixed one, say 8. We will use sign extension to pad with 0s the front of the binary number.

## Slide 83: Shifting 8-bit numbers
37 >> 2
37
number in binary
00100101
shift right two positions
(discard away bits shifting off and pad)
0000100101
9
decimal form
Shifting shifts the binary representation of the number right or left
Notes: As we shift two bits to the right, we will continue padding the front with 0s since we have a fixed length representation.

## Slide 84: Think
15 << 2
?
Shifting shifts the binary representation of the number right or left
Notes: What do you think happens if we wanted to shift 2 positions to the left?

## Slide 85: Think
15 << 2
15
number in binary
?
Shifting shifts the binary representation of the number right or left
Notes: Assuming an 8-bit representation, what is 15 in binary?

## Slide 86: Shifting 8-bit numbers
15 << 2
15
number in binary
00001111
Shifting shifts the binary representation of the number right or left
Notes: 00001111 (we need the four 0s as padding in the front)

## Slide 87: Think
15 << 2
15
number in binary
00001111
?
shift left two positions
(discard bits shifting off)
Shifting shifts the binary representation of the number right or left
Notes: If we were to shift left two positions and discard bits we shift off, what would we get?

## Slide 88: Shifting 8-bit numbers
15 << 2
15
number in binary
00001111
00001111??
shift left two positions
(discard bits shifting off)
Shifting shifts the binary representation of the number right or left
Notes: We discard the first two bits but what happens at the end so that we end up with 8 bits?

## Slide 89: Shifting 8-bit numbers
15 << 2
15
number in binary
00001111
0000111100
shift left two positions
(discard bits shifting off)
Shifting shifts the binary representation of the number right or left
Notes: Just pad it with 0s! We always do so independently of sign

## Slide 90: Shifting 8-bit numbers
15 << 2
15
number in binary
00001111
0000111100
60
decimal form
shift left two positions
(discard bits shifting off)
Shifting shifts the binary representation of the number right or left
Notes: And then as usual, convert to its decimal form which gives you 60.

## Slide 91: Think
What does left shifting by one position do mathematically?
20
21
22
23
A
B
C
0
Notes: Let's think, what does left shifting by 1 position do mathematically?

## Slide 92: Shifting mathematically: unsigned
What does left shifting by one position do mathematically?
20
21
22
23
A
B
C
0
20
21
22
23
B
C
0
A
Notes: We had four bits (assume 0 at the MSB) and shifting discarded that 0 and padded 0 at the end. Try to calculate the decimal result

## Slide 93: Shifting mathematically: unsigned
What does left shifting by one position do mathematically?
20
21
22
23
A
B
C
0
20
21
22
23
B
C
0
A
Notes: Is this what you got?

## Slide 94: Shifting mathematically: unsigned
What does left shifting by one position do mathematically?
20
21
22
23
A
B
C
0
20
21
22
23
B
C
0
A
Doubles the number!
Notes: Do you see that the bottom is twice as big as the top?

## Slide 95: Think
What does left shifting by n positions do mathematically?
Notes: So if we have left shifting by n positions, what do we end up with?

## Slide 96: Think
What does left shifting by n positions do mathematically?
Multiply by 2n (doubles it n times)
Notes: We double n times, or multiply by 2^n

## Slide 97: Shifting mathematically: unsigned
What does right shifting by one position do mathematically?
20
21
22
23
A
B
C
0
Notes: Lets' apply the same idea to right shifting

## Slide 98: Shifting mathematically: unsigned
20
21
22
23
A
B
C
0
20
21
22
23
0
A
B
0
What does right shifting by one position do mathematically?
Notes: If we had four bits (assuming 0 for MSB), right shifting by 1 position would discard C and pad 0 in the front.

## Slide 99: Shifting mathematically: unsigned
20
21
22
23
A
B
C
0
20
21
22
23
0
A
B
0
What does right shifting by one position do mathematically?
Notes: Try to convert this to decimal

## Slide 100: Shifting mathematically: unsigned
20
21
22
23
A
B
C
0
20
21
22
23
0
A
B
0
Integer divide by 2 (// in Python)
What does right shifting by one position do mathematically?
Notes: That's like doing integer division by 2 which by rounding down to infinity. Remember, integer division is // in Python

## Slide 101: Think
What does right shifting by n positions do mathematically?
Notes: So what does right shifting an unsigned number by n positions do?

## Slide 102: Think
What does right shifting by n positions do mathematically?
Integer division by 2n (halves it n times)
Notes: It halves it n times or it performs integer division by 2^n

## Slide 103: Think
Shifting shifts the binary representation of the number right or left
-4 >> 1
What is -4 as a 4-bit binary number?
Notes: Now what if we don't have only unsigned number. Say we work with 4-bit numbers and we want to shift -4 one position to the right.

## Slide 104: Shifting 4-bit numbers
-4 >> 1
-4
number in binary
1100
Shifting shifts the binary representation of the number right or left
Notes: It's 1100 (assuming two's complement)

## Slide 105: Think
-4 >> 1
-4
number in binary
1100
How do we fill in the leftmost bit?
?1100
shift right one position
(discard bits shifting off)
Shifting shifts the binary representation of the number right or left
Notes: If we are to shift one position to the right, how do we fill in the leftmost bit to end up with 4 bits?

## Slide 106: Shifting 4-bit numbers
-4
number in binary
1100
?1100
Two types of right shifts:
  logical shift: always shift in 0s
  arithmetic shift: shift in the same as the high-order bit
shift right one position
(discard bits shifting off)
Notes: We have two options. One is called logical shift and it always adds 0s. In arithmetic shift, in contrast, we pad with the same bit as the MSB or high-order bit.

## Slide 107: Think
-4
number in binary
1100
?1100
Two types of right shifts:
  logical shift: always shift in 0s
  arithmetic shift: shift in the same as the high-order bit
shift right one position
(discard bits shifting off)
Notes: What if we followed arithmetic shift next?

## Slide 108: Think
-4
number in binary
1100
11100
shift right one position
(discard bits shifting off)
Two types of right shifts:
  logical shift: always shift in 0s
  arithmetic shift: shift in the same as the high-order bit
Notes: We would pad it with 1 as this was the MSB.

## Slide 109: Shifting 4-bit numbers
-4
number in binary
1100
11100
-4 >> 1
decimal form
?
shift right one position
(discard bits shifting off)
Two types of right shifts:
  logical shift: always shift in 0s
  arithmetic shift: shift in the same as the high-order bit
Notes: What is the decimal form?

## Slide 110: Shifting 4-bit numbers
-4
number in binary
1100
11100
-4 >> 1
decimal form
-2
shift right one position
(discard bits shifting off)
Two types of right shifts:
  logical shift: always shift in 0s
  arithmetic shift: shift in the same as the high-order bit
Notes: It's -2

## Slide 111: Think
Shifting shifts the binary representation of the number right or left
-4 >> 2
?
Notes: What if we wan to shift -4 2 positions to the right and we have a 4-bit representation?

## Slide 112: Think
-4
number in binary
1100
111100
-4 >> 2
decimal form
-1
shift right two positions
(discard bits shifting off)
Two types of right shifts:
  logical shift: always shift in 0s
  arithmetic shift: shift in the same as the high-order bit
Notes: Assuming again arithmetic shift, we would discard the last two 0s and add two 1s in the front which results in the number -1.

## Slide 113: Think
What does right arithmetic shifting by n positions do mathematically for signed numbers?
Notes: So what does right arithmetic shifting by n positions do mathematically when we are working with signed numbers?

## Slide 114: Arithmetic shifting mathematically
Integer division by 2n (halve n times)
Same thing!!
What does right arithmetic shifting by n positions do mathematically for signed numbers?
Notes: Same thing with unsigned number, it divides them by 2^n.

## Slide 115: Think
-4
number in binary
1100
?1100
shift right one position
(discard bits shifting off)
Two types of right shifts:
  logical shift: always shift in 0s
  arithmetic shift: shift in the same as the high-order bit
Notes: OK what if we did logical shifting?

## Slide 116: Shifting 4-bit numbers
-4
number in binary
1100
01100
shift right one position
(discard bits shifting off)
Two types of right shifts:
  logical shift: always shift in 0s
  arithmetic shift: shift in the same as the high-order bit
Notes: We'd just pad with 0

## Slide 117: Think
-4
number in binary
1100
01100
-4 >>> 1
decimal form
?
shift right one position
(discard bits shifting off)
Two types of right shifts:
  logical shift: always shift in 0s
  arithmetic shift: shift in the same as the high-order bit
Notes: Which would result to?

## Slide 118: Shifting 4-bit numbers
-4
number in binary
1100
0110
-4 >>> 1
decimal form
6
shift right one position
(discard bits shifting off)
Two types of right shifts:
  logical shift: always shift in 0s
  arithmetic shift: shift in the same as the high-order bit
Notes: 6! So with logical shifts it doesn't seem like we are halving.

## Slide 119: Think
Are there two types of left shifts?
  logical shift: always shift in 0s
  arithmetic shift: ?
-3 << 1
-3 <<< 1
?
?
arithmetic
logical
Notes: So if we have logical and arithmetic right shift, do we have the same for left?

## Slide 120: Left shifts
-3 << 1
-3 <<< 1
1101
1101
arithmetic
logical
1101?
11010
(double the number)
Are there two types of left shifts?
  logical shift: always shift in 0s
  arithmetic shift: ?
Notes: How can we double the number if we do an arithmetic left shift?

## Slide 121: Left shifts
-3 << 1
-3 <<< 1
1101
1101
arithmetic
logical
11010
11010
(double the number)
Only one type of left shift
Are there two types of left shifts?
  logical shift: always shift in 0s
  arithmetic shift: ?
Notes: We would need to add a 0. Which means that we only have one type of left shift

## Slide 122: Shifting summarized
Arithmetic shift:
  Right shift n
    shift n bits to the right
    discard right n bits
    left n bits match high-order bits of original number
    Effect: Integer division by 2n (halve n times)
  Left shift
    shift n bits to the left
    discard left n bits
    right n bits are 0s
    Effect: multiply by 2n (double n times)
Logical shift right:
  left n bits are 0s (no mathematical guarantees for negative numbers)
Notes: So if we were to summarize shifting, arithmetic shifting is truly what happens both for left and right but logical shifting can only happen for right.

## Slide 123
PRACTICE TIME - Arithmetic right shift
Let’s assume we work with 4 bits and we want to shift the binary representation of the number by 2 bits to the right, that is -6>>2.
Using two’s complement representation show what the effect of the shift will be on the binary representation of .
Notes: Your turn to apply arithmetic right shift by 2 bits to the binary -6 using two's complement and assuming 4 bits.

## Slide 124
ANSWER - Arithmetic right shift
We start by converting the decimal number to its binary representation in two's complement:
Remember, since we have arithmetic right shift, we shift two positions to the right and copy 2 times the MSB (1) to the left. This results in:
  , that is .
If we convert back to decimal, we get
We said that arithmetic right shift by k divides the original number by rounding down to minus infinity.
  Indeed which is rounded down to -2.
Notes: We will start by converting the decimal number to its binary representation in two's complement, i.e. 1010. We shift two to the right, i.e. 10 and pad it with two MSB signs, i.e. 1110. That would be the number -2. Let's check that the division by 4 holds. Yes, which is rounded down to -2.
We will start by converting the decimal number to its binary representation in two's complement, i.e. 1010. We shift two to the right, i.e. 10 and pad it with two MSB signs, i.e. 1110. That would be the number -2. Let's check that the division by 4 holds. Yes, "−6/4 =−1.5 "which is rounded down to -2.

## Slide 125
PRACTICE TIME – Left shift
What happens when we shift -10<<3 assuming we have 8 bits?
Notes: Your turn, assume you have 8 bits, and you try to shift -10 by 3 bits to the left.

## Slide 126
ANSWER – Left shift
What happens when we shift -10<<3 assuming we have 8 bits?
We start by converting the decimal number to its binary representation using two’s complement and sign extension:
  -
Remember, since we have left shift, we shift three positions to the left and add three 0s to the right. This results in:
  , that is .
If we convert back to decimal, we get
  Invert to and then adding 1 results to so overall
We said that left shift by k multiplies the original number by .
  Indeed .
Notes: Start by converting to the two's complement representation in binary I,e, 10110. Pad it with 1s to reach 8 bits. 11110110.
Shift three to the left and add three 0s to the right. which is equal to -80 and it checks out in terms of multiplying -10 by 2^3!
Start by converting to the two's complement representation in binary I,e, 10110. Pad it with 1s to reach 8 bits. 11110110.
Shift three to the left and add three 0s to the right. 10110000 which is equal to -80 and it checks out in terms of multiplying -10 by 2^3!

## Slide 127
Shifting in Python
Python supports left and arithmetic right shifting. It denotes them as << and >>, respectively.
Other programming languages, like Java, support both arithmetic and logical right shift and use the >> and >>> operators to distinguish them.
Notes: Python supports left shifting and right arithmetic shifting using the << and >> operators. Other languages, like Java, also support logical right shifting making a distinction by using >>>.

## Slide 128
Practice Problems
Notes: Time to practice at home

## Slide 129: Practice Problems – Problem 1
  Convert the following decimal numbers to their unsigned binary representation and add them:
    How many bits do you need to not have overflow?
Assume 6-bit signed numbers in two’s complement representation. Add them and state whether overflow occurs:
  Convert these three numbers to decimal to double check your work.
Add the hex numbers 0xA7+0x5C
  Convert these three numbers to decimal to double check your work.

## Slide 130: Practice Problems – Answer 1
  Convert the following decimal numbers to their unsigned binary representation and add them:
    How many bits do you need to not have overflow? 7
Assume 6-bit signed numbers in two’s complement representation. Add them and state whether overflow occurs:
  . No overflow as we drop the left most bit (1).
  Convert these three numbers to decimal to double check your work. -18+21=-3
Add the hex numbers
  Convert these three numbers to decimal to double check your work.

## Slide 131: Practice Problems – Problem 2
  What will the results of the following operations be in binary and decimal assuming 8 bits?

## Slide 132: Practice Problems – Answer 2
  What will the results of the following operations be in binary and decimal assuming 8 bits?