## Slide 1: Combinational Circuits
CS51 – Fall 2026
Computer Systems
Notes: It's time to move one level higher in our hierarchy. Now that we know about bits and how we encode information, we can see how this information is stored and transmitted.

## Slide 2: Bits, components, gates, and circuits
Computers store and transmit information in the form of bits. This is accomplished by combining electronic components, such as transistors, in increasingly complex ways.
For example, logic operations are evaluated by logic gates or simply gates built out of special types of transistors.
In turn, logic gates can be combined to build more complex circuits.
Today’s lecture will be all about different types of combinational circuits: their output depends on the present inputs and there is no notion of memory of past inputs.
To draw our circuits, we will use the software Logisim-Evolution.
Notes: Computers store and transmit information in the form of bits. This is accomplished by combining electronic components, such as transistors, in increasingly complex ways. For example, logic operations are evaluated by logic gates or simply gates built out of special types of transistors. In turn, logic gates can be combined to build more complex circuits. Today’s lecture will be all about different types of combinational circuits: their output depends on the present inputs and there is no notion of memory of past inputs. To draw our circuits, we will use the software Logisim-Evolution.

## Slide 3: Logic Circuits
Notes: Let's start with the simplest circuits, the logic circuits.

## Slide 4: Gates and Boolean logic
NOT (¬)
AND (∧)
OR (∨)
XOR ()
NAND ()
NOR ()
X | Y | ¬ X | X ∧ Y | X ∨ Y | X Y | X Y | X Y
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
X | Y | ¬ X | X ∧ Y | X ∨ Y |  |  | 
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
Notes: These support the operations we have seen through Boolean Algebra. Logical NOT, AND, OR, and XOR, we saw already. What is new is NAND (the negation of AND) and NOR (the negation of NOR). At this stage, I want you to become familiar with the symbols for the logic gates. Remember, inversion (negation) is symbolized with a circle; you can see it at the end of NOT, NAND, and NOR. AND looks like a D shape; you can see it at the AND and NAND gate. OR is like an arrow/ you can see it at OR and NOR. Exclusive OR is like OR but with a smile.

## Slide 5: PRACTICE TIME – Using gates
What is the output of the following circuit for the provided input?
NOT (¬)
AND (∧)
OR (∨)
XOR ()
NAND ()
NOR ()
1
0
0
?
X | Y | ¬ X | X ∧ Y | X ∨ Y | X Y | X Y | X Y
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
X | Y | ¬ X | X ∧ Y | X ∨ Y |  |  | 
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
Notes: Let's imagine we have built a small circuit with three inputs, two of which go to a NOR gate whose output is combined with the third input in a AND gate. If the inputs are 1, 0, and 0 respectively, what will the AND gate give us output? As an intermediate step, see what the output of NOR would be for an input of 1 and 0.

## Slide 6: ANSWER – Using gates
What is the output of the following circuit for the provided input?
NOT (¬)
AND (∧)
OR (∨)
XOR ()
NAND ()
NOR ()
0
Light green is 1 and dark green is 0
X | Y | ¬ X | X ∧ Y | X ∨ Y | X Y | X Y | X Y
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
X | Y | ¬ X | X ∧ Y | X ∨ Y |  |  | 
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
Notes: NOR would produce 0. 0 AND 0 gives 0.

## Slide 7: PRACTICE TIME – Using gates
What is the output of the following circuit for the provided input?
NOT (¬)
AND (∧)
OR (∨)
XOR ()
NAND ()
NOR ()
1
1
1
?
X | Y | ¬ X | X ∧ Y | X ∨ Y | X Y | X Y | X Y
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
X | Y | ¬ X | X ∧ Y | X ∨ Y |  |  | 
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
Notes: What if all three inputs are 1?

## Slide 8: ANSWER – Using gates
What is the output of the following circuit for the provided input?
NOT (¬)
AND (∧)
OR (∨)
XOR ()
NAND ()
NOR ()
0
Light green is 1 and dark green is 0
X | Y | ¬ X | X ∧ Y | X ∨ Y | X Y | X Y | X Y
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
X | Y | ¬ X | X ∧ Y | X ∨ Y |  |  | 
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
Notes: The output of NOR is 0 combined as 0 AND 1 gives 0.

## Slide 9: PRACTICE TIME – Using gates
What inputs should we pass to get 1 as output?
NOT (¬)
AND (∧)
OR (∨)
XOR ()
NAND ()
NOR ()
1
?
?
?
1
?
X | Y | ¬ X | X ∧ Y | X ∨ Y | X Y | X Y | X Y
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
X | Y | ¬ X | X ∧ Y | X ∨ Y |  |  | 
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
Notes: Let's try to reverse engineering this circuit. What inputs should we pass to get 1 as output?

## Slide 10: ANSWER – Using gates
What is the output of the following circuit for the provided input?
NOT (¬)
AND (∧)
OR (∨)
XOR ()
NAND ()
NOR ()
Χ | Υ | Ζ | OUT
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0
1
Light green is 1 and dark green is 0
X | Y | ¬ X | X ∧ Y | X ∨ Y | X Y | X Y | X Y
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
X | Y | ¬ X | X ∧ Y | X ∨ Y |  |  | 
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
Notes: We know that AND will only produce 1 if it's given two inputs of 1. So the third input has to be 1. For NOR to produce 1, it needs a 0 and 0.

## Slide 11: PRACTICE TIME – Using gates
Can you build a circuit that reproduces the following inputs/outputs?
NOT (¬)
AND (∧)
OR (∨)
XOR ()
NAND ()
NOR ()
X | Y | Z | OUT
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
X | Y | ¬ X | X ∧ Y | X ∨ Y | X Y | X Y | X Y
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
X | Y | ¬ X | X ∧ Y | X ∨ Y |  |  | 
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
Notes: Here's another problem. If the output is always 0, unless the input is three 0s, what circuit would produce this result?

## Slide 12: ANSWER – Using gates
Can you build a circuit that reproduces the following inputs/outputs?
NOT (¬)
AND (∧)
OR (∨)
XOR ()
NAND ()
NOR ()
X | Y | Z | OUT
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Light green is 1 and dark green is 0
X | Y | ¬ X | X ∧ Y | X ∨ Y | X Y | X Y | X Y
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
X | Y | ¬ X | X ∧ Y | X ∨ Y |  |  | 
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
Notes: Two OR gates would give us this result. Only 0,0,0 would produce 0.

## Slide 13: PRACTICE TIME – Using gates
Can you build a circuit that reproduces the following inputs/outputs?
NOT (¬)
AND (∧)
OR (∨)
XOR ()
NAND ()
NOR ()
X | Y | Z | output
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
X | Y | ¬ X | X ∧ Y | X ∨ Y | X Y | X Y | X Y
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
X | Y | ¬ X | X ∧ Y | X ∨ Y |  |  | 
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
Notes: But how do we generalize this process? Let's put a hold here for a moment.

## Slide 14: Minterm expansion
We will use the following theorem we saw in the Boolean Algebra lecture:
Theorem (Boole, 1847): Any Boolean function can be represented as a disjunction of conjunctions (one OR of a bunch of ANDs) of its arguments and their negation (NOT). This is also known as disjunctive normal form (DNF) or a sum of products/minterms.
How to find the disjunctive normal form of a function (minterm expansion):
  Using truth tables, we isolate the rows where the function evaluates to TRUE/1. Each row contributes to the OR an AND statement of the arguments (if TRUE/1) or their negation (if FALSE/0).
Notes: Remember the theorem we saw last week that any Boolean function can be represented as a DNF. We went about it by isolating the rows that had as output 1 and combine with OR statements the corresponding minterms (Boolean expressions of literals that appear as is or negations and are connected with AND). This technique is known as minterm expansion.

## Slide 15: Minterm expansion for building circuits
Using minterm expansion, we are able to build any circuit as an OR gate of AND gates of inputs and their negation (gate NOT) based on a disjunctive normal form.
Such circuits will always have a depth of 3 which is significant because any signal has to pass through at most three gates to reach the output. This is quite fast!
On the other hand, the minterm expansion produces circuits with lots of gates, which affects the total power consumption and the reliability of the circuit.
  Assignment 2 introduced Karnaugh maps that allow us to simplify Boolean functions and thus circuits, too!
Notes: We will use minterm expansion to build any circuit as an OR gate of AND gates of inputs and negation (which we achieve using NOT gates) based on a DNF. Such circuits will always have a depth of 3 which is great because it means that any signal must only pass at most three gates which is very quick. On the other hand, even if it's a shallow circuit, it still might have a lot of gates. We could go about it using K-maps which we learned about in assignment 2 to make our circuits even smaller!

## Slide 16: PRACTICE TIME – Using gates
What is a DNF for this function?
NOT (¬)
AND (∧)
OR (∨)
XOR ()
NAND ()
NOR ()
in1 | in2 | in3 | output
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
Notes: OK let's go back to our question and start by building a DNF.

## Slide 17: ANSWER – Using Gates
Can you build a circuit that reproduces the following inputs/outputs?
NOT (¬)
AND (∧)
OR (∨)
XOR ()
NAND ()
NOR ()
in1 | in2 | in3 | output
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
(¬in1 ∧¬in2 ∧ ¬in3) ∨ (in1 ∧ ¬in2 ∧ ¬in3) ∨
(in1 ∧ in2 ∧¬in3)
Notes: You should have gotten this.

## Slide 18: ANSWER – Using Gates
Can you build a circuit that reproduces the following inputs/outputs?
NOT (¬)
AND (∧)
OR (∨)
XOR ()
NAND ()
NOR ()
in1 | in2 | in3 | output
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
(¬in1 ∧¬in2 ∧ ¬in3) ∨ (in1 ∧ ¬in2 ∧ ¬in3) ∨
(in1 ∧ in2 ∧¬in3)
Light green is 1 and dark green is 0
Notes: We will use it to build now the following circuit. Three inputs, in1, in2, in3, will feed to three AND gates which will feed to one OR gate. Note that each AND gate corresponds to a minterm so we need to pass the right literals to them. For example, the top AND gate will need to be given the negation of in1, the negation of in2, and the negation of in3. And so on.

## Slide 19: PRACTICE TIME – Using Gates
Can you build a K-map for this table?
NOT (¬)
AND (∧)
OR (∨)
XOR ()
NAND ()
NOR ()
in1 | in2 | in3 | output
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
Notes: What if we use what we learned in assignment 2, can you build a K-map for this truth table?

## Slide 20: ANSWER – Using Gates
Can you build a K-map for this table?
NOT (¬)
AND (∧)
OR (∨)
XOR ()
NAND ()
NOR ()
in1 | in2 | in3 | output
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
(in1 ∧ ¬in3) ∨ (¬in2 ∧ ¬in3)
in1
in2 in3
Notes: You should have ended up with this simple expression.

## Slide 21: PRACTICE TIME – Using Gates
Can you build a circuit using the Boolean expression you derived from the K-map?
NOT (¬)
AND (∧)
OR (∨)
XOR ()
NAND ()
NOR ()
in1 | in2 | in3 | output
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
(in1 ∧ ¬in3) ∨ (¬in2 ∧ ¬in3)
in1
in2 in3
Notes: OK now try to build a circuit using the K-map you built.

## Slide 22: ANSWER – Using Gates
Can you build a circuit using the Boolean expression you derived from the K-map?
NOT (¬)
AND (∧)
OR (∨)
XOR ()
NAND ()
NOR ()
in1 | in2 | in3 | output
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
Notes: Even simpler, right?

## Slide 23: Arithmetic Circuits
Notes: Time to build some more interesting circuits.

## Slide 24: Quick recap
0 1 0 1 0
0 1 1 1 1
+
Notes: Do you remember how to add two binary numbers?

## Slide 25: Quick recap
0 1 0 1 0
0 1 1 1 1
0
1
1
1
+
0
1 1 0 0 1
Notes: At the top, you can see the carry bit.

## Slide 26: Think
0 1 0 1 0
0 1 1 1 1
0
1
1
1
+
0
1 1 0 0 1
in1
in2
sum
carry-out
How can we build a circuit that given input bits in1 and in2 produces carry-out and sum bits?
Notes: If we focus on the last column of this addition we see that what we are doing is adding two bits, let's call them in1 and in2, and they give us back two bits: a carry-out and sum.

## Slide 27: Think
We want to design a circuit that given two input bits, in1 and in2, it will produce the sum and carry-out bits.
Can you fill in the missing values for carry-out and sum?
Inputs |  | Outputs | 
in1 | in2 | carry-out | sum
0 | 0 | ? | ?
0 | 1 | ? | ?
1 | 0 | ? | ?
1 | 1 | ? | ?
Notes: Can you fill in the missing values in the table?

## Slide 28: Revisiting addition
So far, our circuits have been performing logical operations. Now we will see how to build circuits that perform arithmetic operations
We want to design a circuit that given two input bits, in1 and in2, it will produce the sum and carry-out bits shown below, that is it will add two bits.
We can think of the circuit for each output independently.
Inputs |  | Outputs | 
in1 | in2 | carry-out | sum
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
Notes: So far, our circuits have been performing logical operations. Now we will see how to build circuits that perform arithmetic operations. We want to design a circuit that given two inputs, in1 and in2, it will produce the sum and carry-out bits shown below. We can think of the circuit for each output independently.

## Slide 29: PRACTICE TIME – Carry out
Given input bits in1 and in2, what logical expression can we build to return the carry-out?
Inputs |  | Outputs | 
in1 | in2 | carry-out | sum
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
X | Y | ¬ X | X ∧ Y | X ∨ Y | X Y | X Y | X Y
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
X | Y | ¬ X | X ∧ Y | X ∨ Y |  |  | 
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
Notes: If someone gave you this truth table on the right and asked you to design a circuit or a Boolean expression that given in1 and in2 gives you output carry out, what would you do?

## Slide 30: ANSWER – Carry out
Given input bits in1 and in2, what logical expression can we build to return the carry-out?
  Carry-out is calculated as in1 ∧ in2.
X | Y | ¬ X | X ∧ Y | X ∨ Y | X Y | X Y | X Y
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
X | Y | ¬ X | X ∧ Y | X ∨ Y |  |  | 
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
Inputs |  | Outputs | 
in1 | in2 | carry-out | sum
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
Notes: You can combine them with the logical AND operator

## Slide 31: PRACTICE TIME - Sum
Given input bits in1 and in2, what logical expression can we build to return the carry-out?
  Carry-out is calculated as in1 ∧ in2.
How about the sum?
Inputs |  | Outputs | 
in1 | in2 | carry-out | sum
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
X | Y | ¬ X | X ∧ Y | X ∨ Y | X Y | X Y | X Y
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
X | Y | ¬ X | X ∧ Y | X ∨ Y |  |  | 
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
Notes: How about the sum?

## Slide 32: ANSWER – Sum
Given input bits in1 and in2, what logical expression can we build to return the carry-out?
  Carry-out is calculated as in1 ∧ in2.
How about the sum?
  Sum is calculated as in1 ⊕ in2.
X | Y | ¬ X | X ∧ Y | X ∨ Y | X Y | X Y | X Y
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
X | Y | ¬ X | X ∧ Y | X ∨ Y |  |  | 
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
Inputs |  | Outputs | 
in1 | in2 | carry-out | sum
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
Notes: This would be in1 XOR in2

## Slide 33: Half adder - circuit to add two bits
A half adder is a circuit that computes the sum and carry of adding two bits, A and B, together.
  Carry-out is calculated as in1 ∧ in2 and sum is calculated as in1 ⊕ in2.
Inputs |  | Outputs | 
in1 | in2 | carry-out | sum
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
Notes: Putting these two parts together, we can design a circuit called half adder whose job is to add two bits, A and B, together and produce the carry-out and sum as we saw.

## Slide 34: Abstracting the half adder component
Ignoring implementation details, we can treat the half-adder as a reusable component
in1
in2
sum
carry-out
Notes: We will next do something that is very common in Computer Science. We will ignore the details and abstract away from the implementation of the half-adder, treating it as a reusable component. The only thing we care at this point is that our component receives two input bits, in1 and in2, and gives us back two things: the carry-out bit and the sum bit.

## Slide 35: Think
The half-adder adds two bits together and returns a carry-out and sum bit. How can we build a circuit that adds two bits and a carry-in to produce a sum and carry-out?
in1
in2
sum
carry-out
0 1 0 1 0
0 1 1 1 1
1 1 0 0 1
0
1
1
1
+
?
carry-in
in1
in2
sum
carry-out
0
Notes: The half-adder adds two bits together which only corresponds to adding the two least significant bits together. How can we build a circuit that adds two bits and a carry-in to produce a sum and carry-out, that is it corresponds to any other column in our addition?

## Slide 36: Full adder - circuit to add two bits and a carry-in
in1
in2
sum
carry-out
carry-in
0 1 0 1 0
0 1 1 1 1
1 1 0 0 1
0
1
1
1
+
carry-in
in1
in2
sum
carry-out
0
Notes: If we were to think abstractly, we realize that we want to build a component that does a full addition by taking three inputs, in1, in2, and carry-in, and giving us back two ouputs, a carry-out and a sum bit.

## Slide 37: Revisiting addition
in1
in2
sum
carry-out
carry-in
01010
01 11 1
in1
in2
sum
carry-out
in1
in2
carry-out
carry-in
sum
in1
in2
carry-out
carry-in
sum
0
1
1
1
0
1
1
1
+
0
1
1
1
1
0
0
1
1
0
0
1
1
1
1
1
0
in1
in2
sum
carry-out
carry-in
0
0
0
0
1
Notes: So we could stitch together our half-adder for the last column with four more full adders, each being responsible with propagating the right carry-out to the column to the left.

## Slide 38: Think
Inputs |  |  | Outputs | 
in1 | in2 | carry-in | sum | carry-out
0 | 0 | 0 | ? | ?
0 | 0 | 1 | ? | ?
0 | 1 | 0 | ? | ?
0 | 1 | 1 | ? | ?
1 | 0 | 0 | ? | ?
1 | 0 | 1 | ? | ?
1 | 1 | 0 | ? | ?
1 | 1 | 1 | ? | ?
Notes: If a full adder is a component that adds two bits and a carry-in together, what are the outputs sum and carry-out for each row of this truth table?

## Slide 39: Full adder - circuit to add two bits and a carry-in
Inputs |  |  | Outputs | 
in1 | in2 | carry-in | sum | carry-out
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Notes: If a full adder is a component that adds two bits and a carry-in together, what are the outputs sum and carry-out for each row of this truth table?

## Slide 40: Implementing a full adder
half-adder
half-adder
Inputs |  |  | Outputs | 
in1 | in2 | carry-in | sum | carry-out
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
The sum is calculated as (in1 ⊕ in2) ⊕ carry-in.
The carry-out is calculated as (in1 ∧ in2) ∨ ((in1 ⊕ in2) ∧ carry-in).
Notes: I am not going to ask you to implement a full adder as it's slightly more complicated. The sum is calculated as before in1 XOR in2 but then we XOR with the carry-in. The carry out is either in1 AND in2 or in1 XOR in2 AND carry-in. Take a moment to confirm it works as intended.

## Slide 41: Think
A full adder calculates the sum of a single column of the addition operation.
If we want to add two n-bit numbers together, we chain n full adders, each responsible for one of the n columns of the addition operation. This circuit is known as a ripple-carry adder.
For example, let’s say we want to add two 4-bit numbers A and B, with and .
What goes in carry-in1?
A0
B0
sum0
carry-out0
A1
B1
sum1
carry-out1
carry-in1
A2
B2
sum2
carry-out2
carry-in2
A3
B3
sum3
carry-out3
carry-in3
carry-in0
?
Notes: If we want to go beyond a single column to adding two n-bit numbers together, we can chain n full adders (instead of n-1 full adders and 1 half adder), each responsible for one of the n columns of the addition operation. This circuit is known as a ripple-carry adder. What would the first carry-in bit?

## Slide 42: Ripple-carry adder
A full adder calculates the sum of a single column of the addition operation.
If we want to add two n-bit numbers together, we chain n full adders, each responsible for one of the n columns of the addition operation. This circuit is known as a ripple-carry adder.
For example, let’s say we want to add two 4-bit numbers A and B, with and .
The first carry-in1 will be 0.
A0
B0
sum0
carry-out0
A1
B1
sum1
carry-out1
carry-in1
A2
B2
sum2
carry-out2
carry-in2
A3
B3
sum3
carry-out3
carry-in3
carry-in0
0
Notes: The first carry-in is always 0. How can we detect overflow if we're working with signed two's complement numbers?

## Slide 43: Decoders
Notes: Next, we will talk about another type of combinational circuits called decoders.

## Slide 44: Think
Inputs |  | Outputs |  |  | 
0 | 0 |  |  |  | 
0 | 1 |  |  |  | 
1 | 0 |  |  |  | 
1 | 1 |  |  |  | 
Inputs |  | Outputs |  |  | 
0 | 0 |  |  |  | 
0 | 1 |  |  |  | 
1 | 0 |  |  |  | 
1 | 1 |  |  |  | 
Notes: Given the following circuit, can you fill out the truth table?

## Slide 45: 2-bit decoders
Inputs |  | Outputs |  |  | 
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1
Inputs |  | Outputs |  |  | 
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1
Notes: Did you notice that it sends a 1 along one of the output lines only? This circuit is called a 2-bit decoder.

## Slide 46: 2-bit decoders
2-bit decoders are basic circuits that take 2 inputs and convert them up to 4 outputs.
Exactly one of the outputs will be 1. Which one is determined by the value, in binary, of the two inputs.
You can think of them as a binary to unary converter (from 2 to 1)
Inputs |  | Outputs |  |  | 
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1
Inputs |  | Outputs |  |  | 
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1
Notes: 2-bit decoders are basic circuits that take 2 inputs and convert them up to 4 outputs. Exactly one of the outputs will be 1. Which one is determined by the value, in binary, of the two inputs as seen in the table above. You can think of them as a binary to unary converter. How it's done, is by passing all combinations of d1 and d0 to four AND gates,

## Slide 47: Think
Inputs |  |  | Outputs |  |  | 
enable |  |  |  |  |  | 
0 | 0 | 0 |  |  |  | 
0 | 0 | 1 |  |  |  | 
0 | 1 | 0 |  |  |  | 
0 | 1 | 1 |  |  |  | 
1 | 0 | 0 |  |  |  | 
1 | 0 | 1 |  |  |  | 
1 | 1 | 0 |  |  |  | 
1 | 1 | 1 |  |  |  | 
Inputs |  |  | Outputs |  |  | 
enable |  |  |  |  |  | 
0 | 0 | 0 |  |  |  | 
0 | 0 | 1 |  |  |  | 
0 | 1 | 0 |  |  |  | 
0 | 1 | 1 |  |  |  | 
1 | 0 | 0 |  |  |  | 
1 | 0 | 1 |  |  |  | 
1 | 1 | 0 |  |  |  | 
1 | 1 | 1 |  |  |  | 
Notes: What if we add one more input, let's say enable? What does the table look like?

## Slide 48: 2-bit decoders with enable input
When enable is on (1) the turned on and works as usual. When enable is off (0), the decoder is off.
Inputs |  |  | Outputs |  |  | 
enable |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1
Inputs |  |  | Outputs |  |  | 
enable |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1
Notes: Here's the table. What this means is that when enable is on (that is it gets passed the value 1), the decoder works as usual. When enable is off (that is 0), then no flow passes the decoder and all outputs are zero. What changes now is that our AND gates take three inputs.

## Slide 49: Think
What if we wanted to build a 3-bit decoder? How many lines would we have?
Notes: What if we were to move from 2 to 3 input bits and a build a decoder. How many output lines would we need?

## Slide 50: 3-bit decoder
What if we wanted to build a 3-bit decoder? How many lines would we have?
  8
Inputs |  |  | Outputs |  |  |  |  |  |  | 
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Inputs |  |  | Outputs |  |  |  |  |  |  | 
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Notes: 2^3=8

## Slide 51: Building a 3-bit decoder
We could design a circuit for scratch, but instead we will reuse 2-bit decoders.
We will also use the idea of the enable input.
Inputs |  |  | Outputs |  |  |  |  |  |  | 
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Inputs |  |  | Outputs |  |  |  |  |  |  | 
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Notes: How can we build a 3-bit decoder? We could design a circuit for it from scratch, but instead, we will try to take advantage of prior work and reuse the 2-bit decoder. Remember, this is a picture of what 2 decoders with an enable input would look like.

## Slide 52: Building a 3-bit decoder
acts as the enable bit to two decoders.
When is 0, the top decoder is activated, sending output to one of t0xx.
When is 1, the bottom decoder is activated, sending output to one of t1xx.
Complicated design
Inputs |  |  | Outputs |  |  |  |  |  |  | 
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Inputs |  |  | Outputs |  |  |  |  |  |  | 
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
2-bit decoder
2-bit decoder
Notes: We are going to consolidate the two enable inputs into a single input d2. d2 acts as the enable bit for both decoders. When is 0, the top decoder is activated, sending output to one of t0xx. When is 1, the bottom decoder is activated, sending output to one of t1xx. But the design is kinda complicated.
We are going to consolidate the two enable inputs into a single input d2. d2 acts as the enable bit for both decoders. When 𝑑_2 is 0, the top decoder is activated, sending output to one of t0xx. When 𝑑_2 is 1, the bottom decoder is activated, sending output to one of t1xx. But the design is kinda complicated.

## Slide 53: Abstraction in decoders
acts as the enable bit to two decoders.
When is 0, the top decoder is activated, sending output to one of t0xx.
When is 1, the bottom decoder is activated, sending output to one of t1xx.
Cleaner design
Inputs |  |  | Outputs |  |  |  |  |  |  | 
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Inputs |  |  | Outputs |  |  |  |  |  |  | 
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Notes: Instead, we will introduce abstraction in decoders and hide away the components of how the two bit decoders are implemented. Instead, we will treat them as two black boxes that we give them three inputs and they give us back one of 8 outputs as 1.

## Slide 54: k-bit decoders
We can generalize the idea of 2-bit decoders to -bit decoders. There will now be inputs and up to outputs.
Exactly one of the outputs will be 1 for a given row in the truth table. This is known as "1-hot." Which one is determined by the value, in binary, of the inputs.
Notes: We can generalize the idea of 2-bit decoders to -bit decoders. There will now be inputs and up to outputs. Exactly one of the outputs will be 1 for a given row in the truth table. This is known as 1-hot. Which one is determined by the value, in binary, of the inputs.
We can generalize the idea of 2-bit decoders to 𝑘-bit decoders. There will now be 𝑘 inputs and up to 2^𝑘 outputs. Exactly one of the 2^𝑘 outputs will be 1 for a given row in the truth table. This is known as 1-hot. Which one is determined by the value, in binary, of the 𝑘 inputs.

## Slide 55: 7-Segment Display Decoders
Notes: Last type of combinational circuits is the 7-segnent display decoders.

## Slide 56: Decoder application example
How do clocks like this work?
Notes: Have you ever thought how clocks like this work?

## Slide 57: Decoding 7-segment displays
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
We will assume that there are 7 segments, labeled a to g, as shown above.
By illuminating different combinations of these segments, we can generate the digits 0-9.
Notes: Decoders provide a general idea of how we can generate different types of circuits.
One such example is a 7-segment display found on digital clocks and watches.
We will assume that there are 7 segments, labeled a to g, as shown above.
By illuminating different combinations of these segments, we can generate the digits 0-9.

## Slide 58: 7-segment display
Number to display
circuit
c
d
g
f
e
b
a
7
c
d
g
f
e
b
a
a = 0
b = 0
c = 1
d = 1
e = 0
f = 0
g = 1
hardware component with 7 inputs
a b c d
e f g
Notes: The way that this will happen is by activating the right segments to display a specific digit. For example, the number 7 gets displayed if we activate c, d, and g. All other segments need to be off.

## Slide 59: Decoding 7-segment displays in clocks
Digit | Illuminated segments |  |  |  |  |  | 
 | a | b | c | d | e | f | g
0 |  | x | x | x | x | x | x
1 |  |  |  | x |  |  | x
2 | x |  | x | x | x | x | 
3 | x |  | x | x |  | x | x
4 | x | x |  | x |  |  | x
5 | x | x | x |  |  | x | x
6 | x | x | x |  | x | x | x
7 |  |  | x | x |  |  | x
8 | x | x | x | x | x | x | x
9 | x | x | x | x |  |  | x
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
Each cell is marked with an X if the corresponding segment is illuminated in that particular digit.
Let’s see how we can use this information to build a 7-segment display in Logisim-Evolution.
Notes: Using these illustrations, we can build a table where each row corresponds to one of the 10 digits 0-9, each column to one of the 7 segments a-g, and each cell is marked with an X if the corresponding segment is illuminated in that particular digit. How can we build this on Logisim-Evolution?

## Slide 60: Think
Digit | Illuminated segments |  |  |  |  |  | 
 | a | b | c | d | e | f | g
0 |  | x | x | x | x | x | x
1 |  |  |  | x |  |  | x
2 | x |  | x | x | x | x | 
3 | x |  | x | x |  | x | x
4 | x | x |  | x |  |  | x
5 | x | x | x |  |  | x | x
6 | x | x | x |  | x | x | x
7 |  |  | x | x |  |  | x
8 | x | x | x | x | x | x | x
9 | x | x | x | x |  |  | x
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
Each cell is marked with an X if the corresponding segment is illuminated in that particular digit.
How many binary inputs do we need for the numbers 0-9?
Notes: We will start with asking the question, how many binary inputs do we need for 0-9?

## Slide 61: Decoding 7-segment displays in clocks
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
Each cell is marked with an X if the corresponding segment is illuminated in that particular digit.
How many binary inputs do we need for the numbers 0-9?
  Since we have 10 digits, we need 4 bits of input to encode them.
Input | Digit | Illuminated segments |  |  |  |  |  | 
 |  | a | b | c | d | e | f | g
0000 | 0 |  | x | x | x | x | x | x
0001 | 1 |  |  |  | x |  |  | x
0010 | 2 | x |  | x | x | x | x | 
0011 | 3 | x |  | x | x |  | x | x
0100 | 4 | x | x |  | x |  |  | x
0101 | 5 | x | x | x |  |  | x | x
0110 | 6 | x | x | x |  | x | x | x
0111 | 7 |  |  | x | x |  |  | x
1000 | 8 | x | x | x | x | x | x | x
1001 | 9 | x | x | x | x |  |  | x
Notes: Since we have 10 digits, we need at least 4 bits of input to encode them. 3 wouldn't be enough

## Slide 62: Think
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
Since we have 10 digits, we need 4 bits of input to encode them.
If we use a 4-bit decoder, how many output lines will we have?
Input | Digit | Illuminated segments |  |  |  |  |  | 
 |  | a | b | c | d | e | f | g
0000 | 0 |  | x | x | x | x | x | x
0001 | 1 |  |  |  | x |  |  | x
0010 | 2 | x |  | x | x | x | x | 
0011 | 3 | x |  | x | x |  | x | x
0100 | 4 | x | x |  | x |  |  | x
0101 | 5 | x | x | x |  |  | x | x
0110 | 6 | x | x | x |  | x | x | x
0111 | 7 |  |  | x | x |  |  | x
1000 | 8 | x | x | x | x | x | x | x
1001 | 9 | x | x | x | x |  |  | x
Notes: With a 4-bit decoder, how many lines will we have?

## Slide 63: Think
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
Since we have 10 digits, we need 4 bits of input to encode them.
If we use a 4-bit decoder, how many output lines will we have?
  24=16. exactly 1 will be activated depending on the input
Input | Digit | Illuminated segments |  |  |  |  |  | 
 |  | a | b | c | d | e | f | g
0000 | 0 |  | x | x | x | x | x | x
0001 | 1 |  |  |  | x |  |  | x
0010 | 2 | x |  | x | x | x | x | 
0011 | 3 | x |  | x | x |  | x | x
0100 | 4 | x | x |  | x |  |  | x
0101 | 5 | x | x | x |  |  | x | x
0110 | 6 | x | x | x |  | x | x | x
0111 | 7 |  |  | x | x |  |  | x
1000 | 8 | x | x | x | x | x | x | x
1001 | 9 | x | x | x | x |  |  | x
Notes: It would be 2^4=16

## Slide 64: Our friend the decoder
Input | Digit | Illuminated segments |  |  |  |  |  | 
 |  | a | b | c | d | e | f | g
0000 | 0 |  | x | x | x | x | x | x
a b c d
e f g
0000
decoder
c
d
g
f
e
b
a
0000 line will be 1
all others will be 0
Notes: Let's assume we are given the input 0000, That means that the output line 0000 will be 1 and all others will be 0.

## Slide 65: Think
Input | Digit | Illuminated segments |  |  |  |  |  | 
 |  | a | b | c | d | e | f | g
0000 | 0 |  | x | x | x | x | x | x
a b c d
e f g
0000
decoder
c
d
g
f
e
b
a
0000 line will be 1
all others will be 0
c
d
g
f
e
b
a
How do we get it to display a 0?
Notes: How do we get it to display the number 0?

## Slide 66: Our friend the decoder
Input | Digit | Illuminated segments |  |  |  |  |  | 
 |  | a | b | c | d | e | f | g
0000 | 0 |  | x | x | x | x | x | x
a b c d
e f g
0000
decoder
c
d
g
f
e
b
a
0000 line will be 1
all others will be 0
c
d
g
f
e
b
a
Connect the 0000 line to: b c d e f g
When the line is active those segments will illuminate
When it’s not active, no display
Notes: We would connect the 0000 line to b, c, d, e, g, and g. Whne the line is active those segments will illuminate. When it's not active, nothing is displayed.

## Slide 67: Our friend the decoder
Input | Digit | Illuminated segments |  |  |  |  |  | 
 |  | a | b | c | d | e | f | g
0001 | 1 |  |  |  | x |  |  | x
a b c d
e f g
0001
decoder
c
d
g
f
e
b
a
0001 line will be 1
all others will be 0
How do we get it to display a 1?
c
d
g
f
e
b
a
Notes: What if we wanted to display 1 (that is our input is 0001)?

## Slide 68: Our friend the decoder
Input | Digit | Illuminated segments |  |  |  |  |  | 
 |  | a | b | c | d | e | f | g
0001 | 1 |  |  |  | x |  |  | x
a b c d
e f g
0001
decoder
c
d
g
f
e
b
a
0001 line will be 1
all others will be 0
c
d
g
f
e
b
a
Connect the 0001 line to: d g
When the line is active those segments will illuminate
When it’s not active, no display
Notes: We'd similarly connect 0001 to d and g.

## Slide 69: Our friend the decoder
Input | Digit | Illuminated segments |  |  |  |  |  | 
 |  | a | b | c | d | e | f | g
0000 | 0 |  | x | x | x | x | x | x
0001 | 1 |  |  |  | x |  |  | x
a b c d
e f g
decoder
c
d
g
f
e
b
a
0001 line
4-input bits
0000 line
Both of these lines want to connect to d
How do we do this? Hint: gate??
Notes: We just saw that both 0 and 1 want to connect to segment d. What is the gate that we'd need for that?

## Slide 70: Our friend the decoder
Input | Digit | Illuminated segments |  |  |  |  |  | 
 |  | a | b | c | d | e | f | g
0000 | 0 |  | x | x | x | x | x | x
0001 | 1 |  |  |  | x |  |  | x
a b c d
e f g
decoder
c
d
g
f
e
b
a
0001 line
4-input bits
0000 line
Since only one line will be active at a time, use OR gate
Notes: We can connect them with an OR gate!

## Slide 71: Building a 7-segment display in Logisim
Digit | Illuminated segments |  |  |  |  |  | 
 | a | b | c | d | e | f | g
0 |  | x | x | x | x | x | x
1 |  |  |  | x |  |  | x
2 | x |  | x | x | x | x | 
3 | x |  | x | x |  | x | x
4 | x | x |  | x |  |  | x
5 | x | x | x |  |  | x | x
6 | x | x | x |  | x | x | x
7 |  |  | x | x |  |  | x
8 | x | x | x | x | x | x | x
9 | x | x | x | x |  |  | x
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
For each segment a-f of the clock, we will go to the corresponding table column and find the digits that have that segment illuminated. We will then connect the corresponding outputs of the decoder to an OR gate.
  For example, the segment e is illuminated in 0, 2, 6, and 8. We will connect the 0, 2, 6, and 8 outputs of the 4-bit decoder to an OR gate.
We will repeat this process for all 7 segments, ending up with 7 OR gates.
We will then connect each OR gate with the appropriate input of a 7-segment display.
Notes: Putting it all together, for each segment a-f of the clock, we will go to the corresponding table column and find the digits that have that segment illuminated. We will then connect the corresponding outputs of the decoder to an OR gate.
  For example, the segment e is illuminated in 0, 2, 6, and 8. We will connect the 0, 2, 6, and 8 outputs of the 4-bit decoder to an OR gate.
We will repeat this process for all 7 segments, ending up with 7 OR gates.
We will then connect each OR gate with the appropriate input of a 7-segment display.

## Slide 72: A 7-segment display in Logisim
Input | Digit | Illuminated segments |  |  |  |  |  | 
 |  | a | b | c | d | e | f | g
0000 | 0 |  | x | x | x | x | x | x
0001 | 1 |  |  |  | x |  |  | x
0010 | 2 | x |  | x | x | x | x | 
0011 | 3 | x |  | x | x |  | x | x
0100 | 4 | x | x |  | x |  |  | x
0101 | 5 | x | x | x |  |  | x | x
0110 | 6 | x | x | x |  | x | x | x
0111 | 7 |  |  | x | x |  |  | x
1000 | 8 | x | x | x | x | x | x | x
1001 | 9 | x | x | x | x |  |  | x
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
Notes: Cool stuff?

## Slide 73: PRACTICE TIME – Expanding to 16 characters
Input | Character | Illuminated segments |  |  |  |  |  | 
 |  | a | b | c | d | e | f | g
0000 | 0 |  | x | x | x | x | x | x
0001 | 1 |  |  |  | x |  |  | x
0010 | 2 | x |  | x | x | x | x | 
0011 | 3 | x |  | x | x |  | x | x
0100 | 4 | x | x |  | x |  |  | x
0101 | 5 | x | x | x |  |  | x | x
0110 | 6 | x | x | x |  | x | x | x
0111 | 7 |  |  | x | x |  |  | x
1000 | 8 | x | x | x | x | x | x | x
1001 | 9 | x | x | x | x |  |  | x
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
Imagine that the 7-segment display we have built so far is expanded to include 16 characters, the existing 10 digits, and A-F, as depicted here to differentiate among them.
Expand the table on the right to reflect all 16 characters.
How will the design of the circuit change on Logisim-Evolution?
Notes: Your turn now. Imagine that the 7-segment display we have built so far is expanded to include 16 characters, the existing 10 digits, and A-F, as depicted here to differentiate among them. Expand the table on the right to reflect all 16 characters. How will the design of the circuit change on Logisim-Evolution?

## Slide 74: ANSWER – Expanding to 16 characters
Input | Character | Illuminated segments |  |  |  |  |  | 
 |  | a | b | c | d | e | f | g
0000 | 0 |  | x | x | x | x | x | x
0001 | 1 |  |  |  | x |  |  | x
0010 | 2 | x |  | x | x | x | x | 
0011 | 3 | x |  | x | x |  | x | x
0100 | 4 | x | x |  | x |  |  | x
0101 | 5 | x | x | x |  |  | x | x
0110 | 6 | x | x | x |  | x | x | x
0111 | 7 |  |  | x | x |  |  | x
1000 | 8 | x | x | x | x | x | x | x
1001 | 9 | x | x | x | x |  |  | x
1010 | A | x | x | x | x | x |  | x
1011 | B | x | x |  |  | x | x | x
1100 | C | x |  |  |  | x | x | 
1101 | D | x |  |  | x | x | x | x
1110 | E | x | x | x |  | x | x | 
1111 | F | x | x | x |  | x |  | 
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
c
d
g
f
e
b
a
Expanded table:
Circuit in Logisim-Evolution is expanded to include all outputs of decoders connected to 6 additional or gates
Notes: You can see how we have added more rows to capture all 16 possible outputs and have matched the illuminated segments. The circuit in Logisim-Evolution is expanded to include all outputs of decoders connected to 6 additional or gates

## Slide 75: Combinational circuits
So far, all circuits we have seen have been combinational: their output depends on the present inputs and there is no notion of memory of past inputs.
Roughly speaking, combinational circuits perform arithmetic and logical operations, transmit data, or convert code. So far, we have seen for
  Arithmetic and logical operations: logic circuits and half/full/and ripple-carry adders
  Transmit data: decoders (and we will see multiplexers in the next assignment)
  Convert code: 7-segment display decoders
Other combinational circuits you might hear about are encoders (the opposite of decoders, they compress multiple lines of inputs into a smaller number of outputs) and demultiplexers (the opposite of multiplexers, you go from one input to multiple outputs, instead of multiple inputs to one output).
Notes: To summarize, so far, all circuits we have seen have been combinational: their output depends on the present inputs and there is no notion of memory of past inputs. Roughly speaking, combinational circuits perform arithmetic and logical operations, transmit data, or convert code. So far, we have seen for
Arithmetic and logical operations: logic circuits and half/full/and ripple-carry adders
Transmit data: decoders (and we will see multiplexers in the next assignment). A multiplexer (MUX) selects one of many data inputs and sends it to a single output, acting like a digital switch, while a decoder converts a binary code into a unique set of output signals, activating one specific output out of many for a given input code. The key difference is the direction of data flow and purpose: a MUX combines multiple data lines into one, and a decoder distributes a coded signal to multiple possible lines
Convert code: 7-segment display decoders
Other combinational circuits you might hear about are encoders (the opposite of decoders, they compress multiple lines of inputs into a smaller number of outputs) and demultiplexers (the opposite of multiplexers, you go from one input to multiple outputs, instead of multiple inputs to one output).

## Slide 76: Resources
Download Logisim Evolution from https://github.com/logisim-evolution/logisim-evolution?tab=readme-ov-file#download
Combinational circuits shown in lecture today if you want to work with them on Logisim Evolution https://cs.pomona.edu/classes/cs51/circuits/combinational_circuits.circ