## Slide 1: CS52 machine
David Kauchak CS 54 – Fall 2022

## Slide 2: Admin
Midterm 1
Practice problems posted
Very light coverage of numbers with different bases (I wouldn’t put Q7 on the midterm)
Assignment 2 grading
Assignment 3
Assignment 4

## Slide 3: Admin
Extra mentor hours:
Monday, 8-10pm (Gabriel)
Tuesday, 8:15-9:30 (Will)
My Wednesday office hours:
9:30-10:30am (No hours 10:30am-12)

## Slide 4: Examples from this lecture
https://cs.pomona.edu/classes/cs54/examples/cs52machine

## Slide 5: Computer internals

## Slide 6: Computer internals simplified
What does it stand for?
What does it do?
CPU
RAM
What does it stand for?
What does it do?

## Slide 7: Computer internals simplified
(Central Processing Unit,
aka “the processor”)
CPU
RAM
(Random Access Memory,
aka “memory” or “main memory”)
Does all the work!
Temporary storage

## Slide 8: Computer internals simplified
CPU
RAM
hard drive
“the computer”
Why do we need a hard drive?

## Slide 9: Computer internals simplified
CPU
RAM
hard drive
“the computer”
Persistent memory
RAM only stores data while it has power

## Slide 10: Computer simplified
hard drive
media drive
CPU
RAM
“the computer”
display
network
input devices

## Slide 11: Inside the CPU
CPU
processor
…
registers
processor: does the work
registers: local, fast memory slots
Why all these levels of memory?

## Slide 12: Memory speed
operation | access time | times slower than register access | for comparison…
register | 0.3 ns | 1 | 1 s
RAM | 120 ns | 400 | 6 min
Hard disk | 1ms | ~million | 1 month
box, onedrive, … | 0.4s | ~billion | 30 years

## Slide 13: Memory
RAM
010101111000101000010010 …
What is a byte?
?

## Slide 14: Memory
RAM
01010111 10001010 00010010 …
byte = 8 bits
byte is abbreviated as B
My laptop has 32GB (gigabytes) of memory. How many bits is that?

## Slide 15: Memory sizes
 | bits
byte | 8
kilobyte (KB) | 2^10 bytes = ~8,000
megabyte (MB) | 2^20 =~ 8 million
gigabyte (GB) | 2^30 = ~8 billion
My laptop has 32GB (gigabytes) of memory. How many bits is that?

## Slide 16: Memory sizes
 | bits
byte | 8
kilobyte (KB) | 2^10 bytes = ~8,000
megabyte (MB) | 2^20 =~ 8 million
gigabyte (GB) | 2^30 = ~8 billion
~256 billion bits!

## Slide 17: Memory
RAM
01010111
10001010
00010010
01011010
…
Memory is byte addressable
address
0
1
2
3
…

## Slide 18: Memory
RAM
01010111
10001010
00010010
01011010
…
Memory is organized into “words”, which is the most common functional unit
address
0
1
2
3
…

## Slide 19: Memory
RAM
10101011 10001010 00010010 01011010
11001011 00001110 01010010 01010110
10111011 10010010 00000000 01110100
…
Most modern computers use 32-bit (4 byte) or 64-bit (8 byte) words
address
0
4
8
...
32-bit words

## Slide 20: Memory in the CS52 Machine
RAM
10101011 10001010
00010010 01011010
11001011 00001110
…
We’ll use 16-bit words for our model (the CS52 machine)
address
0
2
4
...
16-bit words

## Slide 21: CS52 machine
CPU
processor
registers
ic
r0
r1
r2
r3
instruction counter
(location in memory of the next
instruction in memory)
holds the value 0 (read only)
general purpose
read/write

## Slide 22
ic
r0
r1
r2
r3
instruction counter
(location in memory of the next
instruction in memory)
holds the value 0 (read only)
general purpose
read/write

## Slide 23: CS52 machine instructions
CPU
processor
registers
What types of operations might we want to do (think really basic)?

## Slide 24: CS52 machine code
Four main types of instructions
math
branch/conditionals
memory
control the machine (e.g. stop it)

## Slide 25
instruction name
arguments

## Slide 26
instruction name
arguments
instruction/operation name
(always three characters)

## Slide 27
instruction name
arguments
operation arguments
R = register (e.g. r0)
S = signed number (byte)

## Slide 28
instruction name
arguments
1st R: register where the answer will go
2nd R: register of first operand
3rd S/R: register/value of second operand

## Slide 29
add r1 r2 r3
What does this do?
1st R: register where the answer will go
2nd R: register of first operand
3rd S/R: register/value of second operand

## Slide 30
add r1 r2 r3
r1 = r2 + r3
Add contents of registers r2 and r3 and store the result in r1
1st R: register where the answer will go
2nd R: register of first operand
3rd S/R: register/value of second operand

## Slide 31
add r2 r1 10
What does this do?
1st R: register where the answer will go
2nd R: register of first operand
3rd S/R: register/value of second operand

## Slide 32
add r2 r1 10
r2 = r1 + 10
Add 10 to the contents of register r1 and store in r2
1st R: register where the answer will go
2nd R: register of first operand
3rd S/R: register/value of second operand

## Slide 33
add r1 r0 8
neg r2 r1
sub r2 r1 r2
What number is in r2?
1st R: register where the answer will go
2nd R: register of first operand
3rd S/R: register/value of second operand

## Slide 34
add r1 r0 8
neg r2 r1
sub r2 r1 r2
r1 = 8
r2 = -8, r1 = 8
r2 = 16
1st R: register where the answer will go
2nd R: register of first operand
3rd S/R: register/value of second operand

## Slide 35: Accessing memory
sto = save data in register TO memory
loa = put data FROM memory into a register
sto r1 r2 ; store the contents of r1 to mem[r2]
loa r1 r2 ; get data from mem[r2] and put into r1

## Slide 36: Accessing memory
sto = save data in register TO memory
loa = put data FROM memory into a register
Special cases:
saving TO (sto) address 0 prints
reading from (loa) address 0 gets input from user

## Slide 37: Basic structure of CS52 program
; great comments at the top!
;
instruction1 ; comment
instruction2 ; comment
...
hlt
whitespace before operations/instructions

## Slide 38: Running the CS52 machine
Look at subtract.a52
load two numbers from the user
subtract
print the result

## Slide 39: CS52 simulator
Different windows
  Memory (left)
  Instruction execution (right)
  Registers
  I/O and running program

## Slide 40
1st R: first register for comparison
2nd R: second register in comparison
3rd B: label

## Slide 41
beq r3 r0 done
What does this do?
1st R: first register for comparison
2nd R: second register in comparison
3rd B: label

## Slide 42
beq r3 r0 done
If r3 = 0, branch to the label “done”
if not (else) ic is incremented as normal to the next instruction
1st R: first register for comparison
2nd R: second register in comparison
3rd B: label

## Slide 43
ble r2 r3 done
What does this do?
1st R: first register for comparison
2nd R: second register in comparison
3rd B: label

## Slide 44
ble r2 r3 done
If r2 <= r3, branch to the label done
1st R: first register for comparison
2nd R: second register in comparison
3rd B: label

## Slide 45
Conditionals
Loops
Change the order that instructions are executed

## Slide 46: CS52 machine execution

## Slide 47: Basic structure of CS52 program
; great comments at the top!
;
instruction1 ; comment
instruction2 ; comment
...
label1
instruction ; comment
instruction ; comment
label2
...
hlt
end
- whitespace before operations/instructions
- labels go here

## Slide 48: More CS52 examples
Look at max_simple.a52
Get two values from the user
Compare them
Use a branch to distinguish between the two cases
  Goal is to get largest value in r3
print largest value