## Slide 1: Lecture 1: Introduction to Computer Systems
CS 105

## Slide 2: Exercise 0: Introductions
Go onto the CS 105 Zulip (https://cs105s21.zulipchat.com) and introduce yourself
Notice that there is a channel called #q&a. If you have questions while watching the lecture videos, post them there!

## Slide 3: Abstraction

## Slide 4: Correctness
Example 1: Is x2 ≥ 0?
  Floats: Yes!
  Ints:
    40000 * 40000 ➙ 1600000000
    50000 * 50000 ➙ ??
Example 2: Is (x + y) + z = x + (y + z)?
  Ints: Yes!
  Floats:
    (2^30 + -2^30) + 3.14 ➙ 3.14
    2^30 + (-2^30 + 3.14) ➙ ??
Notes: Source: xkcd.com/571

## Slide 5: Computer Arithmetic
Does not generate random values
  Arithmetic operations have important mathematical properties
Cannot assume all “usual” mathematical properties
  Due to finiteness of representations
  Integer operations satisfy “ring” properties
    Commutativity, associativity, distributivity
  Floating point operations satisfy “ordering” properties
    Monotonicity, values of signs
Observation
  Need to understand which abstractions apply in which contexts
  Important issues for compiler writers and serious application programmers

## Slide 6: Performance
Hierarchical memory organization
Performance depends on access patterns
  Including how step through multi-dimensional array
void copyji(int src[2048][2048],
int dst[2048][2048]){
int i,j;
for (j = 0; j < 2048; j++){
for (i = 0; i < 2048; i++){
dst[i][j] = src[i][j];
}
}
}
void copyij(int src[2048][2048],
int dst[2048][2048]){
int i,j;
for (i = 0; i < 2048; i++){
for (j = 0; j < 2048; j++){
dst[i][j] = src[i][j];
}
}
}
81.8ms
4.3ms
Notes: 2.0 GHz Intel Core i7 Haswell

## Slide 7: Real-World Performance
Constant factors matter too!
And even exact op count does not predict performance
  Easily see 10:1 performance range depending on how code written
  Must optimize at multiple levels: algorithm, data representations, procedures, and loops
Must understand system to optimize performance
  How programs compiled and executed
  How to measure program performance and identify bottlenecks
  How to improve performance without destroying code modularity and generality

## Slide 8: Security
void admin_stuff(int authenticated){
if(authenticated){
// do admin stuff
}
}
int dontTryThisAtHome(char * user_input, int size) {
char data[size];
int ret = memcpy(*user_input, data);
return ret;
}

## Slide 9: Bits
a bit is a binary digit that can have two possible values
can be physically represented with a two state device

## Slide 10: Storing bits
Static random access memory (SRAM): stores each bit of data in a flip-flop, a circuit with two stable states
Dynamic Memory (DRAM): stores each bit of data in a capacitor, which stores energy in an electric field (or not)
Magnetic Disk: regions of the platter are magnetized with either N-S polarity or S-N polarity
Optical Disk: stores bits as tiny indentations (pits) or not (lands) that reflect light differently
Flash Disk: electrons are stored in one of two gates separated by oxide layers

## Slide 11: Boolean Algebra
Developed by George Boole in 19th Century
Algebraic representation of logic---encode “True” as 1 and “False” as 0
And
Or
Not
Exclusive-Or (Xor)

## Slide 12: Exercise 1: Boolean Operations
Evaluate each of the following expressions
  1 | (~1)
  ~( 1 | 1)
  (~1) & 1
  ~( 1 ^ 1)

## Slide 13: Exercise 1: Boolean Operations
Evaluate each of the following expressions
  1 | (~1)
  ~( 1 | 1)
  (~1) & 1
  ~( 1 ^ 1)
  = 1 | 0 = 1
  = ~1 = 0
  = 0 & 1 = 0
  = ~0 = 1

## Slide 14: Bytes and Memory
Memory is an array of bits
A byte is a unit of eight bits
An index into the array is an address, location, or pointer
  Often expressed in hexadecimal
We speak of the value in memory at an address
  The value may be a single byte …
  … or a multi-byte quantity starting at that address
1
0
1
0
0
0
1
1
0
1
1
0
1
1
0
0
0
1
1
1
0
1
0
0
1
1
0
0
1
1
1
0
0
1
2
3
01101100
01010011
11010001
00110111
bytes

## Slide 15: General Boolean algebras
Bitwise operations on bytes
How does this map to set operations?
01101001
& 01010101
01000001
01101001
| 01010101
01111101
01101001
^ 01010101
00111100
~ 01010101
10101010
01000001
01111101
00111100
10101010

## Slide 16: Exercise 2 : Bitwise Operations
Assume: a = 01101100, b = 10101010
What are the results of evaluating the following Boolean operations?
  ~a
  ~b
  a & b
  a | b
  a ^ b

## Slide 17: Exercise 2 : Bitwise Operations
Assume: a = 01101100, b = 10101010
What are the results of evaluating the following Boolean operations?
  ~a
  ~b
  a & b
  a | b
  a ^ b
  = ~01101100 = 10010011
  = ~10101010 = 01010101
  = 01101100 & 10101010 = 00101000
  = 01101100 | 10101010 = 11101110
  = 01101100 ^ 10101010 = 11000110

## Slide 18: Bitwise vs Logical Operations in C
Bitwise Operators &, |, ~, ^
  View arguments as bit vectors
  operations applied bit-wise in parallel
Logical Operators &&, ||, !
  View 0 as “False”
  View anything nonzero as “True”
  Always return 0 or 1
  Early termination

## Slide 19: Exercise 3: Bitwise vs Logical Operations
~01000001
~00000000
~~01000001
!01000001
!00000000
!!01000001
01101001 & 01010101
01101001 | 01010101
01101001 && 01010101
01101001 || 01010101
Notes: 0xBE, 0xFF, 0x41
0x41, 0x7D
0x00, 0x01, 0x01
0x01, 0x01

## Slide 20: Exercise 3: Bitwise vs Logical Operations
~01000001
~00000000
~~01000001
!01000001
!00000000
!!01000001
01101001 & 01010101
01101001 | 01010101
01101001 && 01010101
01101001 || 01010101
10111110
11111111
01000001
00000000
00000001
00000001
01000001
01111101
00000001
00000001
Notes: 0xBE, 0xFF, 0x41
0x41, 0x7D
0x00, 0x01, 0x01
0x01, 0x01

## Slide 21: Bit Shifting
Left Shift: x << y
  Shift bit-vector x left y positions
  Throw away extra bits on left
  Fill with 0’s on right
Right Shift: x >> y
  Shift bit-vector x right y positions
  Throw away extra bits on right
  Logical shift: Fill with 0’s on left
  Arithmetic shift: Replicate most significant bit on left
Choice between logical and arithmetic depends on the type of data
Undefined Behavior if you shift amount < 0 or ≥ word size

## Slide 22: Example: Bit Shifting
01101001 << 4
01101001 >>l 2
01101001 >>a 4
10010000
00011010
00000110
Notes: Note: Shift demo

## Slide 23: Exercise 4: Bit Shifting
10101010 << 4
10101010 >>l 4
10101010 >>a 4
10100000
00001010
11111010
Notes: Note: Shift demo

## Slide 24: Bits and Bytes Require Interpretation
00000000 00110101 00110000 00110001
might be interpreted as
  The integer 3,485,74510
  A floating point number close to 4.884569 x 10-39
  The string “105”
  A portion of an image or video
  An address in memory

## Slide 25: Information is Bits + Context

## Slide 26: Exercise 5: Feedback
Rate how well you think this recorded lecture worked
  Better than an in-person class
  About as well as an in-person class
  Less well than an in-person class, but you still learned something
  Total waste of time, you didn't learn anything
How much time did you spend on this video lecture (including time spent on exercises)?
Are there any particular questions that you would like me to address in this week’s problem session?
Do you have any other comments or feedback?