## Slide 1: Lecture 2: Representing Integers
CS 105

## Slide 2: Abstraction

## Slide 3: Memory: A (very large) array of bytes
Memory is an array of bits
A byte is a unit of eight bits
An index into the array is an address, location, or pointer
  Often expressed in hexadecimal
We speak of the value in memory at an address
  The value may be a single byte …
  … or a multi-byte quantity starting at that address
1
0
1
0
0
0
1
1
0
1
1
0
1
1
0
0
0
1
1
1
0
1
0
0
1
1
0
0
1
1
1
0
0
1
2
3
01101100
01010011
11010001
00110111
bytes

## Slide 4: Representing Integers
Arabic Numerals: 47
Roman Numerals: XLVII
Brahmi Numerals:
Tally Marks: IIII IIII IIII IIII IIII IIII IIII IIII IIII II

## Slide 5: Base-10 Integers
1000 (103) | 100 (102) | 10 (101) | 1 (100)
0 | 0 | 0 | 5
0 | 0 | 4 | 7
1 | 8 | 8 | 7

## Slide 6: Storing bits
Static random access memory (SRAM): stores each bit of data in a flip-flop, a circuit with two stable states
Dynamic Memory (DRAM): stores each bit of data in a capacitor, which stores energy in an electric field (or not)
Magnetic Disk: regions of the platter are magnetized with either N-S polarity or S-N polarity
Optical Disk: stores bits as tiny indentations (pits) or not (lands) that reflect light differently
Flash Disk: electrons are stored in one of two gates separated by oxide layers

## Slide 7: Base-2 Integers (aka Binary Numbers)
128 (27) | 64 (26) | 32 (25) | 16 (24) | 8 (23) | 4 (22) | 2 (21) | 1 (20)
0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 8: Binary Numbers
Decimal (Base-10):
Binary (Base-2):
4211
1011

## Slide 9: Exercise 1: Binary Numbers
Consider the following four-bit binary values. What is the (base-10) integer interpretation of these values?
  0001
  1010
  0111
  1111

## Slide 10: Exercise 1: Binary Numbers
Consider the following four-bit binary values. What is the (base-10) integer interpretation of these values?
  0001
  1010
  0111
  1111

## Slide 11: Binary Numbers

## Slide 12: Exercise 2: Binary Number Range
What are the max number and min number that can be represented by a w-bit binary number?
  w = 3
  w = 4
  w = 8

## Slide 13: Exercise 2: Binary Number Range
What are the max number and min number that can be represented by a w-bit binary number?
  w = 3
  w = 4
  w = 8

## Slide 14: Unsigned Integers in C
C Data Type | Size (bytes)
unsigned char | 1
unsigned short | 2
unsigned int | 4
unsigned long | 8
Notes: Note: unsigned demo

## Slide 15: ASCII characters
Char | Dec | Binary
! | 33 | 00100001
" | 34 | 00100010
# | 35 | 00100011
$ | 36 | 00100100
% | 37 | 00100101
& | 38 | 00100110
' | 39 | 00100111
( | 40 | 00101000
) | 41 | 00101001
* | 42 | 00101010
+ | 43 | 00101011
, | 44 | 00101100
- | 45 | 00101101
. | 46 | 00101110
/ | 47 | 00101111
0 | 48 | 00110000
Char | Dec | Binary
1 | 49 | 00110001
2 | 50 | 00110010
3 | 51 | 00110011
4 | 52 | 00110100
5 | 53 | 00110101
6 | 54 | 00110110
7 | 55 | 00110111
8 | 56 | 00111000
9 | 57 | 00111001
: | 58 | 00111010
; | 59 | 00111011
< | 60 | 00111100
= | 61 | 00111101
> | 62 | 00111110
? | 63 | 00111111
@ | 64 | 01000000
Char | Dec | Binary
A | 65 | 01000001
B | 66 | 01000010
C | 67 | 01000011
D | 68 | 01000100
E | 69 | 01000101
F | 70 | 01000110
G | 71 | 01000111
H | 72 | 01001000
I | 73 | 01001001
J | 74 | 01001010
K | 75 | 01001011
L | 76 | 01001100
M | 77 | 01001101
N | 78 | 01001110
O | 79 | 01001111
P | 80 | 01010000
Char | Dec | Binary
Q | 81 | 01010001
R | 82 | 01010010
S | 83 | 01010011
T | 84 | 01010100
U | 85 | 01010101
V | 86 | 01010110
W | 87 | 01010111
X | 88 | 01011000
Y | 89 | 01011001
Z | 90 | 01011010
[ | 91 | 01011011
\ | 92 | 01011100
] | 93 | 01011101
^ | 94 | 01011110
_ | 95 | 01011111
` | 96 | 01100000
Char | Dec | Binary
a | 97 | 01100001
b | 98 | 01100010
c | 99 | 01100011
d | 100 | 01100100
e | 101 | 01100101
f | 102 | 01100110
g | 103 | 01100111
h | 104 | 01101000
i | 105 | 01101001
j | 106 | 01101010
k | 107 | 01101011
l | 108 | 01101100
m | 109 | 01101101
n | 110 | 01101110
o | 111 | 01101111
p | 112 | 01110000

## Slide 16: Hexidecimal Numbers
00101100 00110101 00110000 11100001
Dec | Hex
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
8 | 
9 | 
10 | 
11 | 
12 | 
13 | 
14 | 
15 | 
0
1
2
3
4
5
6
7
8
9
a
b
c
d
e
f
2
c
3
5
3
0
e
1
0x2c3530e1

## Slide 17: Exercise 3: Hexidecimal Numbers
Consider the following hexidecimal values. What is the representation of each value in (1) binary and (2) decimal?
  0x0a
  0x11
  0x2f

## Slide 18: Exercise 3: Hexidecimal Numbers
Consider the following hexidecimal values. What is the representation of each value in (1) binary and (2) decimal?
  0x0a
  0x11
  0x2f

## Slide 19: Endianness
47 vs 74

## Slide 20: Endianness
Big Endian: low-order bits go on the right (47)
  I tend to think in big endian numbers, so examples in class will generally use this representation
  Networks generally use big endian (aka network byte order)
Little Endian: low-order bits go on the left (74)
  Most modern machines use this representation
I will try to always be clear about whether I'm using a big endian or little endian representation
When in doubt, ask!

## Slide 21: Arithmetic Logic Unit (ALU)
circuit that performs bitwise operations and arithmetic on integer binary types

## Slide 22: Bitwise vs Logical Operations in C
Bitwise Operators &, |, ~, ^
  View arguments as bit vectors
  operations applied bit-wise in parallel
Logical Operators &&, ||, !
  View 0 as “False”
  View anything nonzero as “True”
  Always return 0 or 1
  Early termination
Shift operators <<, >>
  Left shift fills with zeros
  For unsigned integers, right shift is logical (fills with zeros)

## Slide 23: Exercise 4: Bitwise vs Logical Operations
Assume unsigned char data type (one byte). What do each of the following expressions evaluate to (interpreted as unsigned integers and expressed base-10)?
  ~226
  !226
  120 & 85
  120 | 85
  120 && 85
  120 || 85
  81 << 4
  81 << 2
  81 >> 4
  81 >> 2
Notes: 0xBE, 0xFF, 0x41
0x41, 0x7D
0x00, 0x01, 0x01
0x01, 0x01

## Slide 24: Exercise 4: Bitwise vs Logical Operations
Assume unsigned char data type (one byte). What do each of the following expressions evaluate to (interpreted as unsigned integers and expressed base-10)?
  ~226
  !226
  120 & 85
  120 | 85
  120 && 85
  120 || 85
  81 << 4
  81 << 2
  81 >> 4
  81 >> 2
= ~11100010
= !11100010 = 00000000 = 0
= 01111000 & 01010101
= 01111000 | 01010101 = 01111101 = 125
= 01111000 && 01010101 = 00000001 = 1
= 01111000 || 01010101 = 00000001 = 1
= 01010001 << 4
= 01010001 << 2 = 01000100 = 68
= 01010001 >> 4 = 00000101 = 5
= 01010001 >> 2 = 00010100 = 20
= 00011101
= 01010000 = 80
= 29
= 00010000 = 16
Notes: 0xBE, 0xFF, 0x41
0x41, 0x7D
0x00, 0x01, 0x01
0x01, 0x01

## Slide 25: Example: Using Bitwise Operations
x & 1
(x + 7) & 0xFFFFFFF8
x << 2
“x is odd”
“round up to a multiple of 8”
"multiply by 4"
Notes: Note: int demo

## Slide 26: Addition Example
Compute 5 + 6 assuming all ints are stored as eight-bit (1 byte) unsigned values
Like you learned in grade school, only binary!
0 0 0 0 0 1 0 1
+ 0 0 0 0 0 1 1 0
1
1
0
1
1
… and with a finite number of digits
0
0
0
0
= 11 (Base-10)

## Slide 27: Addition Example with Overflow
Compute 200 + 100 assuming all ints are stored as eight-bit (1 byte) unsigned values
Like you learned in grade school, only binary!
1 1 0 0 1 0 0 0
+ 0 1 1 0 0 1 0 0
0
0
1
1
… and with a finite number of digits
0
1
0
0
1
1
= 44 (Base-10)

## Slide 28: Error Cases
Assume -bit unsigned values
overflow has occurred iff
[ )
representable values
[ )
Possible values of

## Slide 29: Exercise 5: Binary Addition
Given the following 5-bit unsigned values, compute their sum and indicate whether or not an overflow occurred
x | y | x+y | overflow?
00010 | 00101 |  | 
01100 | 00100 |  | 
10100 | 10001 |  | 

## Slide 30: Exercise 5: Binary Addition
Given the following 5-bit unsigned values, compute their sum and indicate whether or not an overflow occurred
x | y | x+y | overflow?
00010 | 00101 |  | 
01100 | 00100 |  | 
10100 | 10001 |  | 
00111
10000
00101
no
no
yes

## Slide 31: Multiplication Example
Compute 5 x 6 assuming all ints are stored as eight-bit (1 byte) unsigned values
Like you learned in grade school, only binary!
0 0 0 0 0 1 0 1
x 0 0 0 0 0 1 1 0
… and with a finite number of digits
= 30 (Base-10)
0 0 0 0 0 0 0 0
0 0 0 0 0 1 0 1 0
+ _
0 0 0 0 0 1 0 1 0 0
0 0 0 1 1 1 1 0

## Slide 32: Addition Example
Compute 200 x 3 assuming all ints are stored as eight-bit (1 byte) unsigned values
Like you learned in grade school, only binary!
1 1 0 0 1 0 0 0
x 0 0 0 0 0 0 1 1
… and with a finite number of digits
= 88 (Base-10)
1 1 0 0 1 0 0 0
+ _
1 1 0 0 1 0 0 0 0
0 1 0 1 1 0 0 0
1 0

## Slide 33: Error Cases
Assume -bit unsigned values
[ )
representable values
[ )
Possible values of

## Slide 34: Exercise 6: Binary Multiplication
Given the following 3-bit unsigned values, compute their product and indicate whether or not an overflow occurred
x | y | x*y | overflow?
100 | 101 |  | 
010 | 011 |  | 
111 | 010 |  | 

## Slide 35: Exercise 6: Binary Multiplication
Given the following 3-bit unsigned values, compute their product and indicate whether or not an overflow occurred
x | y | x*y | overflow?
100 | 101 |  | 
010 | 011 |  | 
111 | 010 |  | 
100
110
110
yes
no
yes

## Slide 36: Multiplying with Shifts
Multiplication is slow
Bit shifting is kind of like multiplication, and is often faster
  x * 8 = x << 3
  x * 10 = x << 3 + x << 1
Most compilers will automatically replace multiplications with shifts where possible

## Slide 37: Exercise 7: Feedback
Rate how well you think this recorded lecture worked
  Better than an in-person class
  About as well as an in-person class
  Less well than an in-person class, but you still learned something
  Total waste of time, you didn't learn anything
How much time did you spend on this video lecture (including time spent on exercises)?
Do you have any particular questions you’d like me to address in this week’s problem session?
Do you have any comments or feedback?