## Slide 1: Lecture 6: Control Flow in Assembly
CS 105 Spring 2021

## Slide 2: Assembly/Machine Code View
Memory
0x7FFF
0x0000
Central Processing Unit (CPU)
Programmer-Visible State
  PC: Program counter (%rip)
  Register file: 16 Registers
  Float registers
  Condition codes
    Memory
    Byte addressable array
    Code and user data
    Stack to support procedures
PC
Data
Addresses
Instructions
Code
Data
Stack
Heap
Registers
Condition
Codes
Float registers

## Slide 3: Assembly Characteristics: Operations
Transfer data between memory and register
  Load data from memory into register
  Store register data into memory
Perform arithmetic function on register or memory data
Transfer control
  Conditional branches
  Unconditional jumps to/from procedures

## Slide 4: Jumps
A jump instruction can cause the execution to switch to a completely new position in the program (updates the program counter)
  jmp Label
  jmp *Operand
.L0:
movq $0, %rax
jmp .L1
movq (%rax), %rdx
.L1:
movq %rcx, %rax
jmp *%rax

## Slide 5: Branches and Jumps
Processor state (partial)
  Temporary data ( %rax, … )
  Location of runtime stack ( %rsp )
  Location of current code control point ( %rip, … )
  Status of recent tests ( CF, ZF, SF, OF )
%rip
Registers
Instruction pointer
CF
ZF
SF
OF
Condition codes
%rsp (stack ptr)
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax (return val)
%rbx
%rcx (4th arg)
%rdx (3rd arg)
%rsi (2nd arg)
%rdi (1st arg)
%rbp

## Slide 6: Condition Codes
Single bit registers
    SF Sign Flag (for signed)
    ZF Zero Flag
    CF Carry Flag (for unsigned)
    OF Overflow Flag (for signed)
Implicitly set (as a side effect) by arithmetic operations and comparison operations
Not set by leaq instruction

## Slide 7: Condition Codes: compare
Instruction cmp explicitly sets condition codes
cmpq a,b like computing b-a without setting destination
  ZF set if (b-a) == 0
  SF set if (b-a) < 0 (as signed)
  CF set if carry out from most significant bit (used for unsigned comparisons)
  OF set if two’s-complement (signed) overflow

## Slide 8: Condition Codes: test
Instruction test explicitly sets condition codes
testq a,b like computing a&b without setting destination
  ZF set when a&b == 0
  SF set when a&b < 0
Test for zero: testq %rax, %rax

## Slide 9: Reading Condition Codes
  Set low-order byte of destination to 0 or 1 based on combinations of condition codes
  Does not alter remaining 7 bytes
SetX | Condition | Description
sete | ZF | Equal / Zero
setne | ~ZF | Not Equal / Not Zero
sets | SF | Negative
setns | ~SF | Nonnegative
setg | ~(SF ^ OF) & ~ZF | Greater (signed)
setge | ~(SF ^ OF) | Greater or Equal (signed)
setl | SF ^ OF | Less (signed)
setle | (SF ^ OF) ¦ ZF | Less or Equal (signed)

## Slide 10: Reading Condition Codes
setX instruction: set a single byte based on condition codes
Does not alter remaining bytes of destination
Typically use movz to set the rest of the bits to zero
long gt (long x, long y){
return x > y;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value
gt:
cmpq %rsi, %rdi # set flags for x-y
setg %al # ~(SF^OF)&~ZF, True when x > y
movzbq %al, %rax # Zero rest of %rax
ret # return

## Slide 11: Jumping
jX instructions
  Jump to different part of code if condition is true
jX | Condition | Description
jmp | 1 | Unconditional
je | ZF | Equal / Zero
jne | ~ZF | Not Equal / Not Zero
jl | (SF ^ OF) | Less (Signed)
jle | (SF ^ OF) ¦ ZF | Less or Equal (Signed)
jg | ~(SF ^ OF) & ~ZF | Greater (Signed)
jge | ~(SF ^ OF) | Greater or Equal (Signed)
cmpq a,b like computing b-a without setting destination
Notes: js SF Negative
jns ~SF Nonnegative

## Slide 12: Exercise 1: Conditional Jumps
Consider each of the following segments of assembly code, and indicate whether or not the jump will occur. In all cases, assume that %rdi contains the value 47 and %rsi contains the value 13
  addq %rdi, %rsi
  je .L0
  subq %rdi, %rsi
  jge .L0
  cmpq %rdi, %rsi
  jl .L0
  testq %rdi, %rdi
  jne .L0

## Slide 13: Exercise 1: Conditional Jumps
Consider each of the following segments of assembly code, and indicate whether or not the jump will occur. In all cases, assume that %rdi contains the value 47 and %rsi contains the value 13
  addq %rdi, %rsi
  je .L0
  subq %rdi, %rsi
  jge .L0
  cmpq %rdi, %rsi
  jl .L0
  testq %rdi, %rdi
  jne .L0
no jump
no jump
jump
jump

## Slide 14: Conditional Branching
absdiff:
movq %rdi, %rax
subq %rsi, %rax
ret
.L4
movq %rsi, %rax
subq %rdi, %rax
ret
long absdiff(long x, long y){
long result;
if (x > y){
result = x-y;
} else {
result = y-x;
}
return result;
}
Register | Use
%rdi | x
%rsi | y
%rax | result
cmpq %rsi, %rdi
jle .L4
# x–y <= 0

## Slide 15: Exercise 2: Conditionals
test:
leaq (%rdi, %rsi), %rax
addq %rdx, %rax
cmpq $-3, %rdi
jge .L2
cmpq %rdx, %rsi
jge .L3
movq %rdi, %rax
imulq %rsi, %rax
ret
.L3:
movq %rsi, %rax
imulq %rdx, %rax
ret
.L2
cmpq $2, %rdi
jle .L4
movq %rdi, %rax
imulq %rdx, %rax
.L4:
rep; ret
long test(long x, long y, long z){
long val = __________;
if(_______){
if(_______){
val = ______;
} else {
val = ______;
}
} else if (______){
val = _______;
}
return val;
}

## Slide 16: Exercise 2: Conditionals
test:
leaq (%rdi, %rsi), %rax
addq %rdx, %rax
cmpq $-3, %rdi
jge .L2
cmpq %rdx, %rsi
jge .L3
movq %rdi, %rax
imulq %rsi, %rax
ret
.L3:
movq %rsi, %rax
imulq %rdx, %rax
ret
.L2
cmpq $2, %rdi
jle .L4
movq %rdi, %rax
imulq %rdx, %rax
.L4:
rep; ret
long test(long x, long y, long z){
long val = __________;
if(_______){
if(_______){
val = ______;
} else {
val = ______;
}
} else if (______){
val = _______;
}
return val;
}
x + y + z
x < -3
y < z
x*y
y*z
x > 2
x*z
Reg | Use
%rdi | x
%rsi | y
%rdx | z
%rax | val

## Slide 17: Loops
All use conditions and jumps
  do-while
  while
  for

## Slide 18: Do-while Loops
long bitcount(unsigned long x){
long result = 0;
do {
result += x & 0x1;
x >>= 1;
} while (x);
return result;
}
long bitcount(unsigned long x){
long result = 0;
loop:
result += x & 0x1;
x >>= 1;
if(x) goto loop;
return result;
}
movq $0, %rax # result = 0
.L2: # loop:
movq %rdi, %rdx
andq $1, %rdx # t = x & 0x1
addq %rdx, %rax # result += t
shrq %rdi, $1 # x >>= 1
jne .L2 # if (x) goto loop
rep; ret
Register | Use(s)
%rdi | x
%rax | result

## Slide 19: While Loops
while (Condition) {
Body
}
if (Condition){
do {
Body
} while (Condition)
}
long bitcount(unsigned long x) {
long result = 0;
while (x) {
result += x & 0x1;
x >>= 1;
}
return result;
}
movq $0, %rax
jmp .L2
.L3:
movq %rdi, %rdx
andq $1, %rdx
addq %rdx, %rax
shrq %rdi, $1
.L2:
testq %rdi, %rdi
jne .L3
rep ret
Register | Use(s)
%rdi | x
%rax | result

## Slide 20: For loops
for (Init; Cond; Incr){
Body
}
Init;
while (Cond) {
Body;
Incr;
}
Initial test can often be optimized away:
for (j = 0; j < 99; j++)
long bitcount(unsigned long x) {
long result;
for (result = 0; x; x >>= 1)
result += x & 0x1;
return result;
}
movq $0, %rax
jmp .L2
.L3:
movq %rdi, %rdx
andq $1, %rdx
addq %rdx, %rax
shrq %rdi, $1
.L2:
testq %rdi, %rdi
jne .L3
rep ret
Register | Use(s)
%rdi | Argument x
%rax | result
Register | Use(s)
%rdi | x
%rax | result

## Slide 21: Exercise 3: Loops
loop:
movq $0, %rax
movq $0, %rdx
jmp L1
L0:
addq %rdx, %rax
incq %rdx
L1:
cmp %rdi, %rdx
jl L0
ret
long loop(long val){
long ret = ______;
long i;
for(i = ___; ________; ____){
ret = _______;
}
return ret;
}

## Slide 22: Exercise 3: Loops
loop:
movq $0, %rax
movq $0, %rdx
jmp L1
L0:
addq %rdx, %rax
incq %rdx
L1:
cmp %rdi, %rdx
jl L0
ret
long loop(long val){
long ret = ______;
long i;
for(i = ___; ________; ____){
ret = _______;
}
return ret;
}
# init
Register | Use(s)
%rdi | Argument val
%rdx | Local i
%rax | Local ret
# update
# condition
0
0
i < val
i++
ret + i

## Slide 23: Exercise 4: Feedback
Rate how well you think this recorded lecture worked
  Better than an in-person class
  About as well as an in-person class
  Less well than an in-person class, but you still learned something
  Total waste of time, you didn't learn anything
How much time did you spend on this video lecture (including time spent on exercises)?
Do you have any comments or feedback?