## Slide 1: Lecture 14: Caches
CS 105 Spring 2021

## Slide 2: Life without caches
You decide that you want to learn more about computer systems than is covered in this course
The library contains all the books you could possibly want, but you don't like to study in libraries, you prefer to study at home.
You have the following constraints:
Desk
(can hold one book)
Library
(can hold many books)

## Slide 3: Life without caches
Average latency to access a book: 40mins
Average throughput (incl. reading time): 1.2 books/hr

## Slide 4: A Computer System
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Display
Disk
I/O bus
Expansion slots for
other devices such
as network adapters
hello executable
stored on disk
PC

## Slide 5: The CPU-Memory Gap
Chart: Year
| 1985 | 1990 | 1995 | 2000 | 2003 | 2005 | 2010 | 2015
Disk seek time | 75000000 | 28000000 | 10000000 | 8000000 | 6000000 | 5000000 | 3000000 | 3000000
SSD access time | 50000
DRAM access time | 200 | 100 | 70 | 60 | 55 | 50 | 40 | 20
SRAM access time | 150 | 35 | 15 | 3 | 2.5 | 2 | 1.5 | 1.3
CPU cycle time | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4 | 0.33
Effective CPU cycle time | 0.3 | 0.25 | 0.1 | 0.08
Chart: Year
| 1985 | 1990 | 1995 | 2000 | 2003 | 2005 | 2010 | 2015
Disk seek time | 75000000 | 28000000 | 10000000 | 8000000 | 6000000 | 5000000 | 3000000 | 3000000
SSD access time | 50000
DRAM access time | 200 | 100 | 70 | 60 | 55 | 50 | 40 | 20
CPU cycle time | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4 | 0.33
Effective CPU cycle time | 0.3 | 0.25 | 0.1 | 0.08
DRAM
CPU
SSD
Disk
SRAM
Notes:   SRAM: Faster (only 10 or so times slower than the CPU)
  Expensive (1000x relative to DRAM)

## Slide 6: Caching—The Very Idea
Keep some memory values nearby in fast memory
Modern systems have 3 or even 4 levels of caches
Cache idea is widely used:
  Disk controllers
  Web
  (Virtual memory: main memory is a “cache” for the disk)

## Slide 7: Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., cloud, web servers)
Local disks hold files retrieved from disks
on remote servers
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds
disk blocks retrieved
from local disks.

## Slide 8: Latency numbers every programmer should know (2020)
L1 cache reference | 1 ns | 
Branch mispredict | 3 ns | 
L2 cache reference | 4 ns | 
Main memory reference | 100 ns | 
memory 1MB sequential read | 3,000 ns | 3 s
SSD random read | 16,000 ns | 16 s
SSD 1MB sequential read | 49,000 ns | 49 s
Magnetic Disk seek | 2,000,000 ns | 2 ms
Magnetic Disk 1MB sequential read | 825,000 ns | 825 s
Round trip in Datacenter | 500,000 ns | 500 s
Round trip CA<->Europe | 150,000,000 ns | 150 ms
L1 cache reference | 1 ns | 
Branch mispredict | 3 ns | 
L2 cache reference | 4 ns | 
Main memory reference | 100 ns | 
memory 1MB sequential read | 3,000 ns | 
SSD random read | 16,000 ns | 
SSD 1MB sequential read | 49,000 ns | 
Magnetic Disk seek | 2,000,000 ns | 2 ms
Magnetic Disk 1MB sequential read | 825,000 ns | 
Round trip in Datacenter | 500,000 ns | 
Round trip CA<->Europe | 150,000,000 ns | 150 ms
Notes: https://people.eecs.berkeley.edu/~rcs/research/interactive_latency.html
register access ~.2-.4ns (2.6 GHz cycle => register ~.38ns )

## Slide 9: Life with caching
Average latency to access a book: <20mins
Average throughput (incl. reading time): ~2 books/hr

## Slide 10: Caching—The Vocabulary
Size: the total number of bytes that can be stored in the cache
Cache Hit: the desired value is in the cache and returned quickly
Cache Miss: the desired value is not in the cache and must be fetched from a more distant cache (or ultimately from main memory)

## Slide 11: Caching—The Vocabulary
Size: the total number of bytes that can be stored in the cache
Cache Hit: the desired value is in the cache and returned quickly
Cache Miss: the desired value is not in the cache and must be fetched from a more distant cache (or ultimately from main memory)
Miss rate: the fraction of accesses that are misses
Hit time: the time to process a hit
Miss penalty: the additional time to process a miss
Average access time: hit-time + miss-rate * miss-penalty

## Slide 12: Exercise 1: Caching Strategies
How should we decide which books to keep in the bookshelf?

## Slide 13: Example Access Patterns
Data references
  Reference array elements in succession.
  Reference variable sum each iteration.
Instruction references
  Reference instructions in sequence.
  Cycle through loop repeatedly.
int sum = 0;
for (int i = 0; i < n; i++){
sum += a[i];
}
return sum;

## Slide 14: Example Access Patterns

## Slide 15: Principle of Locality
Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time

## Slide 16: Cache Organization

## Slide 17: Cache Lines
data block: cached data (i.e., copy of bytes from memory)
tag: uniquely identifies which data is stored in the cache line
valid bit: indicates whether or not the line contains meaningful information
0
1
2
7
tag
v
3
6
5
4
valid bit
tag
data block

## Slide 18: Direct-mapped Cache
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find line
identifies byte in line
Address of data:
tag
offset
index
the rest of the bits
log(# lines) bits
log(block size) bits
Notes: Note: low-order bits are always zero if we assume 4-byte words (since we'll always be looking up the address of a word), but we'll just think about those bits as part of the offset

## Slide 19: Example: Direct-mapped Cache
0D
00
00
00
101
1
00
00
00
2F
00
00
00
1D
001
1
00
06
40
00
0F
12
AB
68
110
1
34
EA
FF
FF
00
11
22
77
001
0
33
66
55
44
Assume: cache block size 8 bytes
Address of data:
Assume: assume 8-bit machine
0xB4
1011 0100
3 bit tag
2 bit index
3 bit offset
101
100
10
Line 0
Line 1
Line 2
Line 3

## Slide 20: Exercise 2: Interpreting Addresses
Consider the hex address 0xA59. What would be the tag, index, and offset for this address with each of the following cache configurations?
A direct-mapped cache with 8 cache lines and 8-byte data blocks
A direct-mapped cache with 16 cache lines and 4-byte data blocks
A direct-mapped cache with 16 cache lines and 8-byte data blocks

## Slide 21: Exercise 2: Interpreting Addresses
Consider the hex address 0xA59. What would be the tag, index, and offset for this address with each of the following cache configurations?
A direct-mapped cache with 8 cache lines and 8-byte data blocks
A direct-mapped cache with 16 cache lines and 4-byte data blocks
A direct-mapped cache with 16 cache lines and 8-byte data blocks
1010 0101 1001
tag
idx
off
101001
001
011
tag
idx
off
101001
01
0110
tag
idx
off
10100
001
1011

## Slide 22: Exercise 3: Cache Indices
Assume you have an array of 6 integers a that begins at address 0x601940. Assume you are running on a machine that has a direct-mapped cache with 8 cache lines and 8-byte data blocks. Which cache line would each of the 6 integers be stored in when it is in cache?
0x601940

## Slide 23: Exercise 3: Cache Indices
Assume you have an array of 6 integers a that begins at address 0x601940. Assume you are running on a machine that has a direct-mapped cache with 8 cache lines and 8-byte data blocks. Which cache line would each of the 6 integers be stored in when it is in cache?
0x601940
Element | Address | Binary Address | Index | Offset
a[0] |  |  |  | 
a[1] |  |  |  | 
a[2] |  |  |  | 
a[2] |  |  |  | 
a[4] |  |  |  | 
a[5] |  |  |  | 
0x601940
0x601944
0x601948
0x60194c
0x601950
0x601954
… 0100 0000
… 0100 0100
… 0100 1000
… 0100 1100
… 0101 0000
… 0101 0100
000
000
001
001
010
010
000
100
000
100
000
100

## Slide 24: Exercise 3: Direct-mapped Cache
Line 0 |  |  | Line 1 |  |  | Line 2 |  |  | Line 3 |  | 
0 |  | 47 | 0 |  | 47 | 0 |  | 47 | 0 |  | 47
Memory
0x14
0x10
0x0c
0x08
0x04
0x00
17
13
16
15
14
Cache
Access | tag | idx | off | h/m
rd 0x00 |  |  |  | 
rd 0x04 |  |  |  | 
rd 0x14 |  |  |  | 
rd 0x00 |  |  |  | 
rd 0x04 |  |  |  | 
rd 0x14 |  |  |  | 
18
Assume 4 byte data blocks
0000
00
00
0000
0000
0000
0000
m
0000
1
13
Notes: 1. Assume 4 byte data blocks, 4 cache lines
2. Assume 8 byte data blocks, 2 cache lines

## Slide 25: Exercise 3: Direct-mapped Cache
Line 0 |  |  | Line 1 |  |  | Line 2 |  |  | Line 3 |  | 
0 |  | 47 | 0 |  | 47 | 0 |  | 47 | 0 |  | 47
Memory
0x14
0x10
0x0c
0x08
0x04
0x00
17
13
16
15
14
Cache
Access | tag | idx | off | h/m
rd 0x00 |  |  |  | 
rd 0x04 |  |  |  | 
rd 0x14 |  |  |  | 
rd 0x00 |  |  |  | 
rd 0x04 |  |  |  | 
rd 0x14 |  |  |  | 
18
Assume 4 byte data blocks
0000
00
00
0000
0000
0000
0000
m
0000
1
13
0000
01
00
m
0000
1
14
0001
01
00
m
0001
1
18
0000
00
00
h
0000
01
00
m
0000
1
14
0001
01
00
m
0001
1
18
How well does this take advantage of spacial locality?
How well does this take advantage of temporal locality?
Notes: 1. Assume 4 byte data blocks, 4 cache lines
2. Assume 8 byte data blocks, 2 cache lines

## Slide 26: Exercise 4: Direct-mapped Cache
Line 0 |  |  | Line 1 |  | 
0 |  | 47 48 | 0 |  | 47 48
Cache
Assume 8 byte data blocks
18
Memory
0x14
0x10
0x0c
0x08
0x04
0x00
17
13
16
15
14
Access | tag | idx | off | h/m
rd 0x00 |  |  |  | 
rd 0x04 |  |  |  | 
rd 0x14 |  |  |  | 
rd 0x00 |  |  |  | 
rd 0x04 |  |  |  | 
rd 0x14 |  |  |  | 
0000
0000
Notes: 1. Assume 4 byte data blocks, 4 cache lines
2. Assume 8 byte data blocks, 2 cache lines

## Slide 27: Exercise 4: Direct-mapped Cache
Line 0 |  |  | Line 1 |  | 
0 |  | 47 48 | 0 |  | 47 48
How well does this take advantage of spacial locality?
How well does this take advantage of temporal locality?
Cache
Assume 8 byte data blocks
18
Memory
0x14
0x10
0x0c
0x08
0x04
0x00
17
13
16
15
14
Access | tag | idx | off | h/m
rd 0x00 |  |  |  | 
rd 0x04 |  |  |  | 
rd 0x14 |  |  |  | 
rd 0x00 |  |  |  | 
rd 0x04 |  |  |  | 
rd 0x14 |  |  |  | 
0000
0000
0000
0
000
m
0000
1
13 14
0000
0
100
h
0001
0
100
m
0001
1
17 18
0000
0
000
m
0000
0
100
h
0000
1
13 14
0001
0
100
m
0001
1
17 18
Notes: 1. Assume 4 byte data blocks, 4 cache lines
2. Assume 8 byte data blocks, 2 cache lines

## Slide 28: Exercise 5: Feedback
Rate how well you think this recorded lecture worked
  Better than an in-person class
  About as well as an in-person class
  Less well than an in-person class, but you still learned something
  Total waste of time, you didn't learn anything
How much time did you spend on this video lecture (including time spent on exercises)?
Do you have any questions that you would like me to address in this week's problem session?
Do you have any other comments or feedback?