## Slide 1: Lecture 15: Caches (cont'd)
CS 105 Spring 2021

## Slide 2: Review: Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., cloud, web servers)
Local disks hold files retrieved from disks
on remote servers
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds
disk blocks retrieved
from local disks.

## Slide 3: Review: Principle of Locality
Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time

## Slide 4: Review: Direct-mapped Cache
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find line
identifies byte in line
Address of data:
tag
offset
index
the rest of the bits
log(# lines) bits
log(block size) bits
How well does this take advantage of spacial locality?
How well does this take advantage of temporal locality?
valid bit
tag
data block
cache lines

## Slide 5: 2-way Set Associative Cache
E = 2: Two lines per set
Assume: cache block size 8 bytes
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
Address of data:
tag
offset
index
the rest of the bits
log(# sets) bits
log(block size) bits

## Slide 6: Exercise 1: 2-way Set Associative Cache
Cache
Memory
0x14
0x10
0x0c
0x08
0x04
0x00
17
13
16
15
14
18
Assume 8 byte data blocks
Set 0
Set 1
Set 0 | Set 1
Access | tag | idx | off | h/m
rd 0x00 |  |  |  | 
rd 0x04 |  |  |  | 
rd 0x14 |  |  |  | 
rd 0x00 |  |  |  | 
rd 0x04 |  |  |  | 
rd 0x14 |  |  |  | 
Line 0 |  |  | Line 1 |  |  | Line 0 |  |  | Line 1 |  | 
0 | 0 | 47 48 | 0 | 1 | 47 48 | 0 | 0 | 47 48 | 0 | 1 | 47 48

## Slide 7: Exercise 1: 2-way Set Associative Cache
Cache
Memory
0x14
0x10
0x0c
0x08
0x04
0x00
17
13
16
15
14
18
Assume 8 byte data blocks
Set 0
Set 1
Set 0 | Set 1
Access | tag | idx | off | h/m
rd 0x00 |  |  |  | 
rd 0x04 |  |  |  | 
rd 0x14 |  |  |  | 
rd 0x00 |  |  |  | 
rd 0x04 |  |  |  | 
rd 0x14 |  |  |  | 
Line 0 |  |  | Line 1 |  |  | Line 0 |  |  | Line 1 |  | 
0 | 0 | 47 48 | 0 | 1 | 47 48 | 0 | 0 | 47 48 | 0 | 1 | 47 48
rd 0x20 |  |  |  | 
0000
0
000
m
0000
0
100
h
0001
0
100
m
0000
0
000
h
0000
0
100
h
0001
0
100
h
0
1
13 14
1
1
17 18
0010
0
000
m

## Slide 8: Eviction from the Cache
On a cache miss, a new block is loaded into the cache
Direct-mapped cache: A valid block at the same location must be evicted—no choice
Associative cache: If all blocks in the set are valid, one must be evicted
  Random policy
  FIFO
  LIFO
  Least-recently used; requires extra data in each set
  Most-recently used; requires extra data in each set
  Most-frequently used; requires extra data in each set

## Slide 9: Exercise 2: Cache Eviction
Cache
Memory
0x14
0x10
0x0c
0x08
0x04
0x00
17
13
16
15
14
18
Assume 8 byte data blocks, LRU eviction
Set 0
Set 1
Set 0 | Set 1
Access | tag | idx | off | h/m
rd 0x00 |  |  |  | 
rd 0x04 |  |  |  | 
rd 0x14 |  |  |  | 
rd 0x00 |  |  |  | 
rd 0x04 |  |  |  | 
rd 0x14 |  |  |  | 
Line 0 |  |  | Line 1 |  |  | Line 0 |  |  | Line 1 |  | 
0 | 0 | 47 48 | 0 | 1 | 47 48 | 0 | 0 | 47 48 | 0 | 1 | 47 48
rd 0x20 |  |  |  | 
0000
0
000
m
0000
0
100
h
0001
0
100
m
0000
0
000
h
0000
0
100
h
0001
0
100
h
0
1
13 14
1
1
17 18
0010
0
000
m

## Slide 10: Exercise 2: Cache Eviction
Cache
Memory
0x14
0x10
0x0c
0x08
0x04
0x00
17
13
16
15
14
18
Assume 8 byte data blocks, LRU eviction
Set 0
Set 1
Set 0 | Set 1
Access | tag | idx | off | h/m
rd 0x00 |  |  |  | 
rd 0x04 |  |  |  | 
rd 0x14 |  |  |  | 
rd 0x00 |  |  |  | 
rd 0x04 |  |  |  | 
rd 0x14 |  |  |  | 
Line 0 |  |  | Line 1 |  |  | Line 0 |  |  | Line 1 |  | 
0 | 0 | 47 48 | 0 | 1 | 47 48 | 0 | 0 | 47 48 | 0 | 1 | 47 48
rd 0x20 |  |  |  | 
0000
0
000
m
0000
0
100
h
0001
0
100
m
0000
0
000
h
0000
0
100
h
0001
0
100
h
0
1
13 14
1
1
17 18
0010
0
000
m
2
1
21 22

## Slide 11: Caching Organization Summarized
A cache consists of lines
A line contains
  A block of bytes, the data values from memory
  A tag, indicating where in memory the values are from
  A valid bit, indicating if the data are valid
Lines are organized into sets
  Direct-mapped cache: one line per set
  k-way associative cache: k lines per set
  Fully associative cache: all lines in one set

## Slide 12: Caching Vocabulary
Size: the total number of bytes that can be stored in the cache
Cache Hit: the desired value is in the cache and returned quickly
Cache Miss: the desired value is not in the cache and must be fetched from a more distant cache (or ultimately from main memory)
Miss rate: the fraction of accesses that are misses
Hit time: the time to process a hit
Miss penalty: the additional time to process a miss
Average access time: hit-time + miss-rate * miss-penalty

## Slide 13: Categorizing Misses
Compulsory: first-reference to a block
Capacity: cache is too small to hold all of the data
Conflict: collisions in a specific set
Average access time: hit-time + miss-rate * miss-penalty
Notes: Larger block size will reduce compulsory misses
Larger associativity will reduce conflict misses
Larger cache will reduce capacity misses
But: larger block size yields larger miss penalty (more data to copy from memory)
larger cache (and larger associativity): increased hit time
Classifying misses with a particular cache configuration:
  Would this miss occur in a cache with infinite capacity? If the answer is yes, then this is a compulsory miss and we are done. If the answer is no, then consider question 2.
  Would this miss occur in a fully associative cache with the desired capacity? If the answer is yes, then this is a capacity miss and we are done. If the answer is no, then consider question 3.
  Would this miss occur in a cache with the desired capacity and associativity? If the answer is yes, then this is a conflict miss and we are done. If the answer is no, then this is not a miss – it is a hit!

## Slide 14: Exercise 3: Categorizing Misses
For each of the cache misses in Exercise 1, categorize that miss as (1) compulsory, (2) capacity, or (3) conflict
Based on your categorizations, would you recommend (1) increasing the block size, (2) increasing the associativity, or (3) increasing the total cache size
Notes: Both are compulsory misses, so it would make the most sense to increase the data block size

## Slide 15: Typical Intel Core i7 Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 d-cache and i-cache:
  32 KB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 KB, 8-way,
  Access: 10 cycles
L3 unified cache:
  8 MB, 16-way,
  Access: 40-75 cycles
Block size: 64 bytes for all caches.

## Slide 16: Caching and Writes
What to do on a write-hit?
  Write-through: write immediately to memory
  Write-back: defer write to memory until replacement of line
    Need a dirty bit (line different from memory or not)
What to do on a write-miss?
  Write-allocate: load into cache, update line in cache
    Good if more writes to the location follow
  No-write-allocate: writes straight to memory, does not load into cache
Typical
  Write-through + No-write-allocate
  Write-back + Write-allocate

## Slide 17: Exercise 4: Write-through + No-write-allocate
Cache
Memory
0x24
0x20
0x1c
0x18
0x14
0x10
21
17
20
19
18
22
Assume 4 byte data blocks
Line 0 |  |  | Line 1 |  |  | Line 2 |  |  | Line 3 |  |  | W
0 | 0 | 47 | 0 | 1 | 47 | 0 | 2 | 47 | 0 | 3 | 47 | 
Access | tag | idx | off | h/m
rd 0x10 |  |  |  | 
wr 8,0x10 |  |  |  | 
wr 9,0x24 |  |  |  | 
rd 0x24 |  |  |  | 
rd 0x20 |  |  |  | 

## Slide 18: Exercise 4: Write-through + No-write-allocate
Cache
Memory
0x24
0x20
0x1c
0x18
0x14
0x10
21
17
20
19
18
22
Assume 4 byte data blocks
Line 0 |  |  | Line 1 |  |  | Line 2 |  |  | Line 3 |  |  | W
0 | 0 | 47 | 0 | 1 | 47 | 0 | 2 | 47 | 0 | 3 | 47 | 
Access | tag | idx | off | h/m
rd 0x10 |  |  |  | 
wr 8,0x10 |  |  |  | 
wr 9,0x24 |  |  |  | 
rd 0x24 |  |  |  | 
rd 0x20 |  |  |  | 
0001
00
00
m
1
1
17
0001
00
00
h
1
1
8
0010
01
00
m
2
1
9
0010
01
00
m
0010
00
00
m
2
1
21
N
Y
Y
N
N
8
9

## Slide 19: Exercise 5: Write-back + Write-allocate
Cache
Assume 4 byte data blocks
Line 0 |  |  | Line 1 |  |  | Line 2 |  |  | Line 3 |  |  | W
0 | 0 | 47 | 0 | 1 | 47 | 0 | 2 | 47 | 0 | 3 | 47 | 
Memory
0x24
0x20
0x1c
0x18
0x14
0x10
21
17
20
19
18
22
Access | tag | idx | off | h/m
rd 0x10 |  |  |  | 
wr 8,0x10 |  |  |  | 
wr 9,0x24 |  |  |  | 
rd 0x24 |  |  |  | 
rd 0x20 |  |  |  | 

## Slide 20: Exercise 5: Write-back + Write-allocate
Cache
Assume 4 byte data blocks
Line 0 |  |  | Line 1 |  |  | Line 2 |  |  | Line 3 |  |  | W
0 | 0 | 47 | 0 | 1 | 47 | 0 | 2 | 47 | 0 | 3 | 47 | 
Memory
0x24
0x20
0x1c
0x18
0x14
0x10
21
17
20
19
18
22
Access | tag | idx | off | h/m
rd 0x10 |  |  |  | 
wr 8,0x10 |  |  |  | 
wr 9,0x24 |  |  |  | 
rd 0x24 |  |  |  | 
rd 0x20 |  |  |  | 
0001
00
00
m
1
1
17
0001
00
00
h
1
1
8
0010
01
00
m
2
1
9
0010
01
00
h
0010
00
00
m
2
1
21
N
N
N
N
Y
8

## Slide 21: Exercise 6: Feedback
Rate how well you think this recorded lecture worked
  Better than an in-person class
  About as well as an in-person class
  Less well than an in-person class, but you still learned something
  Total waste of time, you didn't learn anything
How much time did you spend on this video lecture (including time spent on exercises)?
Do you have any questions that you would like me to address in this week's problem session?
Do you have any other comments or feedback?