## Slide 1: Lecture 25: Networking
CS 105 Spring 2021

## Slide 2: Physical Layer
Twisted Pair
Coaxial
Fiber
Radio
Notes: Twisted-pair cable is used for wired telephones and Ethernet networks. Pair of wires forms a circuit; twisted to protect against noise from adjacent pairs. Zeros and ones encoded as low/high voltages
I think coax is basically the same thing, but it uses external shielding, and can superimpose wasves of different frequencies to carry multiple signals(?)
Fiberoptic cables use light to transmit bits
Radio waves send bits by alternating the frequency or amplitude of the wave

## Slide 3: Data Link Layer
DSL
Ethernet
WiFi (802.11)
3G
LTE
5G
Twisted Pair
Coaxial
Fiber
Radio

## Slide 4
main
memory
I/O
bridge
MI
ALU
register file
CPU
system bus
memory bus
disk
controller
graphics
adapter
USB
controller
mouse
keyboard
monitor
disk
I/O bus
Expansion slots
network
adapter
network
Notes: Each host has one or more network adapters (aka network interface cards) that translate messages to/from physical network following a particular protocol and export a network abstraction

## Slide 5: Data Link Layer
Each host has one or more network adapter (aka NIC)
  handles particular physical layer and protocol
Each network adapter has a media access control (MAC) address
  unique to that network instance
Messages are organized as packets

## Slide 6: Example: Ethernet
Developed 1976 at Xerox
Simple, scales pretty well
Very successful, still in widespread use
Example address: b8:e3:56:15:6a:72
Carrier sense: listen before you speak
Multiple access: multiple hosts on network
Collision detection: detect and respond to cases where two messages collide
payload
destination address
source address
type
checksum

## Slide 7: Example: Ethernet
Carrier sense: broadcast if wire is available
In case of collision: stop, sleep, retry
  sleep time is determined by collision number
  abort after 16 attempts

## Slide 8: Example: Ethernet
Advantages
completely decentralized
inexpensive
  no state in the network
  no arbiter
  cheap physical links
Disadvantages
endpoints must be trusted
data is available for all to see
  can place ethernet card in promiscuous mode and listen to all messages

## Slide 9: Bridged Ethernet
Spans building or campus
Bridges cleverly learn which hosts are reachable from which ports and then selectively copy frames from port to port
host
host
host
host
host
hub
hub
bridge
100 Mb/s
100 Mb/s
host
host
hub
100 Mb/s
100 Mb/s
1 Gb/s
host
host
host
bridge
host
host
hub
A
B
C
X
Y

## Slide 10: Exercise 1: Data Link Layer
Which of the following are examples of data link layer protocols?
  4G LTE
  Ethernet
  Fiber
  WiFi (802.11)
  IP

## Slide 11: Network Layer
There are lots of lots of local area networks (LANs)
  each determines its own protocols, address format, packet format
What if we wanted to connect them together?
  physically connected by specialized computers called routers
  routers with multiple network adapters can translate
  standardize address and packet formats
This is a internetwork
  aka wide-area network (WAN)
  aka internet
host
host
host
...
host
host
host
...
WAN
WAN
router
router
router
LAN 1
LAN 2

## Slide 12: Logical Structure of an internet
Ad hoc interconnection of networks
  No particular topology
  Vastly different router & link capacities
Send packets from source to destination by hopping through networks
  Router forms bridge from one network to another
  Different packets may take different routes
router
router
router
router
router
router
host
host

## Slide 13: Internet Protocol (IP)
application message (payload)
v
Dest. Port #
offset
source address
header checksum
TTL
protocol
destination address
options
Initiated by the DoD in 60s-70s
Currently transitioning (very slowly) from IPv4 to IPv6
Example address: 128.84.12.43
interoperable
network dynamically routes packets from source to destination
TOS
total length
IHL
identification
fs
Notes: v = version (4 or 6)
IHL = header length in 32-bit words (usually 5 unless options present)
TOS: type of service (?)
total length = total length in bytes
id/flags/offset used for fragmentation/reassembly
TTL = time to live (decrementd each hop
Protocol = TCP, UDP, ICMP

## Slide 14: Aside: IPv4 and IPv6
The original Internet Protocol, with its 32-bit addresses, is known as Internet Protocol Version 4 (IPv4)
1996: Internet Engineering Task Force (IETF) introduced Internet Protocol Version 6 (IPv6) with 128-bit addresses
  Intended as the successor to IPv4
As of November 2019, majority of Internet traffic still carried by IPv4
  24-29% of users access Google services using IPv6.
We will focus on IPv4, but will show you how to write networking code that is protocol-independent.
Notes: https://www.google.com/intl/en/ipv6/statistics.html

## Slide 15: Transferring internet Data Via Encapsulation
LAN2
protocol
software
client
LAN1
adapter
Host A
LAN1
data
(1)
data
PH
FH1
(4)
data
PH
FH2
(6)
data
(8)
data
PH
FH2
(5)
LAN2 frame
protocol
software
LAN1
adapter
LAN2
adapter
Router
data
PH
(3)
FH1
data
PH
FH1
(2)
internet packet
LAN1 frame
(7)
data
PH
FH2
protocol
software
server
LAN2
adapter
Host B
PH: Internet packet header
FH: LAN frame header

## Slide 16: Routing

## Slide 17: Routing

## Slide 18: Exercise 2: IP addresses
What is the current IP address assigned to your computer?

## Slide 19: Transport Layer

## Slide 20: Transport Layer
Clients and servers communicate by sending streams of bytes over a connection.
A transport layer endpoint is identified by an IP address and a port, a 16-bit integer that identifies a process
  Ephemeral port: Assigned automatically by client kernel when client makes a connection request.
  Well-known port: Associated with some service provided by a server (e.g., port 80 is associated with Web servers)

## Slide 21: Sockets
Client
Server
What is a socket?
  IP address + port
  To the kernel, a socket is an endpoint of communication
  To an application, a socket is a file descriptor that lets the application read/write from/to the network
    Note: All Unix I/O devices, including networks, are modeled as files
Clients and servers communicate with each other by reading from and writing to socket descriptors
The main distinction between regular file I/O and socket I/O is how the application “opens” the socket descriptors
clientfd
serverfd

## Slide 22: Anatomy of a Connection
A connection is uniquely identified by the socket addresses of its endpoints (socket pair)
  (cliaddr:cliport, servaddr:servport)
Connection socket pair
(128.2.194.242:51213, 208.216.181.15:80)
Server
(port 80)
Client
Client socket address
128.2.194.242:51213
Server socket address
208.216.181.15:80
Client host address
128.2.194.242
Server host address
208.216.181.15
51213 is an ephemeral port
allocated by the kernel
80 is a well-known port
associated with Web servers

## Slide 23: Well-known Ports and Service Names
Popular services have permanently assigned well-known ports and corresponding well-known service names:
  echo server: 7/echo
  ssh servers: 22/ssh
  email server: 25/smtp
  Web servers: 80/http
Mappings between well-known ports and service names is contained in the file /etc/services on each Linux machine.

## Slide 24: Sockets Interface
5. Stop accepting
messages
4. Stop sending messages
3. Exchange
data
2. Start client
1. Start server
Client / Server
Session
socket
socket
bind
read
write
read
write
close
close
listen
accept
connect
TCP Only

## Slide 25: Sockets Interface: socket
Clients and servers use the socket function to create a socket descriptor:
Example:
Protocol specific! Best practice is to use getaddrinfo to generate the parameters automatically, so that code is protocol independent.
int socket(int domain, int type, int protocol)
int clientfd = Socket(AF_INET, SOCK_DGRAM, 0);
Indicates that we are using 32-bit IPV4 addresses
Indicates transport protocol
int clientfd = Socket(AF_INET, SOCK_STREAM, 0);

## Slide 26: Socket Address Structures
Internet-specific socket address:
  Must cast (struct sockaddr_in *) to (struct sockaddr *) for functions that take socket address arguments.
0
0
0
0
0
0
0
0
sa_family
Family Specific
struct sockaddr_in {
uint16_t sin_family; /* Protocol family (always AF_INET) */
uint16_t sin_port; /* Port num in network byte order */
struct in_addr sin_addr; /* IP addr in network byte order */
unsigned char sin_zero[8]; /* Pad to sizeof(struct sockaddr) */
};
sin_port
AF_INET
sin_addr
sin_family

## Slide 27: Sockets Interface: bind
A server uses bind to ask the kernel to associate the server’s socket address with a socket descriptor:
The process can read bytes that arrive on the connection whose endpoint is addr by reading from descriptor sockfd.
Similarly, writes to sockfd are transferred along connection whose endpoint is addr.
Best practice is to use getaddrinfo to supply the arguments addr and addrlen.
int bind(int sockfd, SA *addr, socklen_t addrlen);

## Slide 28: Transport Layer Segments
Sending application:
  specifies IP address and port
  uses socket bound to source port
Transport Layer:
  breaks application message into smaller chunks
  adds transport-layer header to each message to form a segment
Network Layer (IP):
  adds network-layer header to each datagram
application message (payload)
transport-layer header
Source IP
Dest. IP
application message (payload)
Source Port #
Dest. Port #
length of seg.
checksum

## Slide 29: Should the transport layer guarantee packet delivery?

## Slide 30: Exercise 3: Transport-Layer Guarantees
Which argument makes more sense? Should the transport layer guarantee packet delivery?

## Slide 31: Transport Layer Protocols
User Datagram Protocol (UDP)
unreliable, unordered delivery
connectionless
best-effort, segments might be lost, delivered out-of-order, duplicated
reliability (if required) is the responsibility of the app
Transmission Control Protocol (TCP)
reliable, inorder delivery
connection setup
flow control
congestion control
Notes: Note: neither guarantees latency or bandwidth

## Slide 32: UDP: tradeoffs
fast:
  no connection setup
  no rate-limiting
simple:
  no connection state
  small header (8 bytes)
(possibly) extra work for applications
  reordering
  duplicate suppression
  handle missing packets

## Slide 33: Transport Protocols by Application
Application | Application-Level Protocol | Transport Protocol
Name Translation | DNS | Typically UDP
Routing Protocol | RIP | Typically UDP
Network Management | SNMP | Typically UDP
Remote File Server | NFS | Typically UDP
Streaming multimedia | (proprietary) | UDP or TCP
Internet telephony | (proprietary) | UDP or TCP
Remote terminal access | Telnet | TCP
File Transfer | (S)FTP | TCP
Email | SMTP | TCP
Web | HTTP(S) | TCP

## Slide 34: The Big Picture

## Slide 35: Hardware and Software Interfaces
Notes: http://www.cs.cornell.edu/courses/cs4410/2018sp/schedule/slides/09-networking.pdf

## Slide 36: Exercise 4: Feedback
Rate how well you think this recorded lecture worked
  Better than an in-person class
  About as well as an in-person class
  Less well than an in-person class, but you still learned something
  Total waste of time, you didn't learn anything
How much time did you spend on this video lecture?
Do you have any comments or suggestions for future classes?